## Slide 1: USPAS - Fundamentals of Ion Sources 16. Electron Beam Ion Sources/Traps (EBIS/EBIT)
Daniela Leitner (LBNL, MSU), Damon Todd (LBNL), Daniel Winklehner (MIT)

## Slide 2: Content
EBIT/EBIS Ion sources
EBIT Ion Source Fundamentals
Brief History
Main processes in the EBIT Source
Ionization Potential and Final charge state in an EBIS/EBIT
Trap Capacity
Cathode – E-beam production
  Cathodes – Electron Beam Confinement – Magnetic Fields
Collector
  E-beam dump
Electrodes and trapping
Charge Breeder

## Slide 3: Electron Beam Ion Sources
  1967 first proposed – developed at about the same time as ECR ion sources
  Driven by the need to use high charge states to increase the final energy for the accelerator
    Linac
    Cyclotrons
Notes: Classic possibility: charge stripping after preaccleration- higher losses, reliability of charge stripper, beam quality losses

## Slide 4: Key Concepts – physical basis of operations
Production of an extended electron beam of a given energy (Ionization Energy!, High electron density!)
Creation of an electrostatic trap for the ions while they get ionized by step-by-step ionization (Confinement Time!)
Injection of a defined number of low charge state ions or injection of neutrals into the trap (vapor/gas)
Extraction of the ions when desired charge state is reached (inherently pulsed operation)
EBIS do not operate with a plasma discharge!
Notes: Draw main concepts of EBIT on board
First order: Electron Beam Ion Sources are not plasma sources! – major advantage in terms of control of charge state

## Slide 5: EBIT Ion sources – main concept
arXiv:1411.2445 ; CERN-2013-007
G.Zschornacka,b, M.Schmidtb and A.Thornb
Electron beam | radial confinement and breeding – successive electron impact ionization
Magnetic field | compression of electron beam
Trap electrodes | axial confinement

## Slide 6: EBIT Ion sources – main concept
arXiv:1411.2445 ; CERN-2013-007
G.Zschornacka,b, M.Schmidtb and A.Thornb
Notes: Electron beam energy is determined by the

## Slide 7: EBIT overview
  Development today: family of ion sources, warm magnets, permanent magnets, superconducting
  atomic physics groups, x-ray generator, calibration
  Injector for synchrotrons: RHIC
  Charge Breeder for post –accelerators (Rex-Isolde (CERN), CARIBU (ATLAS, ANL), ReA (FRIB/NSCL, MSU))
Permanent magnet
Superconducting magnets
ReA EBIT
LLNL EBIT

## Slide 8: RHIC: Relativistic Heavy Ion Accelerator (collider)
  2 independent intersecting storage rings with 6 interaction points
  Can circulate heavy ions or protons
Chain of accelerators
  3 injectors (High charge state injector (EBIS source+linac), Tandem injector, proton linac)
  Booster Synchrotron
  Alternating Gradient Synchrotron
  2.4 miles circumference storage ring

## Slide 9: EBIS test stand facility at RHIC

## Slide 10: ReA Post-Accelator at MSU
EBIT CB
RFQ
CM2
CM3
CM1
ReA3
D-Line
N4 Stopped beams
A1900
L-Line
ReA3 Low Energy Experimental Hall
CCF
A1900
> 50 MeV/u
Experiments
Cryomodules : SC LINAC
RFQ
MHB
Mass separation
Gas
Stopper
1+ ‒› n+
ReA High Energy Experimental Hall
EBIT CB

## Slide 11: ReA EBIT Charge Breeder
E-gun
Collector
Ion extraction
Magnet + Trap
Beam Line
Key parameters:
Magnetic field: B=6T,
Electron current: Ie=0.5 … 5 A,
Electron energy: Ee < 30 keV
Current density: j ~ 104 A / cm2
Trap Length: 635 mm

## Slide 12: Ionization Balance in the EBIT Trap
  Ionization through electron impact (step-by-step) until charge state balance is reached
    Charge generation processes x Charge destructive processes
    Main Atomic processes are
      1. Electron Impact Ionization
      2. Charge Exchange
      3. Radiative Recombination
  Multiple collisions are required – ionization time must be long enough to reach desired charge state
  Key Concept Ionization Factor: Product of the electron flux and the time of bombardment

## Slide 13: Ionization Factor

## Slide 14: Maximum Capacity of the trap
How many particles can be stored?
Key Concepts
  Residual gas pressure
  Compensation
  Pulsed operations

## Slide 15: Extraction of Ions from the EBIT

## Slide 16: Particle Distributions
Ensemble of particles can be described in 6D + time:
or