## Slide 1: Molecular Flow
Mean Free Path Vessel Dimensions
  Mean free path = distance between particle-particle collisions
  Vessel dimension = distance between particle-wall collisions
Typicall accelerator dimensions:
  Molecular flow regime occurs at pressures less than
In molecular flow, geometry plays a critical role
  Viscous flow: particles are “carried by the flow”
    geometry of the vessel unimportant
  Molecular flow: particles move independently, interact with walls only
    geometry of the vessel important

## Slide 2: Molecular Flow Simulations
Particles bounce off walls
Random direction
  No memory of momentum before the interaction
Outgoing probability distribution governed by Lambert’s Cosine Law
Pressure obtained from particle hit counts over a given surface
Particles bouncing off the dipole electrodes and chamber walls in the vertical drop dipole in FRIB Front End

## Slide 3: MolFlow+
Windows application written in C++
Developped and maintained by Roberto Kersevan (CERN)
http://test-molflow.web.cern.ch/
Provides stationary-state pressure profiles
Molflow+ interface with a model of the FRIB Front End (from the two ECR sources to the RFQ entrance down in the tunnel)

## Slide 4: Setting up a model in MolFlow+
Geometry
  Vacuum chamber CAD model exported to STL; ensuring it is a leak-tight enclosed volume
Test-facets
  Create area over which pressure is measured (i.e. particle hits are counted)
Outgassing
  Thermal outgassing coefficient
  Any additional sources, e.g. diffusion from ECR source, support gas ions dumped on the analyzing magnet
Pumps
  Pumping speeds for the gas considered
  Each gas considered separately, simulations for different gases superposed to yield final result
In each model:
  The final pressure profile scales linearly with the outgassing coefficient
    A single simulation provides pressure profile for various outgassing results
  Dependence on pumping speeds is more complex (geometry-dependent)
    Each pumping scheme requires a new simulation run
Analyzing magnet in the model of the FRIB Front End with highlighted test-facets along the beam axis

## Slide 5: FRIB Front End Simulations in MolFlow+
Simulations were used to validate vacuum system design against requirements
Two beam scenarios considered:
  Uranium beam with oxygen support gas (nominal beam)
  Argon beam with oxygen support gas (shown here)
Pressure requirements
  Average pressure over FE sections:
    Extraction Region: 1E-7 Torr
    Charge Selection Section: 3E-8 Torr
    Low Energy Beam Transport: 5E-9 Torr
  Requirements established based on the uranium beam scenario
    Based on beam transmission requirement of transmission
  Argon needed to be examined when NEG pumps were introduced
    NEGs do not pump noble gases

## Slide 6: Scenario: Argon Beam with Oxygen Support
Outgassing sources:
  Uniform thermal outgassing from vacuum chamber walls
  Diffusion from ECR source (upstream end of model):
    Argon atoms
    Oxygen molecules
  Diffusion from analyzing magnet
    Argon atoms (dumped charges)
    Oxygen molecules (recombined from oxygen ions in the beam)
  Diffusion from RFQ (downstream end of model)
    Simulating an open boundary condition to a higher pressure region

## Slide 7: Argon & Oxygen Parameters Given by Measurements from the SuSI Source

## Slide 8: Scenario: Argon Beam with Oxygen Support
SuSI data, case with 3 transported charges (Ar10+, Ar11+, Ar12+)
Thermal outgassing: N2 only
Average pressure:
 | ER [Torr] | CSS [Torr] | LEBT [Torr]
Req. | 1E-7 | 3E-8 | 5E-9
N2 | 1.4E-9 | 7.6E-9 | 6.2E-9
O2 (ECR) | 3.6E-8 | 2.6E-9 | <5E-10
O2 (magnet) | 1.2E-8 | 3.1E-8 | 6.0E-10
Ar (ECR) | 1.2E-7 | 8.1E-9 | <5E-10
Ar (magnet) | 1.9E-8 | 5.1E-8 | 1.1E-9
Total | 1.9E-7 | 1.0E-7 | 8.1E-9

## Slide 9: Scenario: Uranium Beam with Oxygen Support
Same model as for Argon case, except:
  No argon, only oxygen
  Oxygen pressure/concentration obtained from an alternative source (measurement with a uranium beam)

## Slide 10: Scenario: Uranium Beam with Oxygen Support
Updates since last model:
  Pumping scheme
  Magnet temperature = 310 K (was 350 K)
  Transmission calculation update: Kimura formula used
Average pressure:
 | ER [Torr] | CSS [Torr] | LEBT [Torr]
Req. | 1E-7 | 3E-8 | 5E-9
N2 | 1.4E-9 | 7.6E-9 | 6.2E-9
O2 (ECR) | 2.5E-7 | 1.8E-8 | <5E-10
O2 (magnet) | 3.1E-8 | 8.0E-8 | 1.5E-9
Total | 2.8E-7 | 1.1E-7 | 8.0E-9

## Slide 11: Vacuum Calculation Results
Pressure levels obtained from simulations are higher than required levels in some sections, however…
Consideration of beam transmission has shown that beam losses with simulation results are still acceptable
Upgrade paths (additional pumping ports) were added in critical areas