ROD Operations Manual

APPENDIX A:

ROD and BOC FPGA Register Definitions

John Joseph

Dr. John Hill, Maurice Goodrick

Jens Dopke, Tobias Flick

| Revision History |
| --- |
| Date | Version | Description |
| March 3, 2008 | 1.9 | See version 1.8 to see Revision History of previous versions Added definitions to Formatter Link FIFO Occupancy Counter Changed bit order in the SDSP definition for HPIC Added definitions for Calibration readout of L1ID |
|  | 2.0 |  |
| May 27, 2009 | 2.1 | Added Formatter Simulator definitions, and various corrections |
| April 21, 2015 | 2.3 | Added Manual Xoff control to Register 0x00402500. Bit 15 Added EFB Wait Limit set and monitoring registers to RCF. Wait Limit Set Register 0x00404418, Wait Count monitor 0x0040442C. |

1	Supported FPGA Versions	4

2	ROD Memory Location Definitions	4

3	ROD Formatter FPGA Registers	5

3.1	Link Configuration Registers	5

3.2	Error Limit Setup Registers	7

3.3	Pixel Trigger Number of Accepts Register	8

3.4	Diagnostic Control Register	9

3.5	Link FIFO Occupancy Count Registers	10

3.6	Error Status Registers	12

3.7	Diagnostic Status Registers	13

3.8	Formatter Link Counters and Link Counter Control	16

3.9	Formatter Data Stream Simulators: Pixel and SCT	19

4	ROD EFB FPGA Registers	25

4.1	EFB Error Mask Registers, Engines 0/1	25

4.2	EFB Data Taking Setup Registers	28

4.3	EFB Diagnostic Registers	30

5	ROD Router FPGA Registers	36

5.1	DSP Trap Setup Registers	36

5.2	Router Slink Command and Status Registers	39

6	ROD Controller FPGA Registers	41

6.1	ROD Controller Command, Status and Mode Registers	41

6.2	ROD Controller FE Command Stream Mask Registers	46

6.3	ROD Controller Calibration Command Registers	47

6.4	ROD Controller Mode Bits and Dynamic Mask Status Registers	47

6.5	ROD Controller Diagnostic Counters Command and Status Registers	48

6.6	ROD Controller Internal TIM FIFO Register	50

6.7	ROD Controller DSP Interrupt Registers	50

6.8	ROD Controller FE Occupancy Counter Control Registers	50

6.9	ROD Controller Internal Scan Calibration and Event ID Registers	51

6.10	ROD Controller Fixed Frequency Trigger Veto Registers	53

6.11	ROD Controller FE Occupancy Counters	54

6.12	ROD Controller Internal Scan Group to Link Map	54

6.13	ROD Controller FE Command Mask LUT	55

6.14	ROD Controller Default Event Type Register	56

6.15	ROD Controller Default Dynamic Mask LUTs	56

6.16	ROD Controller Corrective Event Type Register	56

6.17	ROD Controller Corrective Dynamic Mask LUTs	57

6.18	ROD Controller Corrected Events FIFO	57

6.19	ROD Controller Formatter Mode Bits LUT	57

7	ROD Diagnostic Memory FIFO Registers	64

7.1	Input Memory FIFO Registers	64

7.2	Event Memory FIFO Registers	65

8	BOC Registers	66

8.1	FE Command Stream Control Registers	67

8.2	BPM Laser BPM Test Structure Registers	71

8.3	FE Command Laser Current DAC Registers	72

8.4	FE Link Input Data Delay Registers	73

8.5	BPM Clock Phase and Vernier Registers	75

8.6	Strobe Delay Registers	75

8.7	FE Link Input RX DAC Threshold Registers	76

8.8	Monitoring ADC Setup Registers	78

8.9	BOC Reset and Status and Miscellaneous Registers	78

8.10	Monitoring ADC Tables and Conversion Information: SCT Version	81

8.11	Monitoring ADC Tables and Conversion Information: PIXEL Version	82

9	ROD Slave DSP HPI Registers	83

# Supported FPGA Versions

| FPGA Versions |
| --- |
| ROD Controller FPGA (RCF) | V35F |
| Formatter FPGA (FMT)[S = SCT / P = Pixel] | S34F/P3CF |
| Event Fragment Builder FPGA (EFB) | V2EF |
| Router FPGA (RTR) | V29F |

# ROD Memory Location Definitions

| Description | Address Range |
| --- | --- |
| Formatter FPGA 0 Registers: Links 0 to 11 Configuration, Status, Readout Timeout Limit, Data Overflow Limit, Header Trailer Limit, and ROD Busy Limit | 00400000 | 00400090 |
| Formatter FPGA 1 Registers: Links 12 to 23 Configuration, Status, Readout Timeout Limit, Data Overflow Limit, Header Trailer Limit, and ROD Busy Limit | 00400400 | 00400490 |
| Formatter FPGA 2 Registers: Links 24 to 35 Configuration, Status, Readout Timeout Limit, Data Overflow Limit, Header Trailer Limit, and ROD Busy Limit | 00400800 | 00400890 |
| Formatter FPGA 3 Registers: Links 36 to 47 Configuration, Status, Readout Timeout Limit, Data Overflow Limit, Header Trailer Limit, and ROD Busy Limit | 00400C00 | 00400C90 |
| Formatter FPGA 4 Registers: Links 48 to 59 Configuration, Status, Readout Timeout Limit, Data Overflow Limit, Header Trailer Limit, and ROD Busy Limit | 00401000 | 00401090 |
| Formatter FPGA 5 Registers: Links 60 to 71 Configuration, Status, Readout Timeout Limit, Data Overflow Limit, Header Trailer Limit, and ROD Busy Limit | 00401400 | 00401490 |
| Formatter FPGA 6 Registers: Links 72 to 83 Configuration, Status, Readout Timeout Limit, Data Overflow Limit, Header Trailer Limit, and ROD Busy Limit | 00401800 | 00401890 |
| Formatter FPGA 7 Registers: Links 84 to 95 Configuration, Status, Readout Timeout Limit, Data Overflow Limit, Header Trailer Limit, and ROD Busy Limit | 00401C00 | 00401C90 |
| Event Fragment Builder FPGA Registers Error Mask, Format Version, Source ID, Play Empty Events, Mask BCID Error Check, Diagnostic, Status, Play One Event, FIFO Status Flags, Reset EVENTMEM, W: EVENTMEM A, EVENTMEM B, EVENTMEM C | 00402000 | 004022FC |
| Router FPGA Registers S-Link Control and Status, Event Trapping Control and Status | 00402400 | 004025FC |
| ROD Controller FPGA Registers Function Control, Status, ROD Mode, Diagnostic, Calibration Commands, FE Command Mask, Counter Values, Interrupts, and FE Occupancy Count Control | 00404400 | 004044FC |
| Front End Chip Occupancy Counter Registers | 00404500 | 0040452C |
| FE Command Mask Look-up Table 8 sets of Masks, 64 Locations | 00404600 | 004046FC |
| EFB Dynamic Mask Registers Default and Corrective ROD types | 00404700 | 00404780 |
| Formatter Dynamic Mode Bit Look-up Table 8 sets of Masks, 256 Locations | 00404800 | 00404BFC |
| Diagnostic Memory FIFO Registers R/W: INMEM A, INMEM B R: EVENTMEM A, EVENTMEM B, EVENTMEM C | 00406000 | 00406150 |
| BOC Setup Registers | 00408000 | 00408FFC |
| Slave DSP0 HPI Registers HPIC, HPIA, HPID++, and HPID | 00780000 | 0078000C |
| Slave DSP1 HPI Registers HPIC, HPIA, HPID++, and HPID | 007A0000 | 007A000C |
| Slave DSP2 HPI Registers HPIC, HPIA, HPID++, and HPID | 007C0000 | 007C000C |
| Slave DSP3 HPI Registers HPIC, HPIA, HPID++, and HPID | 007E0000 | 007E000C |

# ROD Formatter FPGA Registers

## Link Configuration Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Link Enable Register: FMT_LINK_EN(fmt) fmt = formatter number |  |  | RW | 12 |
| Formatter Chip 0 | 0 | 00400000 |  |  |
| Formatter Chip 1 | 1 | 00400400 |  |  |
| Formatter Chip 2 | 2 | 00400800 |  |  |
| Formatter Chip 3 | 3 | 00400C00 |  |  |
| Formatter Chip 4 | 4 | 00401000 |  |  |
| Formatter Chip 5 | 5 | 00401400 |  |  |
| Formatter Chip 6 | 6 | 00401800 |  |  |
| Formatter Chip 7 | 7 | 00401C00 |  |  |
| Each bit enables the serial data decoder and data FIFO for a specific link or module input to the Formatter. If the link or module is off, the internal data FIFO will be turned off. On the Pixel ROD, the unused bits are masked. The default register value is 0. | Bit Value |
|  | 1 | 0 |
| Bit 0: Enable SCT Link 0 (40 MHz) / Pixel Module 0 (40/80/160 MHz) | Enable | Off |
| Bit 1: Enable SCT Link 1 (40 MHz) / Pixel Module 1 (40/80 MHz only) | Enable | Off |
| Bit 2: Enable SCT Link 2 (40 MHz) / Pixel Module 2 (40 MHz only) | Enable | Off |
| Bit 3: Enable SCT Link 3 (40 MHz) / Pixel Module 3 (40 MHz only) | Enable | Off |
| Bit 4: Enable SCT Link 4 | Enable | Off |
| Bit 5: Enable SCT Link 5 | Enable | Off |
| Bit 6: Enable SCT Link 6 | Enable | Off |
| Bit 7: Enable SCT Link 7 | Enable | Off |
| Bit 8: Enable SCT Link 8 | Enable | Off |
| Bit 9: Enable SCT Link 9 | Enable | Off |
| Bit 10: Enable SCT Link 10 | Enable | Off |
| Bit 11: Enable SCT Link 11 | Enable | Off |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Expanded Mode Register: FMT_EXP_MODE_EN(fmt) **SCT only** fmt = formatter number |  |  | RW | 12 |
| Formatter Chip 0 | 8 | 00400004 |  |  |
| Formatter Chip 1 | 9 | 00400404 |  |  |
| Formatter Chip 2 | A | 00400804 |  |  |
| Formatter Chip 3 | B | 00400C04 |  |  |
| Formatter Chip 4 | C | 00401004 |  |  |
| Formatter Chip 5 | D | 00401404 |  |  |
| Formatter Chip 6 | E | 00401804 |  |  |
| Formatter Chip 7 | F | 00401C04 |  |  |
| Expanded SCT Data Mode If this bit is set to value 1, the serial input data will be parsed in Expanded Data format. If this bit is set to value 0, the serial input data will be parsed in Condensed Data format. The default register value is 0. The SCT data formats are as follows: Condensed Expanded 1 hit condensed - 1FFFFCCCCCCCxfx0 1st hit cluster - 1FFFFCCCCCCC0DDD 2 hits condensed - 1FFFFCCCCCCCsfx1 1 hit cluster - 1xxxxxxx0xxx1DDD 2 hit cluster - 1xxxxxxx1DDD1DDD x = do not care (The ROD fills these with 0’s) C = cluster base address D = 3 bit hit data F = FE number f = error in condensed mode data, 1st hit s = error in condensed mode data, 2nd hit | Bit Value |
|  | 1 | 0 |
| Bit 0: Link 0 | Expand | Condense |
| Bit 1: Link 1 | Expand | Condense |
| Bit 2: Link 2 | Expand | Condense |
| Bit 3: Link 3 | Expand | Condense |
| Bit 4: Link 4 | Expand | Condense |
| Bit 5: Link 5 | Expand | Condense |
| Bit 6: Link 6 | Expand | Condense |
| Bit 7: Link 7 | Expand | Condense |
| Bit 8: Link 8 | Expand | Condense |
| Bit 9: Link 9 | Expand | Condense |
| Bit 10: Link 10 | Expand | Condense |
| Bit 11: Link 11 | Expand | Condense |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Configuration Mode Register: FMT_CONFIG_MODE_EN(fmt) fmt = formatter number |  |  | RW | 12 |
| Formatter Chip 0 | 10 | 00400008 |  |  |
| Formatter Chip 1 | 11 | 00400408 |  |  |
| Formatter Chip 2 | 12 | 00400808 |  |  |
| Formatter Chip 3 | 13 | 00400C08 |  |  |
| Formatter Chip 4 | 14 | 00401008 |  |  |
| Formatter Chip 5 | 15 | 00401408 |  |  |
| Formatter Chip 6 | 16 | 00401808 |  |  |
| Formatter Chip 7 | 17 | 00401C08 |  |  |
| Configuration Mode (Raw Data Format) If this bit is set to value 1, the Formatter will parse the serial input stream in raw format. If this bit is set to value 0, other registers determine the decoding format. The default register value is 0. The SCT raw data format is as follows: Data Word 011nnnxxDDDDDDDD (n=(number of bits)+1, D=data) The Pixel raw data format is as follows: Link Header 001H11001101DDDDDDDDDDDDDDDDDDDD >> (D=data, H=Header Error) Data Word 0110DDDDDDDDDDDDDDDDDDDDDDDDDDDD >> (D=data) | Bit Value |
|  | 1 | 0 |
| Bit 0: Link 0 | Raw | OFF |
| Bit 1: Link 1 | Raw | OFF |
| Bit 2: Link 2 | Raw | OFF |
| Bit 3: Link 3 | Raw | OFF |
| Bit 4: Link 4 | Raw | OFF |
| Bit 5: Link 5 | Raw | OFF |
| Bit 6: Link 6 | Raw | OFF |
| Bit 7: Link 7 | Raw | OFF |
| Bit 8: Link 8 | Raw | OFF |
| Bit 9: Link 9 | Raw | OFF |
| Bit 10: Link 10 | Raw | OFF |
| Bit 11: Link 11 | Raw | OFF |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Edge Detect Mode Register: FMT_EDGE_MODE_EN(fmt) fmt = formatter number |  |  | RW | 12 |
| Formatter Chip 0 | 18 | 0040000C |  |  |
| Formatter Chip 1 | 19 | 0040040C |  |  |
| Formatter Chip 2 | 1A | 0040080C |  |  |
| Formatter Chip 3 | 1B | 00400C0C |  |  |
| Formatter Chip 4 | 1C | 0040100C |  |  |
| Formatter Chip 5 | 1D | 0040140C |  |  |
| Formatter Chip 6 | 1E | 0040180C |  |  |
| Formatter Chip 7 | 1F | 00401C0C |  |  |
| Edge Detect Mode ** SCT ONLY ** Valid in Condensed Data Mode only. If set, the Formatter will check hit data for Edge Mode or Level Mode format. If an invalid hit pattern is detected, an error flag will be inserted into the condensed hit data word and reported by the EFB. After a reset, this register defaults to all links in Level Detect Mode (all bits 0). Edge Detect Hit Pattern : 01X Level Detect Hit Pattern: X1X | Bit Value |
|  | 1 | 0 |
| Bit 0: Link 0 | Edge | Level |
| Bit 1: Link 1 | Edge | Level |
| Bit 2: Link 2 | Edge | Level |
| Bit 3: Link 3 | Edge | Level |
| Bit 4: Link 4 | Edge | Level |
| Bit 5: Link 5 | Edge | Level |
| Bit 6: Link 6 | Edge | Level |
| Bit 7: Link 7 | Edge | Level |
| Bit 8: Link 8 | Edge | Level |
| Bit 9: Link 9 | Edge | Level |
| Bit 10: Link 10 | Edge | Level |
| Bit 11: Link 11 | Edge | Level |

## Error Limit Setup Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Time Out Limit Register: FMT_READOUT_TIMEOUT(fmt) |  |  | RW | 8 (SCT) 32 (PXL) |
| Formatter Chip 0 | 20 | 00400010 |  |  |
| Formatter Chip 1 | 21 | 00400410 |  |  |
| Formatter Chip 2 | 22 | 00400810 |  |  |
| Formatter Chip 3 | 23 | 00400C10 |  |  |
| Formatter Chip 4 | 24 | 00401010 |  |  |
| Formatter Chip 5 | 25 | 00401410 |  |  |
| Formatter Chip 6 | 26 | 00401810 |  |  |
| Formatter Chip 7 | 27 | 00401C10 |  |  |
| Token to Readout Timeout Limit Reg: The Token to Readout Limit is a user configurable value that is used to determine the time that the ROD allows for a module to transmit event data following a L1 Trigger. If a module does not respond with data before the counter in the Formatter reaches the timeout limit, a time out error event is inserted into the event fragment and the token is passed to the next link. SCT: 800ns increments: The default value at reset is 0xFFh (204.8 us). PXL: 25ns increments: The default value at reset is 0x800h (51.2 us). | Bit Value |
|  | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Data Overflow Limit Register: FMT_DATA_OVERFLOW_LIMIT(fmt) |  |  | RW | 12 |
| Formatter Chip 0 | 28 | 00400014 |  |  |
| Formatter Chip 1 | 29 | 00400414 |  |  |
| Formatter Chip 2 | 2A | 00400814 |  |  |
| Formatter Chip 3 | 2B | 00400C14 |  |  |
| Formatter Chip 4 | 2C | 00401014 |  |  |
| Formatter Chip 5 | 2D | 00401414 |  |  |
| Formatter Chip 6 | 2E | 00401814 |  |  |
| Formatter Chip 7 | 2F | 00401C14 |  |  |
| Data Overflow Limit Value: This value set the maximum number of words played out of the Output FIFO before the ROD determines that a link has received too much data for 1 Event. At reset, the default value is set to 0x200h. | Bit Value |
|  | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Header Trailer Limit Reg: FMT_HEADER_TRAILER_LIMIT(fmt) |  |  | RW | 9 (SCT) 11 (PXL) |
| Formatter Chip 0 | 30 | 00400018 |  |  |
| Formatter Chip 1 | 31 | 00400418 |  |  |
| Formatter Chip 2 | 32 | 00400818 |  |  |
| Formatter Chip 3 | 33 | 00400C18 |  |  |
| Formatter Chip 4 | 34 | 00401018 |  |  |
| Formatter Chip 5 | 35 | 00401418 |  |  |
| Formatter Chip 6 | 36 | 00401818 |  |  |
| Formatter Chip 7 | 37 | 00401C18 |  |  |
| Header Trailer Limit (HTL): This value in the HTL register sets the link FIFO Almost Full word count threshold. When HTL is true, the Formatter only writes Headers and Trailers to the Link FIFO and drops all hit data. At reset, the default value for the SCT Formatter is set to 0x1C0h and for the Pixel Formatter the default value is set to 0x700. | Bit Value |
|  | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Busy Limit Register: FMT_ROD_BUSY_LIMIT(fmt) |  |  | RW | 9 (SCT) 11 (PXL) |
| Formatter Chip 0 | 38 | 0040001C |  |  |
| Formatter Chip 1 | 39 | 0040041C |  |  |
| Formatter Chip 2 | 3A | 0040081C |  |  |
| Formatter Chip 3 | 3B | 00400C1C |  |  |
| Formatter Chip 4 | 3C | 0040101C |  |  |
| Formatter Chip 5 | 3D | 0040141C |  |  |
| Formatter Chip 6 | 3E | 0040181C |  |  |
| Formatter Chip 7 | 3F | 00401C1C |  |  |
| ROD Busy Limit (RBL): The value in the RBL register sets the input link FIFO word count threshold, that, when exceeded, will assert and send ROD BUSY to the trigger system. Because the threshold is configurable, a link that has exceeded ROD BUSY limit may still have a room for more data, but recovery from ROD Busy limit usually requires reset of the link in error. At reset, the default RBL value for the SCT Formatter is 0x1F0h and for the Pixel Formatter the default value is 0x780h. | Bit Value |
|  | Value |

## Pixel Trigger Number of Accepts Register

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Pixel Formatter: Number of L1 Accepts FMT_PXL_LINK_L1A_CNT(fmt) |  | 00400020 | RW | 16 |
| Formatter Chip 0 | 40 | 00400020 |  |  |
| Formatter Chip 1 | 41 | 00400420 |  |  |
| Formatter Chip 2 | 42 | 00400820 |  |  |
| Formatter Chip 3 | 43 | 00400C20 |  |  |
| Formatter Chip 4 | 44 | 00401020 |  |  |
| Formatter Chip 5 | 45 | 00401420 |  |  |
| Formatter Chip 6 | 46 | 00401820 |  |  |
| Formatter Chip 7 | 47 | 00401C20 |  |  |
| The Pixel MCC chip can issue up to 16 L1 Triggers to the FE chips for each L1 trigger sent by the ROD. This register sets a counter value in the Formatter readout state machine that allows all of the data from a multi trigger event to be played out with one trigger. | Bit Value |
| Bits[ 3: 0]: Input Module 0 | Value |
| Bits[ 7: 4]: Input Module 1 | Value |
| Bits[11: 8]: Input Module 2 | Value |
| Bits[15:12]: Input Module 3 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Pixel Formatter: Software Decode Type Select FMT_PXL_BANDWIDTH(fmt) - Link Input Map |  | 00400024 | RW | 16 |
| Formatter Chip 0 | 48 | 00400024 |  |  |
| Formatter Chip 1 | 49 | 00400424 |  |  |
| Formatter Chip 2 | 4A | 00400824 |  |  |
| Formatter Chip 3 | 4B | 00400C24 |  |  |
| Formatter Chip 4 | 4C | 00401024 |  |  |
| Formatter Chip 5 | 4D | 00401424 |  |  |
| Formatter Chip 6 | 4E | 00401824 |  |  |
| Formatter Chip 7 | 4F | 00401C24 |  |  |
| If the Decode Select Jumpers are not installed, then the value in bits 0 and 1 of this register selects the input decode type. Pixel Decoder Type == “00” – Single Link 40MHz Decoder (default) “01” – Dual Link 80MHz input “10” – Quad Link 160MHz input See diagram below for information on Link Map values. The Formatter does not protect against incorrect link map values. | Bit Value |
| Bits[ 1: 0]: Decode Select Value | Value |
| Bits[19:16]: Module 0 - Data Input 0 Link Map (0 to 11) / DTO 2 Rising Edge | Value |
| Bits[23:20]: Module 1 - Data Input 1 Link Map (0 to 11) / DTO 2 Falling Edge | Value |
| Bits[27:24]: Module 2 - Data Input 2 Link Map (0 to 11) / DTO Rising Edge | Value |
| Bits[31:28]: Module 3 - Data Input 3 Link Map (0 to 11) / DTO Falling Edge | Value |

## Diagnostic Control Register

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter L1A Counter Register: |  |  | R | 24 |
| Formatter Chip 0 |  | 00400030 |  |  |
| Formatter Chip 1 |  | 00400430 |  |  |
| Formatter Chip 2 |  | 00400830 |  |  |
| Formatter Chip 3 |  | 00400C30 |  |  |
| Formatter Chip 4 |  | 00401030 |  |  |
| Formatter Chip 5 |  | 00401430 |  |  |
| Formatter Chip 6 |  | 00401830 |  |  |
| Formatter Chip 7 |  | 00401C30 |  |  |
| This register keeps track of all L1A triggers that are sent to the Formatter. It is cleared when the Formatter receives an ECR command | Bit Value |
|  | Value |
| Bits [23:0] : L1A Count | L1A Count |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter BCR and ECR Counter Register: |  |  | R | 32 |
| Formatter Chip 0 |  | 00400034 |  |  |
| Formatter Chip 1 |  | 00400434 |  |  |
| Formatter Chip 2 |  | 00400834 |  |  |
| Formatter Chip 3 |  | 00400C34 |  |  |
| Formatter Chip 4 |  | 00401034 |  |  |
| Formatter Chip 5 |  | 00401434 |  |  |
| Formatter Chip 6 |  | 00401834 |  |  |
| Formatter Chip 7 |  | 00401C34 |  |  |
| This register keeps track of all ECR and BCR commands triggers that are sent to the Formatter. It is cleared when the Formatter is reset. | Bit Value |
|  | Value |
| Bits [31:16] : BCR Count | BCR Count |
| Bits [15: 0] : ECR Count | ECR Count |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Link Data Test Output Mux Register: FMT_LINK_DATA_TEST_MUX(fmt) |  |  | RW | 4 |
| Formatter Chip 0 | 70 | 00400038 |  |  |
| Formatter Chip 1 | 71 | 00400438 |  |  |
| Formatter Chip 2 | 72 | 00400838 |  |  |
| Formatter Chip 3 | 73 | 00400C38 |  |  |
| Formatter Chip 4 | 74 | 00401038 |  |  |
| Formatter Chip 5 | 75 | 00401438 |  |  |
| Formatter Chip 6 | 76 | 00401838 |  |  |
| Formatter Chip 7 | 77 | 00401C38 |  |  |
| Link Data Test Output Mux: This value selects the input link to send to the EFB output mux that drives the front panel LEMO. The decoding is as follows: 0x0h = Link0, 0x1h = Link1, … 0xBh = Link11, 0xFh = ROD Busy Monitor | Bit Value |
|  | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Mode Bits Diagnostic, Read Enable: FMT_MB_DIAG_REN(fmt) |  |  | RW | 8 |
| Formatter Chip 0 | 78 | 0040003C |  |  |
| Formatter Chip 1 | 79 | 0040043C |  |  |
| Formatter Chip 2 | 7A | 0040083C |  |  |
| Formatter Chip 3 | 7B | 00400C3C |  |  |
| Formatter Chip 4 | 7C | 0040103C |  |  |
| Formatter Chip 5 | 7D | 0040143C |  |  |
| Formatter Chip 6 | 7E | 0040183C |  |  |
| Formatter Chip 7 | 7F | 00401C3C |  |  |
| Mode Bits Diagnostic REN: This bit enables the readout of Mode Bits to check that they are being sent to the Formatters correctly. This register is only to be used as board diagnostics. | Bit Value |
|  | 1 | 0 |
| Bit 0: Mode Bit FIFO Read Enable | RD | Idle |
| Bit 1: Enable Link FIFO read command | RD | Idle |
| Bit 2: Enable Link FIFO write command | WR | Idle |
| Bit 3: Not Used |  |  |
| Bits [7:4]: Link FIFO Select | Value |

## Link FIFO Occupancy Count Registers

The value in the Data FIFO Occupancy Count Register indicates the number of data words (headers/hits/trailers) that are currently stored for a specific link or module.  The counter increments by 1 for each word stored and decrements by one for each word transmitted on the ROD data path.  The number of words in the link/module FIFO is not equal to the number of hits received from the FE modules.

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Link 0 / Module 0 Data FIFO Occupancy Count Register: FMT_LINK_OCC_COUNT(fmt,lnk) |  |  | R | [S]/[P] 9 / 11 |
| Formatter Chip 0 | 80 | 00400040 |  |  |
| Formatter Chip 1 | 8C | 00400440 |  |  |
| Formatter Chip 2 | 98 | 00400840 |  |  |
| Formatter Chip 3 | A4 | 00400C40 |  |  |
| Formatter Chip 4 | B0 | 00401040 |  |  |
| Formatter Chip 5 | BC | 00401440 |  |  |
| Formatter Chip 6 | C8 | 00401840 |  |  |
| Formatter Chip 7 | D4 | 00401C40 |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Link 1 / Module 1 Data FIFO Occupancy Count Register: FMT_LINK_OCC_COUNT(fmt,lnk) |  |  | R | [S]/[P] 9 / 11 |
| Formatter Chip 0 | 81 | 00400044 |  |  |
| Formatter Chip 1 | 8D | 00400444 |  |  |
| Formatter Chip 2 | 99 | 00400844 |  |  |
| Formatter Chip 3 | A5 | 00400C44 |  |  |
| Formatter Chip 4 | B1 | 00401044 |  |  |
| Formatter Chip 5 | BD | 00401444 |  |  |
| Formatter Chip 6 | C9 | 00401844 |  |  |
| Formatter Chip 7 | D5 | 00401C44 |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Link 2 / Module 2 Data FIFO Occupancy Count Register: FMT_LINK_OCC_COUNT(fmt,lnk) |  |  | R | [S]/[P] 9 / 11 |
| Formatter Chip 0 | 82 | 00400048 |  |  |
| Formatter Chip 1 | 8E | 00400448 |  |  |
| Formatter Chip 2 | 9A | 00400848 |  |  |
| Formatter Chip 3 | A6 | 00400C48 |  |  |
| Formatter Chip 4 | B2 | 00401048 |  |  |
| Formatter Chip 5 | BE | 00401448 |  |  |
| Formatter Chip 6 | CA | 00401848 |  |  |
| Formatter Chip 7 | D6 | 00401C48 |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Link 3 / Module 3 Data FIFO Occupancy Count Register: FMT_LINK_OCC_COUNT(fmt,lnk) |  |  | R | [S]/[P] 9 / 11 |
| Formatter Chip 0 | 83 | 0040004C |  |  |
| Formatter Chip 1 | 8F | 0040044C |  |  |
| Formatter Chip 2 | 9B | 0040084C |  |  |
| Formatter Chip 3 | A7 | 00400C4C |  |  |
| Formatter Chip 4 | B3 | 0040104C |  |  |
| Formatter Chip 5 | BF | 0040144C |  |  |
| Formatter Chip 6 | CB | 0040184C |  |  |
| Formatter Chip 7 | D7 | 00401C4C |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Link 4 Data FIFO Occupancy Count Register: FMT_LINK_OCC_COUNT(fmt,lnk) |  |  | R | [S]/[P] 9 / 11 |
| Formatter Chip 0 | 84 | 00400050 |  |  |
| Formatter Chip 1 | 90 | 00400450 |  |  |
| Formatter Chip 2 | 9C | 00400850 |  |  |
| Formatter Chip 3 | A8 | 00400C50 |  |  |
| Formatter Chip 4 | B4 | 00401050 |  |  |
| Formatter Chip 5 | C0 | 00401450 |  |  |
| Formatter Chip 6 | CC | 00401850 |  |  |
| Formatter Chip 7 | D8 | 00401C50 |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Link 5 Data FIFO Occupancy Count Register: FMT_LINK_OCC_COUNT(fmt,lnk) |  |  | R | 9 |
| Formatter Chip 0 | 85 | 00400054 |  |  |
| Formatter Chip 1 | 91 | 00400454 |  |  |
| Formatter Chip 2 | 9D | 00400854 |  |  |
| Formatter Chip 3 | A9 | 00400C54 |  |  |
| Formatter Chip 4 | B5 | 00401054 |  |  |
| Formatter Chip 5 | C1 | 00401454 |  |  |
| Formatter Chip 6 | CD | 00401854 |  |  |
| Formatter Chip 7 | D9 | 00401C54 |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Link 6 Data FIFO Occupancy Count Register: FMT_LINK_OCC_COUNT(fmt,lnk) |  |  | R | 9 |
| Formatter Chip 0 | 86 | 00400058 |  |  |
| Formatter Chip 1 | 92 | 00400458 |  |  |
| Formatter Chip 2 | 9E | 00400858 |  |  |
| Formatter Chip 3 | AA | 00400C58 |  |  |
| Formatter Chip 4 | B6 | 00401058 |  |  |
| Formatter Chip 5 | C2 | 00401458 |  |  |
| Formatter Chip 6 | CE | 00401858 |  |  |
| Formatter Chip 7 | DA | 00401C58 |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Link 7 Data FIFO Occupancy Count Register: FMT_LINK_OCC_COUNT(fmt,lnk) |  |  | R | 9 |
| Formatter Chip 0 | 87 | 0040005C |  |  |
| Formatter Chip 1 | 93 | 0040045C |  |  |
| Formatter Chip 2 | 9F | 0040085C |  |  |
| Formatter Chip 3 | AB | 00400C5C |  |  |
| Formatter Chip 4 | B7 | 0040105C |  |  |
| Formatter Chip 5 | C3 | 0040145C |  |  |
| Formatter Chip 6 | CF | 0040185C |  |  |
| Formatter Chip 7 | DB | 00401C5C |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Link 8 Data FIFO Occupancy Count Register: FMT_LINK_OCC_COUNT(fmt,lnk) |  |  | R | 9 |
| Formatter Chip 0 | 88 | 00400060 |  |  |
| Formatter Chip 1 | 94 | 00400460 |  |  |
| Formatter Chip 2 | A0 | 00400860 |  |  |
| Formatter Chip 3 | AC | 00400C60 |  |  |
| Formatter Chip 4 | B8 | 00401060 |  |  |
| Formatter Chip 5 | C4 | 00401460 |  |  |
| Formatter Chip 6 | D0 | 00401860 |  |  |
| Formatter Chip 7 | DC | 00401C60 |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Link 9 Data FIFO Occupancy Count Register: FMT_LINK_OCC_COUNT(fmt,lnk) |  |  | R | 9 |
| Formatter Chip 0 | 89 | 00400064 |  |  |
| Formatter Chip 1 | 95 | 00400464 |  |  |
| Formatter Chip 2 | A1 | 00400864 |  |  |
| Formatter Chip 3 | AD | 00400C64 |  |  |
| Formatter Chip 4 | B9 | 00401064 |  |  |
| Formatter Chip 5 | C5 | 00401464 |  |  |
| Formatter Chip 6 | D1 | 00401864 |  |  |
| Formatter Chip 7 | DD | 00401C64 |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Link 10 Data FIFO Occupancy Count Register: FMT_LINK_OCC_COUNT(fmt,lnk) |  |  | R | 9 |
| Formatter Chip 0 | 8A | 00400068 |  |  |
| Formatter Chip 1 | 96 | 00400468 |  |  |
| Formatter Chip 2 | A2 | 00400868 |  |  |
| Formatter Chip 3 | AE | 00400C68 |  |  |
| Formatter Chip 4 | BA | 00401068 |  |  |
| Formatter Chip 5 | C6 | 00401468 |  |  |
| Formatter Chip 6 | D2 | 00401868 |  |  |
| Formatter Chip 7 | DE | 00401C68 |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Link 11 Data FIFO Occupancy Count Register: FMT_LINK_OCC_COUNT(fmt,lnk) |  |  | R | 9 |
| Formatter Chip 0 | 8B | 0040006C |  |  |
| Formatter Chip 1 | 97 | 0040046C |  |  |
| Formatter Chip 2 | A3 | 0040086C |  |  |
| Formatter Chip 3 | AF | 00400C6C |  |  |
| Formatter Chip 4 | BB | 0040106C |  |  |
| Formatter Chip 5 | C7 | 0040146C |  |  |
| Formatter Chip 6 | D3 | 0040186C |  |  |
| Formatter Chip 7 | DF | 00401C6C |  |  |

## Error Status Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Time Out Error Register: FMT_TIMEOUT_ERROR(fmt) |  |  | R | 12 |
| Formatter Chip 0 | E0 | 00400070 |  |  |
| Formatter Chip 1 | E1 | 00400470 |  |  |
| Formatter Chip 2 | E2 | 00400870 |  |  |
| Formatter Chip 3 | E3 | 00400C70 |  |  |
| Formatter Chip 4 | E4 | 00401070 |  |  |
| Formatter Chip 5 | E5 | 00401470 |  |  |
| Formatter Chip 6 | E6 | 00401870 |  |  |
| Formatter Chip 7 | E7 | 00401C70 |  |  |
| Time Out Error Status Bit to indicate that the link has received the token but no data has arrived from the module within the time limit set by the Token to Readout Timeout Limit Register. When a time out occurs on a link, the status is latched into this register. This register is cleared when it is read by the host | Bit Value |
|  | 1 | 0 |
| Bits[11:0] : Links/Modules[11:0] | Error | OK |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Data Overflow Error Register: FMT_DATA_OVERFLOW_ERROR(fmt) |  |  | R | 12 |
| Formatter Chip 0 | E8 | 00400074 |  |  |
| Formatter Chip 1 | E9 | 00400474 |  |  |
| Formatter Chip 2 | EA | 00400874 |  |  |
| Formatter Chip 3 | EB | 00400C74 |  |  |
| Formatter Chip 4 | EC | 00401074 |  |  |
| Formatter Chip 5 | ED | 00401474 |  |  |
| Formatter Chip 6 | EE | 00401874 |  |  |
| Formatter Chip 7 | EF | 00401C74 |  |  |
| Data Overflow Error Status Bit to indicate that too much data has gone into the FIFO for 1 Event. When a data overflow error occurs on a link, the status is latched into this register. This register is cleared when the host reads it. | Bit Value |
|  | 1 | 0 |
| Bits[11:0] : Links [11:0] | Error | OK |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Header Trailer Error Register: FMT_HEADER_TRAILER_ERR(fmt) |  |  | R | 12 |
| Formatter Chip 0 | F0 | 00400078 |  |  |
| Formatter Chip 1 | F1 | 00400478 |  |  |
| Formatter Chip 2 | F2 | 00400878 |  |  |
| Formatter Chip 3 | F3 | 00400C78 |  |  |
| Formatter Chip 4 | F4 | 00401078 |  |  |
| Formatter Chip 5 | F5 | 00401478 |  |  |
| Formatter Chip 6 | F6 | 00401878 |  |  |
| Formatter Chip 7 | F7 | 00401C78 |  |  |
| Header/Trailer Limit Status Status of the Header/Trailer Limit bit for this link. Indicates that the link is almost full and the Link Formatter is only writing Header/Trailer words to the Link FIFO. When a header trailer (FIFO almost full) error occurs on a link, the status is latched into this register. This register is cleared when the host reads it. | Bit Value |
|  | 1 | 0 |
| Bits[11:0] : Links [11:0] | Error | OK |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Busy Error Register: FMT_ROD_BUSY_ERR(fmt) |  |  | R | 12 |
| Formatter Chip 0 | F8 | 0040007C |  |  |
| Formatter Chip 1 | F9 | 0040047C |  |  |
| Formatter Chip 2 | FA | 0040087C |  |  |
| Formatter Chip 3 | FB | 00400C7C |  |  |
| Formatter Chip 4 | FC | 0040107C |  |  |
| Formatter Chip 5 | FD | 0040147C |  |  |
| Formatter Chip 6 | FE | 0040187C |  |  |
| Formatter Chip 7 | FF | 00401C7C |  |  |
| ROD Busy Limit Status Status of the ROD Busy Limit bit for this link. Indicates that the FIFO for this is full and data is still arriving from the FE Module. This is a fatal error. Resetting the Formatter is the only way to recover from a ROD Busy Limit Error. This register is cleared when the host reads it. | Bit Value |
|  | 1 | 0 |
| Bits[11:0] : Links [11:0] | Error | OK |

## Diagnostic Status Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Normal or Raw Data Format Status Bit: FMT_DATA_FMT_STATUS(fmt) |  |  | R | 12 |
| Formatter Chip 0 | 100 | 00400080 |  |  |
| Formatter Chip 1 | 101 | 00400480 |  |  |
| Formatter Chip 2 | 102 | 00400880 |  |  |
| Formatter Chip 3 | 103 | 00400C80 |  |  |
| Formatter Chip 4 | 104 | 00401080 |  |  |
| Formatter Chip 5 | 105 | 00401480 |  |  |
| Formatter Chip 6 | 106 | 00401880 |  |  |
| Formatter Chip 7 | 107 | 00401C80 |  |  |
| Data Parsing Mode Status If this bit is set, the Formatter is parsing data in “Normal” Mode (Condensed, or Expanded Data Formats). If this bit is cleared, the Formatter is parsing data in “Raw” format. The status is latched into this register if the link goes into “raw data” mode, and is cleared when the host reads it. | Bit Value |
|  | 1 | 0 |
| Bits[11:0] : Links [11:0] | Normal | Raw |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Status Register: FMT_STATUS(fmt) |  |  | R | 32 |
| Formatter Chip 0 | 108 | 00400084 |  |  |
| Formatter Chip 1 | 109 | 00400484 |  |  |
| Formatter Chip 2 | 10A | 00400884 |  |  |
| Formatter Chip 3 | 10B | 00400C84 |  |  |
| Formatter Chip 4 | 10C | 00401084 |  |  |
| Formatter Chip 5 | 10D | 00401484 |  |  |
| Formatter Chip 6 | 10E | 00401884 |  |  |
| Formatter Chip 7 | 10F | 00401C84 |  |  |
|  | Bit Value |
|  | 1 | 0 |
| Bits[ 4:0] : Trigger Count – Number of pending triggers in the Master Form. | Count |
| Bit 5 : Link Mode Bits FIFO Reset State | Active | Reset |
| Bit 6 : Link Mode Bits FIFO Empty Flag: Mode Bits FIFO is empty | Empty | OK |
| Bit 7 : Link Mode Bits FIFO Full Flag: Mode Bits FIFO is full | Full | OK |
| Bits[11:8] : Active Link Status | Link Number |
| Bit 12 : Chip Has Token Status | Token | Idle |
| Bit 13 : Hold Output | Hold | OK |
| Bit 14 : Master/Slave Status | Master | Slave |
| Bit 15 : Formatter DLL Locked | Locked | Error |
| Bits[26:16]: Extended Trigger Count | Count |
| Bit 27 : Trigger Overflow | Overflow | OK |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Version Register: FMT_VERSION(fmt) |  |  | R | 18 |
| Formatter Chip 0 | 110 | 00400088 |  |  |
| Formatter Chip 1 | 111 | 00400488 |  |  |
| Formatter Chip 2 | 112 | 00400888 |  |  |
| Formatter Chip 3 | 113 | 00400C88 |  |  |
| Formatter Chip 4 | 114 | 00401088 |  |  |
| Formatter Chip 5 | 115 | 00401488 |  |  |
| Formatter Chip 6 | 116 | 00401888 |  |  |
| Formatter Chip 7 | 117 | 00401C88 |  |  |
|  | Bit Value |
|  | 1 | 0 |
| Bits[ 7: 0] : Code Version | Value |
| Bits[12: 8] : Board Revision | 0x0Ch |
| Bits[14:13] : Pixel Decoder Type == “00” – Single Link 40MHz Decoder “01” – Dual Link 80MHz input “10” – Quad Link 160MHz input | Value |
| Bit[15] : Formatter Type | Pixel | SCT |
| Bits[17:16] : Formatter Number == “00” – Formatter 0 “01” – Formatter 1 “10” – Formatter 2 “11” – Formatter 3 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ModeBits Status – Links 0 to 11: FMT_MODEBIT_STAT(fmt) |  |  | R | 32 |
| Formatter Chip 0 | 118 | 0040008C |  |  |
| Formatter Chip 1 | 119 | 0040048C |  |  |
| Formatter Chip 2 | 11A | 0040088C |  |  |
| Formatter Chip 3 | 11B | 00400C8C |  |  |
| Formatter Chip 4 | 11C | 0040108C |  |  |
| Formatter Chip 5 | 11D | 0040148C |  |  |
| Formatter Chip 6 | 11E | 0040188C |  |  |
| Formatter Chip 7 | 11F | 00401C8C |  |  |
| Current Read Out Mode Bits, Links 0 to 5 This value is the last set of mode bits used by this link. It is used as a diagnostic tool, and is used primarily when the ROD is processing events one at a time. MB1 MB0 Formatter Read Out Mode Bits Definitions 0 0 Play 1st event from Link FIFO. Normal data flow from Formatter to EFB. 0 1 Mask this link for 1 event. In this mode, the formatter will dump one event from the link FIFO. 1 0 Skip read out of this link for 1 event for re-synchronization. 1 1 Read out 1st event from FIFO and dump it on the floor, play the 2nd event to the EFB. | Bit Value |
| Bits[ 1: 0] : SCT Link 0 / PXL Module 0 | (MB1:MB0) |
| Bits[ 3: 2] : SCT Link 1 / PXL Module 1 | (MB1:MB0) |
| Bits[ 5: 4] : SCT Link 2 / PXL Module 2 | (MB1:MB0) |
| Bits[ 7: 6] : SCT Link 3 / PXL Module 3 | (MB1:MB0) |
| Bits[ 9: 8] : SCT Link 4 | (MB1:MB0) |
| Bits[11:10] : SCT Link 5 | (MB1:MB0) |
| Bits[13:12] : SCT Link 6 | (MB1:MB0) |
| Bits[15:14] : SCT Link 7 | (MB1:MB0) |
| Bits[17:16] : SCT Link 8 | (MB1:MB0) |
| Bits[19:18] : SCT Link 9 | (MB1:MB0) |
| Bits[21:20] : SCT Link 10 | (MB1:MB0) |
| Bits[23:22] : SCT Link 11 | (MB1:MB0) |
| Bits[31:28] : Diagnostics – Readout FIFO Controller Status Read Out Mode Description Value reset Reset 0x1h idle Wait for Mode from RCF 0x2h fmb Fetch current Mode Bits 0x3h wfmb Wait for current Mode Bits wft Wait for token 0x4h rolf Read out link FIFO 0x5h wfd Wait for data 0x6h wfd_td Trailer detected in wait for data doe Dump one event from the link FIFO 0x7h wfd_doe Wait for data, while dump one event doe_ret Return to DOE roe Read one event from the link FIFO nlnk Start readout of next link 0x8h trto Token to readout timeout error 0x9h dovr Data overflow condition error 0xAh pause Back pressure from EFB (SCT Only) 0xBh done Done with link event, pass token 0xCh “others” 0xFh | Value |

## Formatter Link Counters and Link Counter Control

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Input Counter Control: FMT_CNT_COUNTER(fmt) |  |  | R | 32 |
| Formatter Chip 0 |  | 00400090 |  |  |
| Formatter Chip 1 |  | 00400490 |  |  |
| Formatter Chip 2 |  | 00400890 |  |  |
| Formatter Chip 3 |  | 00400C90 |  |  |
| Formatter Chip 4 |  | 00401090 |  |  |
| Formatter Chip 5 |  | 00401490 |  |  |
| Formatter Chip 6 |  | 00401890 |  |  |
| Formatter Chip 7 |  | 00401C90 |  |  |
| This bit enables the link counters in each formatter. During this bit being reset, the global counter set value (FMT_GLB_COUNTER[15:0]) can be written and is transferred into the global counter recent value register part (FMT_GLB_COUNTER[31:16]), while the stream counters (FMT_STREAM_XY) are reset to zero. While the bit is set, the global counter recent value is counted down to zero and while not being zero, the stream counters are added up. | Bit Value |
|  | 1 | 0 |
| Bit[0] : Enable BOC Scan Counters | Counting | Reset |
| Bit[1] : Enable Opto Bit Counters (Both bit 0 and 1 must be set) | Counting | Reset |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Global Input Counter: FMT_GLB_COUNTER(fmt) |  |  | R | 32 |
| Formatter Chip 0 |  | 00400094 |  |  |
| Formatter Chip 1 |  | 00400494 |  |  |
| Formatter Chip 2 |  | 00400894 |  |  |
| Formatter Chip 3 |  | 00400C94 |  |  |
| Formatter Chip 4 |  | 00401094 |  |  |
| Formatter Chip 5 |  | 00401494 |  |  |
| Formatter Chip 6 |  | 00401894 |  |  |
| Formatter Chip 7 |  | 00401C94 |  |  |
|  | Bit Value |
|  | 1 | 0 |
| Bits[15: 0] : Global Counter Set Value – During FMT_CNT_COUNTER Bit[0]=0 (Reset of the Counters) this value is transferred into Bits[31:16] | Value |
| Bits[31:16] : Global Counter Recent Value – While this value is higher than 0 and the FMT_CNT_COUNTER Bit[0] is equal 1, this value decreased by one every clock cycle | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Global Input Counter: FMT_STREAM_01(fmt) |  |  | R | 32 |
| Formatter Chip 0 |  | 00400098 |  |  |
| Formatter Chip 1 |  | 00400498 |  |  |
| Formatter Chip 2 |  | 00400898 |  |  |
| Formatter Chip 3 |  | 00400C98 |  |  |
| Formatter Chip 4 |  | 00401098 |  |  |
| Formatter Chip 5 |  | 00401498 |  |  |
| Formatter Chip 6 |  | 00401898 |  |  |
| Formatter Chip 7 |  | 00401C98 |  |  |
|  | Bit Value |
|  | 1 | 0 |
| Bits[15: 0] : Stream counter value for input stream 0 of the formatter This value adds up incoming data bits while FMT_CNT_COUNTER[0] is equal 1 and FMT_GLB_COUNTER[31:16] value is not zero | Value |
| Bits[31:16] : Stream counter value for input stream 1 of the formatter This value adds up incoming data bits while FMT_CNT_COUNTER[0] is equal 1 and FMT_GLB_COUNTER[31:16] value is not zero | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Global Input Counter: FMT_STREAM_23(fmt) |  |  | R | 32 |
| Formatter Chip 0 |  | 0040009C |  |  |
| Formatter Chip 1 |  | 0040049C |  |  |
| Formatter Chip 2 |  | 0040089C |  |  |
| Formatter Chip 3 |  | 00400C9C |  |  |
| Formatter Chip 4 |  | 0040109C |  |  |
| Formatter Chip 5 |  | 0040149C |  |  |
| Formatter Chip 6 |  | 0040189C |  |  |
| Formatter Chip 7 |  | 00401C9C |  |  |
|  | Bit Value |
|  | 1 | 0 |
| Bits[15: 0] : Stream counter value for input stream 2 of the formatter This value adds up incoming data bits while FMT_CNT_COUNTER[0] is equal 1 and FMT_GLB_COUNTER[31:16] value is not zero | Value |
| Bits[31:16] : Stream counter value for input stream 3 of the formatter This value adds up incoming data bits while FMT_CNT_COUNTER[0] is equal 1 and FMT_GLB_COUNTER[31:16] value is not zero | Value |

NOTE: The PIXEL Data Stream Simulator starts at 0xA0 in the Formatter.  Check for the register description later in the manual (near the SCT simulator).

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Global Input Counter: FMT_STREAM_45(fmt) |  |  | R | 32 |
| Formatter Chip 0 |  | 004000A0 |  |  |
| Formatter Chip 1 |  | 004004A0 |  |  |
| Formatter Chip 2 |  | 004008A0 |  |  |
| Formatter Chip 3 |  | 00400CA0 |  |  |
| Formatter Chip 4 |  | 004010A0 |  |  |
| Formatter Chip 5 |  | 004014A0 |  |  |
| Formatter Chip 6 |  | 004018A0 |  |  |
| Formatter Chip 7 |  | 00401CA0 |  |  |
| Only exists in SCT formatters | Bit Value |
|  | 1 | 0 |
| Bits[15: 0] : Stream counter value for input stream 4 of the formatter This value adds up incoming data bits while FMT_CNT_COUNTER[0] is equal 1 and FMT_GLB_COUNTER[31:16] value is not zero | Value |
| Bits[31:16] : Stream counter value for input stream 5 of the formatter This value adds up incoming data bits while FMT_CNT_COUNTER[0] is equal 1 and FMT_GLB_COUNTER[31:16] value is not zero | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Global Input Counter: FMT_STREAM_67(fmt) |  |  | R | 32 |
| Formatter Chip 0 |  | 004000A4 |  |  |
| Formatter Chip 1 |  | 004004A4 |  |  |
| Formatter Chip 2 |  | 004008A4 |  |  |
| Formatter Chip 3 |  | 00400CA4 |  |  |
| Formatter Chip 4 |  | 004010A4 |  |  |
| Formatter Chip 5 |  | 004014A4 |  |  |
| Formatter Chip 6 |  | 004018A4 |  |  |
| Formatter Chip 7 |  | 00401CA4 |  |  |
| Only exists in SCT formatters | Bit Value |
|  | 1 | 0 |
| Bits[15: 0] : Stream counter value for input stream 6 of the formatter This value adds up incoming data bits while FMT_CNT_COUNTER[0] is equal 1 and FMT_GLB_COUNTER[31:16] value is not zero | Value |
| Bits[31:16] : Stream counter value for input stream 7 of the formatter This value adds up incoming data bits while FMT_CNT_COUNTER[0] is equal 1 and FMT_GLB_COUNTER[31:16] value is not zero | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Global Input Counter: FMT_STREAM_89(fmt) |  |  | R | 32 |
| Formatter Chip 0 |  | 004000A8 |  |  |
| Formatter Chip 1 |  | 004004A8 |  |  |
| Formatter Chip 2 |  | 004008A8 |  |  |
| Formatter Chip 3 |  | 00400CA8 |  |  |
| Formatter Chip 4 |  | 004010A8 |  |  |
| Formatter Chip 5 |  | 004014A8 |  |  |
| Formatter Chip 6 |  | 004018A8 |  |  |
| Formatter Chip 7 |  | 00401CA8 |  |  |
| Only exists in SCT formatters | Bit Value |
|  | 1 | 0 |
| Bits[15: 0] : Stream counter value for input stream 8 of the formatter This value adds up incoming data bits while FMT_CNT_COUNTER[0] is equal 1 and FMT_GLB_COUNTER[31:16] value is not zero | Value |
| Bits[31:16] : Stream counter value for input stream 9 of the formatter This value adds up incoming data bits while FMT_CNT_COUNTER[0] is equal 1 and FMT_GLB_COUNTER[31:16] value is not zero | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Global Input Counter: FMT_STREAM_AB(fmt) |  |  | R | 32 |
| Formatter Chip 0 |  | 004000AC |  |  |
| Formatter Chip 1 |  | 004004AC |  |  |
| Formatter Chip 2 |  | 004008AC |  |  |
| Formatter Chip 3 |  | 00400CAC |  |  |
| Formatter Chip 4 |  | 004010AC |  |  |
| Formatter Chip 5 |  | 004014AC |  |  |
| Formatter Chip 6 |  | 004018AC |  |  |
| Formatter Chip 7 |  | 00401CAC |  |  |
| Only exists in SCT formatters | Bit Value |
|  | 1 | 0 |
| Bits[15: 0] : Stream counter value for input stream 10 of the formatter This value adds up incoming data bits while FMT_CNT_COUNTER[0] is equal 1 and FMT_GLB_COUNTER[31:16] value is not zero | Value |
| Bits[31:16] : Stream counter value for input stream 11 of the formatter This value adds up incoming data bits while FMT_CNT_COUNTER[0] is equal 1 and FMT_GLB_COUNTER[31:16] value is not zero | Value |

## Formatter Data Stream Simulators: Pixel and SCT

PIXEL SPECIFIC:

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Data Stream Simulator Control: FMT_SIM_CTRL_1(fmt) **** PXL VERSION **** |  |  | RW | 32 |
| Formatter Chip 0 |  | 004000A0 |  |  |
| Formatter Chip 1 |  | 004004A0 |  |  |
| Formatter Chip 2 |  | 004008A0 |  |  |
| Formatter Chip 3 |  | 00400CA0 |  |  |
| Formatter Chip 4 |  | 004010A0 |  |  |
| Formatter Chip 5 |  | 004014A0 |  |  |
| Formatter Chip 6 |  | 004018A0 |  |  |
| Formatter Chip 7 |  | 00401CA0 |  |  |
|  | Bit Value |
|  | 1 | 0 |
| Bit[0] : Activate Simulator | ON | OFF |
| Bits[ 2: 1] : Data Decoder Mode | “00” = 40 Mbit/s “01” = 80 Mbit/s “10” = 160 Mbit/s |
| Bit[3] : Simulator Mode | Multiple | Single |
| Bits[ 7: 4] : Number of sequential L1A triggers in each event | Value |
| Bit[8] : Not Used | x | x |
| Bits[12: 9] : Number of MCC Skipped Events in each event (See note in Users Manual v1.64 or later) | Value |
| Bits[15:13] : Header Pattern to transmit Normal header: '11101' Bit-flip header: '11100' Bit-flip header: '11111' Bit-flip header: '11001' Bit-flip header: '10101' Bit-flip header: '01101' Bit-flip header: '111101' | '000' '001' '010' '011' '100' '101' '110' |
| Bits[23:16] : 8-bit MCC flags | Value |
| Bits[31:24] : 8-bit FE flags | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Data Stream Simulator Control: FMT_SIM_CTRL_2(fmt) **** PXL VERSION **** |  |  | RW | 32 |
| Formatter Chip 0 |  | 004000A4 |  |  |
| Formatter Chip 1 |  | 004004A4 |  |  |
| Formatter Chip 2 |  | 004008A4 |  |  |
| Formatter Chip 3 |  | 00400CA4 |  |  |
| Formatter Chip 4 |  | 004010A4 |  |  |
| Formatter Chip 5 |  | 004014A4 |  |  |
| Formatter Chip 6 |  | 004018A4 |  |  |
| Formatter Chip 7 |  | 00401CA4 |  |  |
|  | Bit Value |
|  | 1 | 0 |
| Bits[ 2: 0] : Bit Flip Patterns No bit flip Bit flip all Periodic bit flip (see reg bits 23-3) | '000' '001' '010' |
| Bits[23: 3] : Bit flip settings (get description from Jens) | Value |
| Bits[31:24] : Number of hits to generate for each event. Hits will be inserted into the mid BC of all sequential L1A events | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Global PXL Resync Counter: xxx(fmt) |  |  | R | 32 |
| Formatter Chip 0, MOD 0 |  | 004000B0 |  |  |
| Formatter Chip 1, MOD 0 |  | 004004B0 |  |  |
| Formatter Chip 2, MOD 0 |  | 004008B0 |  |  |
| Formatter Chip 3, MOD 0 |  | 00400CB0 |  |  |
| Formatter Chip 4, MOD 0 |  | 004010B0 |  |  |
| Formatter Chip 5, MOD 0 |  | 004014B0 |  |  |
| Formatter Chip 6, MOD 0 |  | 004018B0 |  |  |
| Formatter Chip 7, MOD 0 |  | 00401CB0 |  |  |
| Pixel formatters ONLY | Bit Value |
|  | 1 | 0 |
| Bits[31: 0] : Counts the number of times the Formatter forces the FE Module data into synchronization following MCC skipped event flags | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Global PXL Resync Counter: xxx(fmt) |  |  | R | 32 |
| Formatter Chip 0, MOD 1 |  | 004000B4 |  |  |
| Formatter Chip 1, MOD 1 |  | 004004B4 |  |  |
| Formatter Chip 2, MOD 1 |  | 004008B4 |  |  |
| Formatter Chip 3, MOD 1 |  | 00400CB4 |  |  |
| Formatter Chip 4, MOD 1 |  | 004010B4 |  |  |
| Formatter Chip 5, MOD 1 |  | 004014B4 |  |  |
| Formatter Chip 6, MOD 1 |  | 004018B4 |  |  |
| Formatter Chip 7, MOD 1 |  | 00401CB4 |  |  |
| Pixel formatters ONLY | Bit Value |
|  | 1 | 0 |
| Bits[31: 0] : Counts the number of times the Formatter forces the FE Module data into synchronization following MCC skipped event flags | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Global PXL Resync Counter: xxx(fmt) |  |  | R | 32 |
| Formatter Chip 0, MOD 2 |  | 004000B8 |  |  |
| Formatter Chip 1, MOD 2 |  | 004004B8 |  |  |
| Formatter Chip 2, MOD 2 |  | 004008B8 |  |  |
| Formatter Chip 3, MOD 2 |  | 00400CB8 |  |  |
| Formatter Chip 4, MOD 2 |  | 004010B8 |  |  |
| Formatter Chip 5, MOD 2 |  | 004014B8 |  |  |
| Formatter Chip 6, MOD 2 |  | 004018B8 |  |  |
| Formatter Chip 7, MOD 2 |  | 00401CB8 |  |  |
| Pixel formatters ONLY | Bit Value |
|  | 1 | 0 |
| Bits[31: 0] : Counts the number of times the Formatter forces the FE Module data into synchronization following MCC skipped event flags | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Global PXL Resync Counter: xxx(fmt) |  |  | R | 32 |
| Formatter Chip 0, MOD 3 |  | 004000BC |  |  |
| Formatter Chip 1, MOD 3 |  | 004004BC |  |  |
| Formatter Chip 2, MOD 3 |  | 004008BC |  |  |
| Formatter Chip 3, MOD 3 |  | 00400CBC |  |  |
| Formatter Chip 4, MOD 3 |  | 004010BC |  |  |
| Formatter Chip 5, MOD 3 |  | 004014BC |  |  |
| Formatter Chip 6, MOD 3 |  | 004018BC |  |  |
| Formatter Chip 7, MOD 3 |  | 00401CBC |  |  |
| Pixel formatters ONLY | Bit Value |
|  | 1 | 0 |
| Bits[31: 0] : Counts the number of times the Formatter forces the FE Module data into synchronization following MCC skipped event flags | Value |

SCT SPECIFIC:

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Formatter Data Stream Simulator Control: FMT_SIM_CTRL(fmt) **** SCT VERSION **** |  |  | RW | 32 |
| Formatter Chip 0 |  | 004000B0 |  |  |
| Formatter Chip 1 |  | 004004B0 |  |  |
| Formatter Chip 2 |  | 004008B0 |  |  |
| Formatter Chip 3 |  | 00400CB0 |  |  |
| Formatter Chip 4 |  | 004010B0 |  |  |
| Formatter Chip 5 |  | 004014B0 |  |  |
| Formatter Chip 6 |  | 004018B0 |  |  |
| Formatter Chip 7 |  | 00401CB0 |  |  |
|  | Bit Value |
|  | 1 | 0 |
| Bit [0] : Activate Simulation | ON | OFF |
| Bit [1] : CLK/2 Mode | Value |  |
| Bit [2] : Debug Mode - Writes L1ID and BCID to Hit Data | Value |  |
| Bits[ 7: 3] : Custom Header (Field value translated as the header) | Value |
| Bits[ 9: 8] : Hit Probability "00" = always send a hit "01" = half hit / half empty "10" = mostly empty, some hits (1 per strip every 128 events) "11" = always an empty event | Value |
| Bits[11:10] : Error Probability "00" = always send hit/empty, so do nothing "01" = mostly OK, but some errors "10" = half OK / half error "11" = always an error | Value |
| Bits[15:12] : Number of chips ("0000" = 1 chip) | Value |
| Bits[22:16] : Number of Hits/Chip | Value |
| Bits[25:23] : Hit Map "000" = fixed at 011 "001" = fixed at 010 "010" = detector alignment 1xx "011" = detector alignment x1x "100" = detector alignment xx1 "101" = Level mode x1x "110" = Edge mode 01x "111" = Test mode xxx | Value |
| Bits[27:26] : Cluster Size | Value |
| Bits[29:28] : Bit Flip Probability in Link 0 | Value |
| Bits[31:30] : Bit Flip Probability in Link 1 | Value |

| Formatter FE Module Stuck Bit Mask Filter Register: FMT_SB_MASK_FILTER(fmt) **** SCT VERSION **** |  |  | RW | 32 |
| --- | --- | --- | --- | --- |
| Formatter Chip 0, Link0 |  | 004000C0 |  |  |
| Formatter Chip 1, Link0 |  | 004004C0 |  |  |
| Formatter Chip 2, Link0 |  | 004008C0 |  |  |
| Formatter Chip 3, Link0 |  | 00400CC0 |  |  |
| Formatter Chip 4, Link0 |  | 004010C0 |  |  |
| Formatter Chip 5, Link0 |  | 004014C0 |  |  |
| Formatter Chip 6, Link0 |  | 004018C0 |  |  |
| Formatter Chip 7, Link0 |  | 00401CC0 |  |  |
| Formatter Chip 0, Link1 |  | 004000C4 |  |  |
| Formatter Chip 1, Link1 |  | 004004C4 |  |  |
| Formatter Chip 2, Link1 |  | 004008C4 |  |  |
| Formatter Chip 3, Link1 |  | 00400CC4 |  |  |
| Formatter Chip 4, Link1 |  | 004010C4 |  |  |
| Formatter Chip 5, Link1 |  | 004014C4 |  |  |
| Formatter Chip 6, Link1 |  | 004018C4 |  |  |
| Formatter Chip 7, Link1 |  | 00401CC4 |  |  |
| Formatter Chip 0, Link2 |  | 004000C8 |  |  |
| Formatter Chip 1, Link2 |  | 004004C8 |  |  |
| Formatter Chip 2, Link2 |  | 004008C8 |  |  |
| Formatter Chip 3, Link2 |  | 00400CC8 |  |  |
| Formatter Chip 4, Link2 |  | 004010C8 |  |  |
| Formatter Chip 5, Link2 |  | 004014C8 |  |  |
| Formatter Chip 6, Link2 |  | 004018C8 |  |  |
| Formatter Chip 7, Link2 |  | 00401CC8 |  |  |
| Formatter Chip 0, Link3 |  | 004000CC |  |  |
| Formatter Chip 1, Link3 |  | 004004CC |  |  |
| Formatter Chip 2, Link3 |  | 004008CC |  |  |
| Formatter Chip 3, Link3 |  | 00400CCC |  |  |
| Formatter Chip 4, Link3 |  | 004010CC |  |  |
| Formatter Chip 5, Link3 |  | 004014CC |  |  |
| Formatter Chip 6, Link3 |  | 004018CC |  |  |
| Formatter Chip 7, Link3 |  | 00401CCC |  |  |
| The stuck bit pipeline mask is used to mask a single time bin pipeline defect in the SCT front end module. There are 2 independent filters per link. The filter only masks orphan hits in the data stream. The stuck bit will be present in the data if it is included in a cluster | Bit Value |
|  | 1 | 0 |
| Bits[3:0] : Time Bin Pipeline to Mask, Filter A | Value |
| Bits[7:4] : Chip in FE Module to Mask, Filter A | Value |
| Bits[14:8] : Channel in FE Module to Mask , Filter A | Value |
| Bit [15] : Enable Filter A | Enable | Disable |
| Bits[19:16] : Time Bin Pipeline to Mask, Filter B | Value |
| Bits[23:20] : Chip in FE Module to Mask, Filter B | Value |
| Bits[30:24] : Channel in FE Module to Mask , Filter B | Value |
| Bit [31] : Enable Filter B | Enable | Disable |

| Formatter FE Module Stuck Bit Mask Filter Register: FMT_SB_MASK_FILTER(fmt) **** SCT VERSION **** |  |  | RW | 32 |
| --- | --- | --- | --- | --- |
| Formatter Chip 0, Link4 |  | 004000D0 |  |  |
| Formatter Chip 1, Link4 |  | 004004D0 |  |  |
| Formatter Chip 2, Link4 |  | 004008D0 |  |  |
| Formatter Chip 3, Link4 |  | 00400CD0 |  |  |
| Formatter Chip 4, Link4 |  | 004010D0 |  |  |
| Formatter Chip 5, Link4 |  | 004014D0 |  |  |
| Formatter Chip 6, Link4 |  | 004018D0 |  |  |
| Formatter Chip 7, Link4 |  | 00401CD0 |  |  |
| Formatter Chip 0, Link5 |  | 004000D4 |  |  |
| Formatter Chip 1, Link5 |  | 004004D4 |  |  |
| Formatter Chip 2, Link5 |  | 004008D4 |  |  |
| Formatter Chip 3, Link5 |  | 00400CD4 |  |  |
| Formatter Chip 4, Link5 |  | 004010D4 |  |  |
| Formatter Chip 5, Link5 |  | 004014D4 |  |  |
| Formatter Chip 6, Link5 |  | 004018D4 |  |  |
| Formatter Chip 7, Link5 |  | 00401CD4 |  |  |
| Formatter Chip 0, Link6 |  | 004000D8 |  |  |
| Formatter Chip 1, Link6 |  | 004004D8 |  |  |
| Formatter Chip 2, Link6 |  | 004008D8 |  |  |
| Formatter Chip 3, Link6 |  | 00400CD8 |  |  |
| Formatter Chip 4, Link6 |  | 004010D8 |  |  |
| Formatter Chip 5, Link6 |  | 004014D8 |  |  |
| Formatter Chip 6, Link6 |  | 004018D8 |  |  |
| Formatter Chip 7, Link6 |  | 00401CD8 |  |  |
| Formatter Chip 0, Link7 |  | 004000DC |  |  |
| Formatter Chip 1, Link7 |  | 004004DC |  |  |
| Formatter Chip 2, Link7 |  | 004008DC |  |  |
| Formatter Chip 3, Link7 |  | 00400CDC |  |  |
| Formatter Chip 4, Link7 |  | 004010DC |  |  |
| Formatter Chip 5, Link7 |  | 004014DC |  |  |
| Formatter Chip 6, Link7 |  | 004018DC |  |  |
| Formatter Chip 7, Link7 |  | 00401CDC |  |  |
| The stuck bit pipeline mask is used to mask a single time bin pipeline defect in the SCT front end module. There are 2 independent filters per link. The filter only masks orphan hits in the data stream. The stuck bit will be present in the data if it is included in a cluster | Bit Value |
|  | 1 | 0 |
| Bits[3:0] : Time Bin Pipeline to Mask, Filter A | Value |
| Bits[7:4] : Chip in FE Module to Mask, Filter A | Value |
| Bits[14:8] : Channel in FE Module to Mask , Filter A | Value |
| Bit [15] : Enable Filter A | Enable | Disable |
| Bits[19:16] : Time Bin Pipeline to Mask, Filter B | Value |
| Bits[23:20] : Chip in FE Module to Mask, Filter B | Value |
| Bits[30:24] : Channel in FE Module to Mask , Filter B | Value |
| Bit [31] : Enable Filter B | Enable | Disable |

| Formatter FE Module Stuck Bit Mask Filter Register: FMT_SB_MASK_FILTER(fmt) **** SCT VERSION **** |  |  | RW | 32 |
| --- | --- | --- | --- | --- |
| Formatter Chip 0, Link8 |  | 004000E0 |  |  |
| Formatter Chip 1, Link8 |  | 004004E0 |  |  |
| Formatter Chip 2, Link8 |  | 004008E0 |  |  |
| Formatter Chip 3, Link8 |  | 00400CE0 |  |  |
| Formatter Chip 4, Link8 |  | 004010E0 |  |  |
| Formatter Chip 5, Link8 |  | 004014E0 |  |  |
| Formatter Chip 6, Link8 |  | 004018E0 |  |  |
| Formatter Chip 7, Link8 |  | 00401CE0 |  |  |
| Formatter Chip 0, Link9 |  | 004000E4 |  |  |
| Formatter Chip 1, Link9 |  | 004004E4 |  |  |
| Formatter Chip 2, Link9 |  | 004008E4 |  |  |
| Formatter Chip 3, Link9 |  | 00400CE4 |  |  |
| Formatter Chip 4, Link9 |  | 004010E4 |  |  |
| Formatter Chip 5, Link9 |  | 004014E4 |  |  |
| Formatter Chip 6, Link9 |  | 004018E4 |  |  |
| Formatter Chip 7, Link9 |  | 00401CE4 |  |  |
| Formatter Chip 0, Link10 |  | 004000E8 |  |  |
| Formatter Chip 1, Link10 |  | 004004E8 |  |  |
| Formatter Chip 2, Link10 |  | 004008E8 |  |  |
| Formatter Chip 3, Link10 |  | 00400CE8 |  |  |
| Formatter Chip 4, Link10 |  | 004010E8 |  |  |
| Formatter Chip 5, Link10 |  | 004014E8 |  |  |
| Formatter Chip 6, Link10 |  | 004018E8 |  |  |
| Formatter Chip 7, Link10 |  | 00401CE8 |  |  |
| Formatter Chip 0, Link11 |  | 004000EC |  |  |
| Formatter Chip 1, Link11 |  | 004004EC |  |  |
| Formatter Chip 2, Link11 |  | 004008EC |  |  |
| Formatter Chip 3, Link11 |  | 00400CEC |  |  |
| Formatter Chip 4, Link11 |  | 004010EC |  |  |
| Formatter Chip 5, Link11 |  | 004014EC |  |  |
| Formatter Chip 6, Link11 |  | 004018EC |  |  |
| Formatter Chip 7, Link11 |  | 00401CEC |  |  |
| The stuck bit pipeline mask is used to mask a single time bin pipeline defect in the SCT front end module. There are 2 independent filters per link. The filter only masks orphan hits in the data stream. The stuck bit will be present in the data if it is included in a cluster | Bit Value |
|  | 1 | 0 |
| Bits[3:0] : Time Bin Pipeline to Mask, Filter A | Value |
| Bits[7:4] : Chip in FE Module to Mask, Filter A | Value |
| Bits[14:8] : Channel in FE Module to Mask , Filter A | Value |
| Bit [15] : Enable Filter A | Enable | Disable |
| Bits[19:16] : Time Bin Pipeline to Mask, Filter B | Value |
| Bits[23:20] : Chip in FE Module to Mask, Filter B | Value |
| Bits[30:24] : Channel in FE Module to Mask , Filter B | Value |
| Bit [31] : Enable Filter B | Enable | Disable |

# ROD EFB FPGA Registers

## EFB Error Mask Registers, Engines 0/1

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Error mask, Engine0, Link 0, ERROR_MASK(0,0) | 140 | 00402000 | RW | 32 |
| EFB: Error mask, Engine1, Link 0, ERROR_MASK(1,0) | 170 | 00402100 | RW | 32 |
| If an Error Count Mask Bit is set in this register, the EFB will not count that specific type of Error for each specified link. | Bit Value |
|  | 1 | 0 |
| Bit 0: BC ID Error Count | Mask | Count |
| Bit 1: L1 ID Error Count | Mask | Count |
| Bit 2: FE Module Timeout Error Count | Mask | Count |
| Bit 3: Data may be incorrect (see Bits 31:16) | Mask | Count |
| Bit 4: Internal Buffer Overflow (see Bits 17:16) | Mask | Count |
| Bits[5:15]: Reserved for Atlas | Mask | Count |
| Bit 16: Almost Full Error, Data Truncated Count | Mask | Count |
| Bit 17: Data Overflow Count | Mask | Count |
| Bit 18: Header Bit Error Count | Mask | Count |
| Bit 19: Sync Error Count | Mask | Count |
| Bit 20: (SCT)Flagged Error Count / (Pixel)Invalid Row(>159) OR Column(>17) | Mask | Count |
| Bit 21: (SCT)Condensed Mode Hit Pattern Error / (Pixel)MCC Sent Empty Event | Mask | Count |
| Bit 22: (SCT)Non-Sequential Chip Num / (Pixel)MCC Flagged Error - EOCOVERFLOW | Mask | Count |
| Bit 23: (SCT)Invalid FE Chip / (Pixel)MCC Flagged Error - HAMMINGCODE | Mask | Count |
| Bit 24: (SCT)Trailer Bit Error Count / (Pixel)MCC Flagged Error - REGPARITY | Mask | Count |
| Bit 25: (SCT)Active Link Masked / (Pixel)MCC Flagged Error - HITPARITY | Mask | Count |
| Bit 26: (Pixel)MCC Flagged Error - BITFLIP | Mask | Count |
| Bit 27: (Pixel)MCC Flagged Error - HITOVERFLOW | Mask | Count |
| Bit 28: (Pixel)MCC Flagged Error - EOEOVERFLOW | Mask | Count |
| Bit 29: (Pixel)MCC Flagged Error - L1CHKFAILFE | Mask | Count |
| Bit 30: (Pixel)MCC Flagged Error - BCIDCHKFAIL | Mask | Count |
| Bit 31: (Pixel)MCC Flagged Error - L1CHKFAILGLOBAL | Mask | Count |

| DESCRIPTION | REG ID | ADDRESS | TYPE | WD |
| --- | --- | --- | --- | --- |
| EFB: Error mask, Engine0, SCT LINK0/PXL MOD00, ERROR_MASK(0,0) | 140 | 00402000 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK1/PXL MOD01, ERROR_MASK(0,1) | 141 | 00402004 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK2/PXL MOD02, ERROR_MASK(0,2) | 142 | 00402008 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK3/PXL MOD03, ERROR_MASK(0,3) | 143 | 0040200C | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK4, ERROR_MASK(0,4) | 144 | 00402010 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK5, ERROR_MASK(0,5) | 145 | 00402014 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK6, ERROR_MASK(0,6) | 146 | 00402018 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK7, ERROR_MASK(0,7) | 147 | 0040201C | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK8, ERROR_MASK(0,8) | 148 | 00402020 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK9, ERROR_MASK(0,9) | 149 | 00402024 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK10, ERROR_MASK(0,10) | 14A | 00402028 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK11, ERROR_MASK(0,11) | 14B | 0040202C | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK12/PXL MOD10, ERROR_MASK(0,12) | 14C | 00402040 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK13/PXL MOD11, ERROR_MASK(0,13) | 14D | 00402044 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK14/PXL MOD12, ERROR_MASK(0,14) | 14E | 00402048 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK15/PXL MOD13, ERROR_MASK(0,15) | 14F | 0040204C | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK16, ERROR_MASK(0,16) | 150 | 00402050 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK17, ERROR_MASK(0,17) | 151 | 00402054 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK18, ERROR_MASK(0,18) | 152 | 00402058 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK19, ERROR_MASK(0,19) | 153 | 0040205C | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK20, ERROR_MASK(0,20) | 154 | 00402060 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK21, ERROR_MASK(0,21) | 155 | 00402064 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK22, ERROR_MASK(0,22) | 156 | 00402068 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK23, ERROR_MASK(0,23) | 157 | 0040206C | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK24/PXL MOD20, ERROR_MASK(0,24) | 158 | 00402080 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK25/PXL MOD21, ERROR_MASK(0,25) | 159 | 00402084 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK26/PXL MOD22, ERROR_MASK(0,26) | 15A | 00402088 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK27/PXL MOD23, ERROR_MASK(0,27) | 15B | 0040208C | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK28, ERROR_MASK(0,28) | 15C | 00402090 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK29, ERROR_MASK(0,29) | 15D | 00402094 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK30, ERROR_MASK(0,30) | 15E | 00402098 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK31, ERROR_MASK(0,31) | 15F | 0040209C | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK32, ERROR_MASK(0,32) | 160 | 004020A0 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK33, ERROR_MASK(0,33) | 161 | 004020A4 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK34, ERROR_MASK(0,34) | 162 | 004020A8 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK35, ERROR_MASK(0,35) | 163 | 004020AC | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK36/PXL MOD30, ERROR_MASK(0,36) | 164 | 004020C0 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK37/PXL MOD31, ERROR_MASK(0,37) | 165 | 004020C4 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK38/PXL MOD32, ERROR_MASK(0,38) | 166 | 004020C8 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK39/PXL MOD33, ERROR_MASK(0,39) | 167 | 004020CC | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK40, ERROR_MASK(0,40) | 168 | 004020D0 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK41, ERROR_MASK(0,41) | 169 | 004020D4 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK42, ERROR_MASK(0,42) | 16A | 004020D8 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK43, ERROR_MASK(0,43) | 16B | 004020DC | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK44, ERROR_MASK(0,44) | 16C | 004020E0 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK45, ERROR_MASK(0,45) | 16D | 004020E4 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK46, ERROR_MASK(0,46) | 16E | 004020E8 | RW | 32 |
| EFB: Error mask, Engine0, SCT LINK47, ERROR_MASK(0,47) | 16F | 004020EC | RW | 32 |

| DESCRIPTION | REG ID | ADDRESS | TYPE | WD |
| --- | --- | --- | --- | --- |
| EFB: Error mask, Engine1, SCT LINK48/PXL MOD40, ERROR_MASK(1,0) | 170 | 00402100 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK49/PXL MOD41, ERROR_MASK(1,1) | 171 | 00402104 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK50/PXL MOD42, ERROR_MASK(1,2) | 172 | 00402108 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK51/PXL MOD43, ERROR_MASK(1,3) | 173 | 0040210C | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK52, ERROR_MASK(1,4) | 174 | 00402110 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK53, ERROR_MASK(1,5) | 175 | 00402114 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK54, ERROR_MASK(1,6) | 176 | 00402118 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK55, ERROR_MASK(1,7) | 177 | 0040211C | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK56, ERROR_MASK(1,8) | 178 | 00402120 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK57, ERROR_MASK(1,9) | 179 | 00402124 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK58, ERROR_MASK(1,10) | 17A | 00402128 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK59, ERROR_MASK(1,11) | 17B | 0040212C | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK60/PXL MOD50, ERROR_MASK(1,12) | 17C | 00402140 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK61/PXL MOD51, ERROR_MASK(1,13) | 17D | 00402144 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK62/PXL MOD52, ERROR_MASK(1,14) | 17E | 00402148 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK63/PXL MOD53, ERROR_MASK(1,15) | 17F | 0040214C | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK64, ERROR_MASK(1,16) | 180 | 00402150 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK65, ERROR_MASK(1,17) | 181 | 00402154 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK66, ERROR_MASK(1,18) | 182 | 00402158 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK67, ERROR_MASK(1,19) | 183 | 0040215C | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK68, ERROR_MASK(1,20) | 184 | 00402160 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK69, ERROR_MASK(1,21) | 185 | 00402164 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK70, ERROR_MASK(1,22) | 186 | 00402168 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK71, ERROR_MASK(1,23) | 187 | 0040216C | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK72/PXL MOD60, ERROR_MASK(1,24) | 188 | 00402180 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK73/PXL MOD61, ERROR_MASK(1,25) | 189 | 00402184 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK74/PXL MOD62, ERROR_MASK(1,26) | 18A | 00402188 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK75/PXL MOD63, ERROR_MASK(1,27) | 18B | 0040218C | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK76, ERROR_MASK(1,28) | 18C | 00402190 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK77, ERROR_MASK(1,29) | 18D | 00402194 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK78, ERROR_MASK(1,30) | 18E | 00402198 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK79, ERROR_MASK(1,31) | 18F | 0040219C | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK80, ERROR_MASK(1,32) | 190 | 004021A0 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK81, ERROR_MASK(1,33) | 191 | 004021A4 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK82, ERROR_MASK(1,34) | 192 | 004021A8 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK83, ERROR_MASK(1,35) | 193 | 004021AC | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK84/PXL MOD70, ERROR_MASK(1,36) | 194 | 004021C0 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK85/PXL MOD71, ERROR_MASK(1,37) | 195 | 004021C4 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK86/PXL MOD72, ERROR_MASK(1,38) | 196 | 004021C8 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK87/PXL MOD73, ERROR_MASK(1,39) | 197 | 004021CC | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK88, ERROR_MASK(1,40) | 198 | 004021D0 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK89, ERROR_MASK(1,41) | 199 | 004021D4 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK90, ERROR_MASK(1,42) | 19A | 004021D8 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK91, ERROR_MASK(1,43) | 19B | 004021DC | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK92, ERROR_MASK(1,44) | 19C | 004021E0 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK93, ERROR_MASK(1,45) | 19D | 004021E4 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK94, ERROR_MASK(1,46) | 19E | 004021E8 | RW | 32 |
| EFB: Error mask, Engine1, SCT LINK95, ERROR_MASK(1,47) | 19F | 004021EC | RW | 32 |

## EFB Data Taking Setup Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Format Version Register, FORMAT_VRSN | 1A0 | 00402200 | R RW | 32 16 |
| This is the Format Version Word in the Event Header. The lower half word is RW, and the upper half word is read only and refers to the Format Version defined in the Event Format Specification Distributed by CERN (Current Version = 4.0) The latest specifcation states that this field can still be 3.1 on the ROD with out causing data stream errors) EDMS: ATL-D-ES-0019 Atlas Communication: ATL-DAQ-98-129 | Bit Value |
| Bits[31:0]: Format Version Value (U=User Defined) | 0301UUUU |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Source ID Register, SOURCE_ID | 1A1 | 00402204 | R RW | 32 23 |
| This is the Source ID Word in the Event Header. The lower half word is RW, and the upper half word is read only and refers to the Source ID defined in the Event Format Specification Distributed by CERN (Current Version = 3.1) EDMS: ATL-D-ES-0019 Atlas Communication: ATL-DAQ-98-129 | Bit Value |
| Bits[31:0]: Source ID Value (U=User Defined) | 0x00UUUUUU |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Run Number Register, RUN_NUMBER | 1A2 | 00402208 | RW | 31 |
| This is the Run Number Word in the Event Header. This register stores the Run Number defined in the Event Format Specification Distributed by CERN (Current Version = 3.1) EDMS: ATL-D-ES-0019 Atlas Communication: ATL-DAQ-98-129 | Bit Value |
| Bits[30:0]: Run Number Value | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Reserved | 1A3 | 0040220C | RW | 32 |
|  | Bit Value |
|  | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: EFB Command 0 Register, EFB_CMND_0 | 1A4 | 00402210 | RW | 32 |
|  | Bit Value |
|  | 1 | 0 |
| Bit 0: Not Used. |  |  |
| Bit 1: Mask BCID Error When this bit is set, the EFB will not mark BCID Errors for all links | Mask | Allow |
| Bit 2: Group Event Counter Enable When this bit is set, the EFB will count Events based upon the ROD Specific Event Type | Enable | Disable |
| Bit 3: Mask L1ID Error When this bit is set, the EFB will not mark L1ID Errors for all links | Mask | Allow |
| Bits[7:4] : Data Link Output Select This value selects the formatter that supplies the input data stream to the front panel LEMO connector. Value 0x0h => select links 0 to 11 Value 0x1h => select links 12 to 23 Value 0x2h => select links 24 to 35 Value 0x3h => select links 36 to 47 Value 0x4h => select links 48 to 59 Value 0x5h => select links 60 to 71 Value 0x6h => select links 72 to 83 Value 0x7h => select links 84 to 95 Value 0xFh => OR all inputs to output ROD BUSY on the FP LEMO | Value |
| Bit 8 : Mask TIM Clock Error When this bit is set, the EFB will not mark TIM Clock Errors. | Mask | Allow |
| Bit 9 : Mask BOC Clock Error When this bit is set, the EFB will not mark TIM Clock Errors. | Mask | Allow |
| Bit 10 : Mask Sweeper Event Error When this bit is set, the EFB will not mark Sweeper Event Errors. | Mask | Allow |
| Bit 11 : L1ID Trap Enable When this bit is set, the EFB will trap L1ID values in a block RAM. Describe the Trapping algorithm | Enable | Idle |
| Bit 12 : Rol BCID Value Select | TIM BCID | RoL BCID |
| Bits[23:20] : HV Error Flag Enable | Value |
| Bits[31:24] : BCID Offset Value This value can be used to offset the expected BCID if required. | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Formatter Enabled Status, EFB_EVT_LIMIT_THRESH |  | 00402214 | R/W | 15 |
| This register stores the value used to determine if an Event is over threshold and of interest for trapping in the SDSPs. To trap over threshold events, the proper bit must be set in the Router trapping control registers. | Bit Value |
|  | 1 | 0 |
| Bits[15:0] : Event Limit Threshold for Router Trap | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Run-Time Status Register, EFB_RUNTIME_STAT_REG | 1A6 | 00402218 | R | 16 |
|  | Bit Value |
|  | 1 | 0 |
| Bit 0: Event FIFO A Almost Full Status Flag Almost Full Flag for the external CY7C4265 FIFO used for EFB data engine 0, 127 words from the 16384 limit. | AFull | OK |
| Bit 1: Error Summary FIFO A Almost Full Almost Full Flag for the internal Error Summary FIFO used to queue the Event Error counts for each trigger processed in EFB data engine 0. | AFull | OK |
| Bit 2: Event ID Empty Error, Engine 0 Indicates that event data arrived from Formatter Bank A before the Event ID information was received from the RCF. Can only be cleared with a full ROD Reset. | ID Error | OK |
| Bit 3: Pause to Formatter, Engine 0 Indicates that backpressure is asserted to Formatter Bank A. | Pause Bank A | OK |
| Bit 4: Event FIFO B Almost Full Status Flag Almost Full Flag for the external CY7C4265 FIFO used for EFB data engine 1, 127 words from the 16384 word limit. | AFull | OK |
| Bit 5: Error Summary FIFO B Almost Full Almost Full Flag for the internal Error Summary FIFO used to queue the Event Error counts for each trigger processed in EFB data engine 1. | AFull | OK |
| Bit 6: Event ID Empty Error, Engine 1 Indicates that event data arrived from the Formatters before the Event ID information was received from the RCF. Can only be cleared with a full ROD Reset. Can only be cleared with a full ROD Reset. | ID Error | OK |
| Bit 7: Pause to Formatter, Engine 1 Indicates that back pressure is asserted to Formatter Bank B | Pause Bank B | OK |
| Bit 8: Halt Output from Router Indicates that the Router is asserting backpressure to the EFB. The Event FIFOs will continue to fill until they reach Almost Full | Stop EFB | OK |
| Bit 9: Event ID Data FIFO Almost Full Global Event ID Data FIFO is ??? words from the full limit | AFull | OK |
| Bit 10: ROL Test Block Enabled Indicates that the Read Out Link Test in process | Enabled | Off |
| Bit 11: L1ID Trap data ready for read out | Data Ready | Idle |
| Bit 12: TBD |  |  |
| Bit 13: TBD |  |  |
| Bit 14: TBD |  |  |
| Bit 15: EFB FPGA Delay Locked Loop Lock Status | Locked |  |
| Bit 16: Formatter 0 is Enabled | Enabled | Idle |
| Bit 17: Formatter 1 is Enabled | Enabled | Idle |
| Bit 18: Formatter 2 is Enabled | Enabled | Idle |
| Bit 19: Formatter 3 is Enabled | Enabled | Idle |
| Bit 20: Formatter 4 is Enabled | Enabled | Idle |
| Bit 21: Formatter 5 is Enabled | Enabled | Idle |
| Bit 22: Formatter 6 is Enabled | Enabled | Idle |
| Bit 23: Formatter 7 is Enabled | Enabled | Idle |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: VHDL Code Version and EFB Type, EFB_CODE_VERSION | 1B4 | 0040221C | R | 16 |
|  | Bit Value |
|  | 1 | 0 |
| Bits[ 7:0]: Code Version | Value |
| Bits[14:8]: Board Revision of Code | Value |
| Bit [15] : ROD Type | Pixel | SCT |

## EFB Diagnostic Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Event Header Data, EVENT_HEADER_DATA | 1A7 | 00402220 | R | 16 |
| This register is used for diagnostics to check the Event Header ID that was in the last event sent to the Router | Bit Value |
| Bits[11: 0]: BCID | Value |
| Bits[15:12]: L1ID (Lower Nibble) | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Event FIFO Data 0, EV_FIFO_DATA1 | 1A8 | 00402224 | R | 16 |
| This register is used for diagnostics to check the last Event ID data that was used by EFB Engine 0. | Bit Value |
| Bits[ 7: 0]: BCID (Lower Byte) | Value |
| Bits[11: 8]: L1ID (Lower Nibble) | Value |
| Bits[15:12]: ROD Event Type | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Event FIFO Data 1, EV_FIFO_DATA2 | 1A9 | 00402228 | R | 16 |
| This register is used for diagnostics to check the last Event ID data that was used by EFB Engine 1. | Bit Value |
| Bits[ 7: 0]: BCID (Lower Byte) | Value |
| Bits[11: 8]: L1ID (Lower Nibble) | Value |
| Bits[15:12]: ROD Event Type | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Formatter Group Event Count | 1B2 | 00402230 | R | 32 |
| The Group Event Counters Count the Occupancy of events in the Formatters sorted by the ROD Event Type field in the EVID data. When all of the data for a specific Group has passed through the EFB the appropriate counter shall be incremented by 1 if the Group counters have been enabled. | Bit Value |
| Bits[ 3: 0]: Group 0 Event Count - ROD Event ID 0 | Value |
| Bits[ 7: 4]: Group 1 Event Count - ROD Event ID 1 | Value |
| Bits[11: 8]: Group 2 Event Count - ROD Event ID 2 | Value |
| Bits[15:12]: Group 3 Event Count - ROD Event ID 3 | Value |
| Bits[19:16]: Group 4 Event Count - ROD Event ID 4 | Value |
| Bits[23:20]: Group 5 Event Count - ROD Event ID 5 | Value |
| Bits[27:24]: Group 6 Event Count - ROD Event ID 6 | Value |
| Bits[31:28]: Group 7 Event Count - ROD Event ID 7 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: EFB Bandwidth Counter | 1B3 | 00402234 | R | 32 |
|  | Bit Value |
| Bits[15: 0]: Data Count | Value |
| Bits[31:16]: Time Count | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Temporary Debug Register |  | 00402238 | R | 32 |
|  | Bit Value |
| Bits[31: 0]: | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Temporary Debug Register |  | 0040223C | R | 32 |
|  | Bit Value |
| Bits[31: 0]: | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Diagnostic Mode Control Register, EVT_MEM_MODE | 1AA | 00402240 | RW | 3 |
| This register is used to set the diagnostic mode of the EFB. (Bits 0, 1 and 2 cannot be turned on simultaneously) | Bit Value |
|  | 1 | 0 |
| Bit 0: Enable EFB Diagnostic Mode 0 Write to the EVENTMEM FIFO using the ROD Bus EFB Path, play out to the Router. | Enable | Disable |
| Bit 1: Enable EFB Diagnostic Mode 1 Write to the EVENTMEM FIFO using the ROD Bus EFB Path, read back over the ROD Bus through the EVENTMEM path. | Enable | Disable |
| Bit 2: Enable EFB Diagnostic Mode 2 Trap Link Data in the EVENTMEM FIFO from normal EFB operation, read back over the ROD Bus through the EVENTMEM path. | Enable | Disable |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Diagnostic Mode FIFO Select, EVT_MEM_CMND_STAT | 1AB | 00402244 | RW | 7 |
| Bits 0 to 2 cannot be turned on simultaneously. | Bit Value |
|  | 1 | 0 |
| Bit 0: EVENTMEM FIFO A Select | Select | Off |
| Bit 1: EVENTMEM FIFO B Select | Select | Off |
| Bit 2: Header Trailer FIFO Select | Select | Off |
| Bit 3: Output 1 Event Fragment | Enable | Disable |
| Bit 4: Flag to indicate FIFO A Bus is Enabled | Enable | Disable |
| Bit 5: Flag to indicate FIFO B Bus is Enabled | Enable | Disable |
| Bit 6: Flag to indicate Event Header/Trailer Bus is enabled | Enable | Disable |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Event Memory FIFO Reset, EVT_MEM_RESET | 1AC | 00402248 | RW | 1 |
| When this bit is set, the EFB sends a reset pulse to the Event Memory FIFO. This bit is self-clearing, and cancels an ongoing play command. | Bit Value |
|  | 1 | 0 |
| Bit 0: Reset Event Memory FIFO | Reset | Ready |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: FIFO Status Flags, EVT_MEM_FLAGS | 1AD | 0040224C | R | 24 |
| This register is used for diagnostics to check the EFB FIFO. | Bit Value |
|  | 1 | 0 |
| Bit 0: FIFO A Empty Status Flag | Empty | OK |
| Bit 1: FIFO A Almost Empty Status Flag | AEmpty | OK |
| Bit 2: FIFO A Almost Full Status Flag | AFull | OK |
| Bit 3: FIFO A Full Status Flag | Full | OK |
| Bit 4: FIFO B Empty Status Flag | Empty | OK |
| Bit 5: FIFO B Almost Empty Status Flag | AEmpty | OK |
| Bit 6: FIFO B Almost Full Status Flag | AFull | OK |
| Bit 7: FIFO B Full Status Flag | Full | OK |
| Bit 8: Header Trailer FIFO Empty Status Flag | Empty | OK |
| Bit 9: Header Trailer FIFO Full Status Flag | Full | OK |
| Bit 10: Event ID FIFO A Empty Status Flag | Empty | OK |
| Bit 11: Event ID FIFO A AlmostFull Status Flag | Full | OK |
| Bit 12: Event ID FIFO B Empty Status Flag | Empty | OK |
| Bit 13: Event ID FIFO B AlmostFull Status Flag | Full | OK |
| Bit 14: Header Event ID FIFO Empty Status Flag | Empty | OK |
| Bit 15: Header Event ID FIFO Almost Full Status Flag | AFull | OK |
| Bit 16: Header Event ID FIFO Full Status Flag | Full | OK |
| Bit 17: Event Data ID FIFO Empty Status Flag | Empty | OK |
| Bit 18: Event ID FIFO A FIFO Full Status Flag | Full | OK |
| Bit 19: Event ID FIFO B FIFO Full Status Flag | Full | OK |
| Bit 20: Word Count FIFO A Full Status Flag | Full | OK |
| Bit 21: Word Count FIFO B Full Status Flag | Full | OK |
| Bit 22: Error Summary FIFO A Full Status Flag | Full | OK |
| Bit 23: Error Summary FIFO B Full Status Flag | Full | OK |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: FIFO Input Data Word [15:0] | ACCESS FIFO | 00402250 | RW | 16 |
| This is the low 16 bits of a word that is to be written into the Event Memory FIFO for diagnostics. | Bit Value |
| Bits[15:0]: FIFO Input Data Word (15:0) | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: FIFO Input Data Word [31:16] | ACCESS FIFO | 00402254 | RW | 16 |
| This is the middle 16 bits of a word that is to be written into the Event Memory FIFO for diagnostics. | Bit Value |
| Bits[15:0]: FIFO Input Data Word (31:16) | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: FIFO Input Data Word [45:32] | ACCESS FIFO | 00402258 | RW | 14 |
| This is the upper 14 bits of a word that is to be written into the Event Memory FIFO for diagnostics. | Bit Value |
| Bits[13:0]: FIFO Input Data Word (45:32) | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Write Word to Selected FIFO | ACCESS FIFO | 0040225C | RW | 1 |
| When this bit is set, the EFB sends a write pulse to the Event Memory FIFO. This bit is self-clearing. | Bit Value |
|  | 1 | 0 |
| Bit 0: Write to Event Memory FIFO | Write | Ready |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Number of Words to Play-FIFO A, EVT_MEM_A_WRD_CNT | 1AE | 00402260 | RW | 14 |
| This value is used in diagnostics mode to indicate the number of words to be played from Event Memory FIFO A when simulated data has been written into the FIFO | Bit Value |
| Bits[13:0]: Number of Words | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Number of Words to Play-FIFO B, EVT_MEM_B_WRD_CNT | 1AF | 00402264 | RW | 14 |
| This value is used in diagnostics mode to indicate the number of words to be played from Event Memory FIFO B when simulated data has been written into the FIFO | Bit Value |
| Bits[13:0]: Number of Words | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Play Selected FIFO, EVT_MEM_PLAY_EVENT | 1B0 | 00402268 | RW | 1 |
| When this bit is set, the EFB sends a read pulse to the Event Memory FIFO. This bit will stay set until the Play Command is complete. | Bit Value |
|  | 1 | 0 |
| Bit 0: Write to Event Memory FIFO | Play | Idle |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Diagnostic Status Register, EVT_MEM_STATUS | 1B1 | 0040226C | R | 16 |
|  | Bit Value |
|  | 1 | 0 |
| Bits[15:0]: Miscellaneous Status Bits |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Send Empty Events, |  | 00402270 | RW | 1 |
| When this bit is set, the EFB will flush the output and EVID data FIFOs and send a empty event fragment. This bit is self-clearing. Not Implemented yet | Bit Value |
|  | 1 | 0 |
| Bit 0: Send Empty Events | Send | Idle |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: L1ID/BCID TTC Trap Value |  | 0040227C | RW | 1 |
| The TTC values for BCID and L1ID when trapping Event ID data. | Bit Value |
|  | 1 | 0 |
| Bits[ 3: 0]: EFB Engine 0 – TTC L1ID | Value |
| Bits[15: 8]: EFB Engine 0 – TTC BCID | Value |
| Bits[19:16]: EFB Engine 1 – TTC L1ID | Value |
| Bits[31:24]: EFB Engine 1 – TTC BCID | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB: Link/Module L1ID/BCID Trap Value |  |  | R | 32 |
| Link0/Link48 Trap Values |  | 00402280 |  |  |
| Link1/Link49 Trap Values |  | 00402284 |  |  |
| Link2/Link50 Trap Values |  | 00402288 |  |  |
| Link3/Link51 Trap Values |  | 0040228C |  |  |
| Link4/Link52 Trap Values |  | 00402290 |  |  |
| Link5/Link53 Trap Values |  | 00402294 |  |  |
| Link6/Link54 Trap Values |  | 00402298 |  |  |
| Link7/Link55 Trap Values |  | 0040229C |  |  |
| Link8/Link56 Trap Values |  | 004022A0 |  |  |
| Link9/Link57 Trap Values |  | 004022A4 |  |  |
| Link10/Link58 Trap Values |  | 004022A8 |  |  |
| Link11/Link59 Trap Values |  | 004022AC |  |  |
| Link12/Link60 Trap Values |  | 004022B0 |  |  |
| Link13/Link61 Trap Values |  | 004022B4 |  |  |
| Link14/Link62 Trap Values |  | 004022B8 |  |  |
| Link15/Link63 Trap Values |  | 004022BC |  |  |
| Link16/Link64 Trap Values |  | 004022C0 |  |  |
| Link17/Link65 Trap Values |  | 004022C4 |  |  |
| Link18/Link66 Trap Values |  | 004022C8 |  |  |
| Link19/Link67 Trap Values |  | 004022CC |  |  |
| Link20/Link68 Trap Values |  | 004022D0 |  |  |
| Link21/Link69 Trap Values |  | 004022D4 |  |  |
| Link22/Link70 Trap Values |  | 004022D8 |  |  |
| Link23/Link71 Trap Values |  | 004022DC |  |  |
| Link24/Link72 Trap Values |  | 004022E0 |  |  |
| Link25/Link73 Trap Values |  | 004022E4 |  |  |
| Link26/Link74 Trap Values |  | 004022E8 |  |  |
| Link27/Link75 Trap Values |  | 004022EC |  |  |
| Link28/Link76 Trap Values |  | 004022F0 |  |  |
| Link29/Link77 Trap Values |  | 004022F4 |  |  |
| Link30/Link78 Trap Values |  | 004022F8 |  |  |
| Link31/Link79 Trap Values |  | 004022FC |  |  |
| Link32/Link80 Trap Values |  | 00402300 |  |  |
| Link33/Link81 Trap Values |  | 00402304 |  |  |
| Link34/Link82 Trap Values |  | 00402308 |  |  |
| Link35/Link83 Trap Values |  | 0040230C |  |  |
| Link36/Link84 Trap Values |  | 00402310 |  |  |
| Link37/Link85 Trap Values |  | 00402314 |  |  |
| Link38/Link86 Trap Values |  | 00402318 |  |  |
| Link39/Link87 Trap Values |  | 0040231C |  |  |
| Link40/Link88 Trap Values |  | 00402320 |  |  |
| Link41/Link89 Trap Values |  | 00402324 |  |  |
| Link42/Link90 Trap Values |  | 00402328 |  |  |
| Link43/Link91 Trap Values |  | 0040232C |  |  |
| Link44/Link92 Trap Values |  | 00402330 |  |  |
| Link45/Link93 Trap Values |  | 00402334 |  |  |
| Link46/Link94 Trap Values |  | 00402338 |  |  |
| Link47/Link95 Trap Values |  | 0040233C |  |  |
| Event ID data value trap memory. The data field includes the L1ID and BCID values received from the module or chip and the expected L1ID value used in the error checking process. [n=0 to 47] | Bit Value |
|  | 1 | 0 |
| Bits[ 3: 0] : Module/Chip L1ID – Link(n) | Value |
| Bits[ 7: 4] : Expected Link L1ID – Link(n) | Value |
| Bits[15: 8] : Module/Chip BCID – Link(n) | Value |
| Bits[19:16] : Module/Chip L1ID - Link(n+48) | Value |
| Bits[23:20] : Expected Link L1ID – Link(n+48) | Value |
| Bits[31:24] : Module/Chip BCID – Link(n+48) | Value |

# ROD Router FPGA Registers

## DSP Trap Setup Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: DSP0 Command Register0, RTR_TRAP_CMND_0(0) | 1C2 | 00402400 | RW | 8 |
| Router: DSP1 Command Register0, RTR_TRAP_CMND_0(1) | 1C3 | 00402440 | RW | 8 |
| Router: DSP2 Command Register0, RTR_TRAP_CMND_0(2) | 1C4 | 00402480 | RW | 8 |
| Router: DSP3 Command Register0, RTR_TRAP_CMND_0(3) | 1C5 | 004024C0 | RW | 8 |
|  | Bit Value |
|  | 1 | 0 |
| Bit 0: Trap Atlas Specific Event Type | On | Off |
| Bit 1: Trap TIM Specific Event Type | On | Off |
| Bit 2: Trap ROD Specific Event Type | On | Off |
| Bit 3: Error Data Format (This bit is common to both Traps) Error Format: As the data comes into the router, six 32-bit words with 2 bits per link are built. The two bits encode the following cases: 00 = no data (the router did not get a header for this link) 01 = good data on the link, no errors 10 = bcid or l1id error 11 = timeout error Three of these words overwrite the event fragment trailer words t2-t4. The other three are additional words that would be inserted before the E0F00000 word in the event fragment trailer. Event fragment header into the DSP H0: 0xB0F00000 H1: 0xEE1234EE (start of header word) H2: 0x00000006 (number of header words) H2 H3: L1ID (level 1 ID) -> was H6 <- H4: BCID (bunch crossing ID) -> was H7 <- H5: L1TT (level 1 trigger type) -> was H8 <- H6: DET (detector event type) -> was H9 <- -- Event fragment trailer T0: error count (status 1: count of words with errors) T1: error flags (status 2: bitted error type occurrence word) T2: error status for links 15 - 0 (link 0 bits are stored in bits 1 & 0) T3: error status for links 31 - 16 T4: error status for links 47 - 32 T5: error status for links 63 - 48 T6: error status for links 79 - 64 T7: error status for links 95 - 80 T8: 0xE0F00000 | Error Format | S-Link Format |
| Bit 4: Slink Data Format to the SDSP with the Error codes included in the Event Fragment Trailer. | On | Off |
| Bit 5: Trap All Events | On | Off |
| Bit 6: Set Trap into Data Driven Mode (This bit is common to both Traps) If this bit is set, the router writes Events into the Internal FIFO in consecutive order such that more than 1 Event can occupy the same Frame in the DSP memory. If this bit is cleared, only 1 event will be present in each frame or multiple consecutive groups of frames. A word count of the event is always written to the last memory location of last frame used for the specific event. | On | Off |
| Bit 7: Trap All Error Events | On | Off |
| Bit 8: Trap Events that are larger than the Event Limit Threshold Event Limit Threshold value is set in EFB register 0x00402214 | On | Off |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: DSP0 Command Register1, RTR_TRAP_CMND_1(0) | 1C6 | 00402404 | RW | 7 |
| Router: DSP1 Command Register1, RTR_TRAP_CMND_1(1) | 1C7 | 00402444 | RW | 7 |
| Router: DSP2 Command Register1, RTR_TRAP_CMND_1(2) | 1C8 | 00402484 | RW | 7 |
| Router: DSP3 Command Register1, RTR_TRAP_CMND_1(3) | 1C9 | 004024C4 | RW | 7 |
|  | Bit Value |
|  | 1 | 0 |
| Bit 0: Trap Atlas Specific Event Type | On | Off |
| Bit 1: Trap TIM Specific Event Type | On | Off |
| Bit 2: Trap ROD Specific Event Type | On | Off |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: DSP0 Trap Reset/Load/Flush Reg, RTR_TRAP_RESET(0) | 1CA | 00402408 | RW | 4 |
| Router: DSP1 Trap Reset/Load/Flush Reg, RTR_TRAP_RESET(1) | 1CB | 00402448 | RW | 4 |
| Router: DSP2 Trap Reset/Load/Flush Reg, RTR_TRAP_RESET(2) | 1CC | 00402488 | RW | 4 |
| Router: DSP3 Trap Reset/Load/Flush Reg, RTR_TRAP_RESET(3) | 1CD | 004024C8 | RW | 4 |
| All bits in this Register are self-clearing | Bit Value |
|  | 1 | 0 |
| Bit 0: Reset Trap This bit resets both Traps for a specific DSP. | Reset |  |
| Bit 1: Load New Trap0 Value This bit must be set to load new trap information for Trap0. | Load |  |
| Bit 2: Load New Trap1 Value This bit must be set to load new trap information for Trap1. | Load |  |
| Bit 3: Flush Trap FIFO This bit flushes the Trap FIFO for a specific DSP | Flush |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: DSP0 Status Register, RTR_TRAP_STATUS(0) | 1CE | 0040240C | RW | 9 |
| Router: DSP1 Status Register, RTR_TRAP_STATUS(1) | 1CF | 0040244C | RW | 9 |
| Router: DSP2 Status Register, RTR_TRAP_STATUS(2) | 1D0 | 0040248C | RW | 9 |
| Router: DSP3 Status Register, RTR_TRAP_STATUS(3) | 1D1 | 004024CC | RW | 9 |
|  | Bit Value |
|  | 1 | 0 |
| Bit 0: Trap Enable Control from DSP | Enabled | Idle |
| Bit 1: Interrupt Mask Control from DSP | Mask DFR Int | Allow DFR Int |
| Bit 2: Trapping FIFO Empty | Empty | Not Empty |
| Bit 3: Trapping FIFO Full | Full | Not Full |
| Bit 4: Trap0 – Trap match detected AND/OR Trapping Data | On | Off |
| Bit 5: Trap1 – Trap match detected AND/OR Trapping Data | On | Off |
| Bit 6: Trap0 Ready (Clears on WR to Cmd Reg0, Set on Load New Trap0) | Ready | Not Ready |
| Bit 7: Trap1 Ready (Clears on WR to Cmd Reg1, Set on Load New Trap1) | Ready | Not Ready |
| Bit 8: DSP0 SBSRAM Clock DLL Locked | Locked | Not Locked |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: DSP0 Trap Match Reg0, RTR_TRAP_MATCH_0(0) | 1D2 | 00402410 | RW | 8 |
| Router: DSP1 Trap Match Reg0, RTR_TRAP_MATCH_0(1) | 1D3 | 00402450 | RW | 8 |
| Router: DSP2 Trap Match Reg0, RTR_TRAP_MATCH_0(2) | 1D4 | 00402490 | RW | 8 |
| Router: DSP3 Trap Match Reg0, RTR_TRAP_MATCH_0(3) | 1D5 | 004024D0 | RW | 8 |
|  | Bit Value |
| Bits[ 7:0]: Trap Match value for DSP Command Reg0 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: DSP0 Pre-Scale Value Reg0, RTR_TRAP_MOD_0(0) | 1D6 | 00402414 | RW | 16 |
| Router: DSP1 Pre-Scale Value Reg0, RTR_TRAP_MOD_0(1) | 1D7 | 00402454 | RW | 16 |
| Router: DSP2 Pre-Scale Value Reg0, RTR_TRAP_MOD_0(2) | 1D8 | 00402494 | RW | 16 |
| Router: DSP3 Pre-Scale Value Reg0, RTR_TRAP_MOD_0(3) | 1D9 | 004024D4 | RW | 16 |
| If Trap Match Scale = 0, trap 1 event only If Trap Match Scale = 1, trap all events that match the Trap Match value If Trap Match Scale > 1, trap all events that meet the following. Trap Match is true (Increment Trap Match Count), AND Trap Match Count = Trap Match Remainder (Scale=Period) EXPLAIN REMAINDER FUNCTION | Bit Value |
| Bits[ 7:0]: Trap Match Scale for Trap 0 | Value |
| Bits[15:8]: Trap Match Remainder for Trap0 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: DSP0 Trap Match Reg1, RTR_TRAP_MATCH_1(0) | 1DA | 00402418 | RW | 8 |
| Router: DSP1 Trap Match Reg1, RTR_TRAP_MATCH_1(1) | 1DB | 00402458 | RW | 8 |
| Router: DSP2 Trap Match Reg1, RTR_TRAP_MATCH_1(2) | 1DC | 00402498 | RW | 8 |
| Router: DSP3 Trap Match Reg1, RTR_TRAP_MATCH_1(3) | 1DD | 004024D8 | RW | 8 |
|  | Bit Value |
| Bits[ 7:0]: Trap Match value for DSP Command Reg1 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: DSP0 Pre-Scale Value Reg1, RTR_TRAP_MOD_1(0) | 1DE | 0040241C | RW | 16 |
| Router: DSP1 Pre-Scale Value Reg1, RTR_TRAP_MOD_1(1) | 1DF | 0040245C | RW | 16 |
| Router: DSP2 Pre-Scale Value Reg1, RTR_TRAP_MOD_1(2) | 1E0 | 0040249C | RW | 16 |
| Router: DSP3 Pre-Scale Value Reg1, RTR_TRAP_MOD_1(3) | 1E1 | 004024DC | RW | 16 |
| If Trap Match Scale = 0, trap 1 event only If Trap Match Scale = 1, trap all events that match the Trap Match value If Trap Match Scale > 1, trap all events that meet the following. Trap Match is true (Increment Trap Match Count), AND Trap Match Count = Trap Match Remainder (Scale=Period) | Bit Value |
| Bits[ 7:0]: Trap Match Scale for Trap 1 | Value |
| Bits[15:8]: Trap Match Remainder for Trap1 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: DSP0 FIFO Word Count, RTR_TRAP_FIFO_WRD_CNT(0) | 1E6 | 00402424 | R | 10 |
| Router: DSP1 FIFO Word Count, RTR_TRAP_FIFO_WRD_CNT(1) | 1E7 | 00402464 | R | 10 |
| Router: DSP2 FIFO Word Count, RTR_TRAP_FIFO_WRD_CNT(2) | 1E8 | 004024A4 | R | 10 |
| Router: DSP3 FIFO Word Count, RTR_TRAP_FIFO_WRD_CNT(3) | 1E9 | 004024E4 | R | 10 |
|  | Bit Value |
| Bits[ 9: 0]: Internal FIFO Word Count | Value |
| Bits[15:12]: Data Frame Ready State Machine Status State Value Reset 0x0 Idle 0x1 Re-Test Occupancy 0x2 Issue Frame Ready Interrupt 0x3 Wait for ISR handshake 0x4 ISR Done 0x5 Decrement Block Count 0x6 Mask Interrupt Request 0x7 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: DSP0 Interrupt Mask Delay Count RTR_TRAP_INT_DELAY_CNT(0) | 1F2 | 00402430 | RW | 6 |
| Router: DSP1 Interrupt Mask Delay Count RTR_TRAP_INT_DELAY_CNT(1) | 1F3 | 00402470 | RW | 6 |
| Router: DSP2 Interrupt Mask Delay Count RTR_TRAP_INT_DELAY_CNT(2) | 1F4 | 004024B0 | RW | 6 |
| Router: DSP3 Interrupt Mask Delay Count RTR_TRAP_INT_DELAY_CNT(3) | 1F5 | 004024F0 | RW | 6 |
| This value is used to prevent the Router from issuing interrupts before the Slave DSP has finished exiting its ISR. | Bit Value |
|  | 1 | 0 |
| Bits[ 5:0]: Interrupt Mask Delay Count Value | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: DSP0 Interrupt 4 Period (Diagnostic Reg) |  | 00402434 | RW | 16 |
| Router: DSP1 Interrupt 4 Period (Diagnostic Reg) |  | 00402474 | RW | 16 |
| Router: DSP2 Interrupt 4 Period (Diagnostic Reg) |  | 004024B4 | RW | 16 |
| Router: DSP3 Interrupt 4 Period (Diagnostic Reg) |  | 004024F4 | RW | 16 |
| This value is used to set the period of DSP INT4 pulses sent to the Slave DSPs. If this value is 0, no interrupts will be sent. If the value is equal to 1, the RTR will set the Int4 signal to value = 1. The output signal is not gated by the mask interrupt function, so the user must check that the DSP is ready to accept an interrupt before generating the pulse. If the value is greater than 1, the period of the pulse train will be equal to the register value multiplied by 100ns. | Bit Value |
|  | 1 | 0 |
| Bits[15:0]: Interrupt 4 Period Count Value | Value |

## Router Slink Command and Status Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: Command/Status Register, RTR_CMND_STAT | 202 | 00402500 | RW | 16 |
|  | Bit Value |
|  | 1 | 0 |
| Bit 0: Dump Atlas Specific Event Type | On | Off |
| Bit 1: Dump TIM Specific Event Type | On | Off |
| Bit 2: Dump ROD Specific Event Type | On | Off |
| Bit 3: Inhibit S-Link Write Enable This bit allows the user to block writes to the S-Link. Slink Xoff is ignored is this bit is set to value = 1. | Inhibit | Allow |
| Bit 4: Reset S-Link | Reset | Ready |
| Bit 5: Set S-Link Test Bit | Test | Normal |
| Bit 6: Enable Calibration Back Pressure to EFB This bit can only be used in Calibration and Configuration | Enable | Disable |
| Bit 7: Mask LDOWN# Bit (Allow data transmission when S-Link is down) | Mask | Normal |
| Bit 8: S-Link Xoff Status (Read Only) | Xoff | Xon |
| Bit 9: S-Link LDown Status (Read Only) | LDown | OK |
| Bit 10: Stop Output (Back pressure to the EFB) (Read Only) | Stop EFB | OK |
| Bit 11: 40MHz Clock DLL Locked (Read Only) | Locked | Error |
| Bit 12: 80MHz Clock DLL Locked (Read Only) | Locked | Error |
| Bit 13: S-Link Xoff Status Latched (Read Only) | Xoff | OK |
| Bit 14: S-Link Endianess Bit (SCT Only) | LE | BE |
| Bit 15: Manual Xoff Control | Xoff | Xon |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: S-Link Atlas/TIM Event Type Dump Match Register RTR_SLNK_ATLAS_DUMP_MATCH | 203 | 00402504 | RW | 10 |
|  | Bit Value |
| Bits[ 7:0]: Atlas Specific Event Type | Value |
| Bits[ 9:8]: TIM Specific Event Type | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: S-Link ROD Specific Dump Match Register RTR_SLNK_ATLAS_DUMP_MATCH | 204 | 00402508 | RW | 6 |
|  | Bit Value |
| Bits[ 5:0]: ROD Specific Event Type | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: Code Version - RTR_CODE_VERSION | 205 | 0040250C | RW | 16 |
|  | Bit Value |
| Bits[ 7:0]: Code Version | Value |
| Bits[14:8]: Board Revision of Code | Value |
| Bit[15]: ROD Type | Pixel | SCT |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: Test Output Mux Register - RTR_OUTPUT_SIGNAL_MUX | 206 | 00402510 | RW | 4 |
| Selects the group of test outputs for the Router | Bit Value |
| Bits[ 3:0]: Test Output Mux Value | Value |
| Bits[ 7:4]: S-Link Occupancy Counter Control CODES: 0x0==Stop, 0x1==Start, 0x2==Reset, 0x3==TBD | Value |
| Bits[15:8]: Not Used |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: Xoff Counter Register – RTR_XOFF_COUNT | 207 | 00402514 | R | 16 |
| Indicates the number of times that Xoff has been asserted. Self clears when it is read. | Bit Value |
| Bits[15:0]: Xoff Counter Value | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: S-Link FIFO Status – RTR_SLFIFO_STAT |  | 00402518 | R | 3 |
| Indicates the occupancy status of the S-Link pipeline FIFO at the output of the Router. | Bit Value |
|  | 1 | 0 |
| Bit[0]: S-Link FIFO Empty | EMPTY |  |
| Bit[1]: S-Link FIFO Almost Full | AFULL |  |
| Bit[2]: S-Link FIFO Full | FULL |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: Next Event Delay Count Register – RTR_NEXT EVT_DELAY_COUNT |  | 0040251C | R | 16 |
| To prevent events overlap in calibration mode when multiple group are configured, the B0F and E0F words need to be separated by multiple system clocks. This register allows the user to adjust the time between the end of one event and the star of another for calibration type data runs. The default value is 0x8 (200ns). This function of the register is only active when the Calibration back pressure bit on the Router is valid. | Bit Value |
| Bits[15:0]: Next Event Delay Count | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: S-Link Clock Counter – RTR_SLINK_CLK_COUNT_MSW |  | 00402520 | R | 16 |
| Indicates the number of system clocks periods. Register captures bits[31:16]. The counters must be stopped using the S-Link Counter Control bits in register 0x00402510 to read accurate values from the registers | Bit Value |
| Bits[15:0]: S-Link Clock Count [31:16] | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: S-Link Clock Counter – RTR_SLINK_CLK_COUNT_LSW |  | 00402524 | R | 16 |
| Indicates the number of system clocks periods. Register captures bits[15:0]. The counters must be stopped using the S-Link Counter Control bits in register 0x00402510 to read accurate values from the registers | Bit Value |
| Bits[15:0]: S-Link Clock Count [15:0] | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: S-Link Word Counter – RTR_SLINK_WORD_COUNT_MSW |  | 00402528 | R | 16 |
| Indicates the number of words transmitted up the S-Link. Register captures bits[31:16]. S-Link BW can be calculated using the S-Link Clock Counter Register values. The counters must be stopped using the S-Link Counter Control bits in register 0x00402510 to read accurate values from the registers | Bit Value |
| Bits[15:0]: S-Link Word Count [31:16] | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Router: S-Link Word Counter – RTR_SLINK_WORD_COUNT_LSW |  | 0040252C | R | 16 |
| Indicates the number of words transmitted up the S-Link. Register captures bits[15:0]. S-Link BW can be calculated using the S-Link Clock Counter Register values. The counters must be stopped using the S-Link Counter Control bits in register 0x00402510 to read accurate values from the registers The counters must be stopped using the S-Link Counter Control bits in register 0x00402510 to read accurate values from the registers The counters must be stopped using the S-Link Counter Control bits in register 0x00402510 to read accurate values from the registers | Bit Value |
| Bits[15:0]: S-Link Word Count [15:0] | Value |

# ROD Controller FPGA Registers

## ROD Controller Command, Status and Mode Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Master DSP General Purpose Register | 1C5 | 00404400 | RW | 2 |
|  | Bit Value |
|  | 1 | 0 |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: General Purpose Diagnostics Register |  | 00404404 | R | 32 |
|  | Bit Value |
| TBD | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: HPI Time Out Counter: |  | 00404408 | RW | 32 |
|  | Bit Value |
| Bits[31:0]: HPI Time Out Counter Value | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Code Version and ROD Board Revision: RRIF_CODE_VERSION | 216 | 0040440C | RW | 16 |
|  | Bit Value |
| Bits[ 7:0]: Code Version Number | Value |
| Bits[15:8]: ROD Board Revision Number | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Main Control Register, RRIF_CMND_1 | 217 | 00404410 | RW | 32 |
|  | Bit Value |
|  | 1 | 0 |
| Bit 0: Enable/Disable FE Command Output Data Streams | On | Off |
| Bit 1: Select FE Command Input Source for Mask0 | TIM | DSP SP0 |
| Bit 2: FE Command Mask, “New Mask Ready Bit” (Self Clearing) In Normal Data Taking Mode, when a new FE Command Link Mask has been written to the RCF from the MDSP, this bit must be set to allow the next L1A to use the new mask. If the RRIF_CMND_1, Bit(20) is set, the new mask will be loaded when this bit is set. | Ready | Idle |
| Bit 3: FE Occupancy Counter Enable, Read Link Trailers | Enable | Reset |
| Bit 4: NOT USED |  |  |
| Bit 5: FE Command Pulse Counter Enable When enabled, all L1 Triggers sent to the ROD will increment this counter, and a Command Cycle will be initiated. When a Command Cycle has been completed (Mode bits and Token to the Formatters, and Dynamic Mask to the EFB) the counter will be decremented. | Enable | Reset |
| Bit 6: FE Command Pulse Counter Load Loads maximum value into the FE Command Pulse Counter. This is a function that is used for diagnostic test only. | Load | Idle |
| Bit 7: NOT USED |  |  |
| Bit 8: Trigger Signal Decoder Enable Enable for TIM/TTC serial data decoders. | Enable | Reset |
| Bit 9: NOT USED |  |  |
| Bit 10: Formatter Mode Bits Encoder Enable Enable for the block that writes Dynamic Mode Bit data to the Formatters for each L1 Trigger | Enable | Reset |
| Bit 11: NOT USED |  |  |
| Bit 12: EFB Dynamic Mask Encoder Enable Enable for the block that writes the Event ID ad Dynamic Mask Bit data to the EFB for each L1 Trigger | Enable | Reset |
| Bit 13: NOT USED |  |  |
| Bit 14: NOT USED |  |  |
| Bit 15: NOT USED |  |  |
| Bit 16: Test Bench I/O Enable Enable for the Internal Test Bench Block used for stand-alone testing of the ROD. The Debug-Mode Configuration Registers are used to configure different tests on the ROD. | Enable | Reset |
| Bit 17: Test Bench I/O Run This bit starts the ROD test, and must be cleared by the host when the test is finished. See the Debug-Mode Status Register definitions for more information | Run | Idle |
| Bit 18: Calibration Trigger Signal Decoder Enable This bit selects the ROD Register Calibration Parameters to be used for the testing of Data Taking Modes and calibration and enables the RCF block that detects Command types from the Serial Port Inputs. | Enable | Idle |
| Bit 19: Configuration Read back Enable This bit enables the trapping of data on the input links to the ROD into the Input Memory FIFO. | Enable | Idle |
| Bit 20: Configuration/Calibration Mask Load Enable This bit allows a new FE Command mask to be loaded when the ROD is configuring Modules or is in Calibration Mode | Enable Load | Idle |
| Bit 21: Static Calibration BCID Enable This bit selects between the value for the BCID used during calibration | Static BCID | Dynamic BCID |
| Bit 22: Static Calibration L1ID Enable This bit selects between the value for the L1ID used during calibration | Static L1ID | Dynamic L1ID |
| Bit 23: Corrective Mode Bits and Dynamic Mask Ready (Self Clearing) This bit indicates that corrective Mode Bits and Dynamic Mask bits have been set and are ready to transmit when the next L1A is detected. | Mask Ready | Idle |
| Bit 24: Input Memory FIFO Playback Inhibit | Inhibit | Play |
| Bit 25: Control Signal Mux(0) | See “Modes of Operation” Table |
| Bit 26: Control Signal Mux(1) |  |
| Bit 27: Control Signal Mux(2) |  |
| Bit 28: Control Signal Mux(3) |  |
| Bit 29: Start Internal Scan Engine (WR protected for SCT ROD) | Start | Stop |
| Bit 30: Clear Internal Scan Engine nEvent Counters | Clear | Idle |
| Bit 31: Not Used |  |  |

| Control Signal Mux Value Bits[28:25] | Modes of Operation |
| --- | --- |
| “0000” | Disable FE Inputs |
| “0001” | Connect the RCF FIFO Interface Control Signals to the Diagnostic FIFOs This mode is used to Load and Read the FIFOs with MDSP control |
| “0010” | Connect FE Input Control to the Test Bench Interface Control Signals |
| “0011” | Not Used - Disable FE Inputs |
| “0100” | Enable the normal data Path |
| “0101” | Connect FE Input control for Configuration Readback Mode |
| “0110” | Connect FE Input control for Calibration Test Mode |
| “0111” | Route the input link data to the InMems and Formatters |
| “1000”-“1111” | Not Used - Disable FE Inputs |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Spare Control Register, RRIF_CMND_0 | 218 | 00404414 | RW | 13 |
|  | Bit Value |
|  | 1 | 0 |
| Bit 0: Formatter A Mode Bits FIFO Reset (default: ‘0’, ‘1’ self clearing) | Reset | Ready |
| Bit 1: Formatter B Mode Bits FIFO Reset (default: ‘0’, ‘1’ self clearing) | Reset | Ready |
| Bit 2: EFB Dynamic Mask Bits FIFO Reset (default: ‘0’, ‘1’ self clearing) | Reset | Ready |
| Bit 3: INMEM FIFO Reset | Reset | Ready |
| Bit 4: Not Used |  |  |
| Bit 5: Not Used |  |  |
| Bit 6: Internal TIM FIFO Reset | Reset | Ready |
| Bit 7: Corrective Trigger FIFO Reset | Reset | Ready |
| Bit 8: Internal TIM FIFO Re-Transmit (default: ‘0’, ‘1’ self clearing) | Re-Tx | Idle |
| Bit 9: INMEM FIFO Re-Transmit (default: ‘0’, ‘1’ self clearing) | Re-Tx | Idle |
| Bit 10: Diagnostic EFB Generated ROD Busy | Enable | Disable |
| Bit 11: Diagnostic Event Counters | Enable | Reset |
| Bit 12: ECR ID Counter Reset | Reset | Idle |
| Bits [17:13]: SP1 Frame Sync Offset If Offset Value = 0, the frame sync pulse to SP0 and SP1 will occur on the same clock edge. If Offset Value = n, the Frame Sync pulse to SP1 will occur n system clocks after the Frame Sync pulse for SP0. | Offset Value |
| Bit 18: FSX CLKX Output Enable This bit allows the RCF FSX and CLKX outputs to be set to High Z. | On | Off |
| Bit 19: SP0 Input Mask | Mask | On |
| Bit 20: SP1 Input Mask | Mask | On |
| Bits[24:21]: Not Used |  |  |
| Bit 25: MDSP Tout Enable | On | Off |
| Bit 26: MDSP INT4 Enable | On | Off |
| Bit 27: MDSP INT5 Enable | On | Off |
| Bit 28: MDSP INT6 Enable | On | Off |
| Bit 29: MDSP INT7 Enable | On | Off |
| Bit 30: SDSP Interrupt Enable (All Slaves) | On | Off |
| Bit 31: VME Interrupt Enable | On | Off |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Mode Register, ROD_MODE_REG | 219 | 00404418 | RW | 4 |
| Bits[3:0]: ROD Controller Modes. The ROD Controller Mode is controlled by the MDSP. The Event ID Wait Limit value sets the amount of time the FE Trigger Decoder will wait for an Event ID to arrive from the TIM. If set to 0x0h, the RCF will wait forever if an Event ID does not arrive. | Bit Value |
| Bits[ 3:0]: FE Mask Select | Value |
| Bits[31:8]: Event ID Wait Limit (25ns Increments) | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: FE Mask LUT Select, FE_MASK_LUT_SELECT | 21A | 0040441C | RW | 3 |
|  | Bit Value |
| Bits[ 2:0]: FE Mask Select | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Main Status Register, RRIF_STATUS_1 | 21B | 00404420 | R | 32 |
|  | Bit Value |
|  | 1 | 0 |
| Bit 0: TIM Clock OK | OK | Fail |
| Bit 1: BOC Clock OK | OK | Fail |
| Bit 2: BOC Busy | Busy | Ready |
| Bit 3: Configuration Read Back Done/Trap Link Data Done | Done | Ready |
| Bit 4: Cal Test Ready | Ready | Running |
| Bit 5: FE Trigger FIFO Empty Flag | Empty | Not |
| Bit 6: FE Trigger FIFO Full Flag | Full | Not |
| Bit 7: Formatter A, EFB Stop Output | Stop Tx | TX OK |
| Bit 8: Formatter A Mode Bits FIFO Full Flag | Full | Not |
| Bit 9: Formatter B EFB Stop Output | Stop Tx | TX OK |
| Bit 10: Formatter B Mode Bits FIFO Full Flag | Full | Not |
| Bit 11: Header/Trailer Limit Formatter Bank A | Limit | OK |
| Bit 12: Header/Trailer Limit Formatter Bank B | Limit | OK |
| Bit 13: ROD Busy Limit Formatter Bank A | Busy | OK |
| Bit 14: ROD Busy Limit Formatter Bank B | Busy | OK |
| Bit 15: EFB Dynamic Mask Bits FIFO Empty Flag | Empty | Not |
| Bit 16: EFB Dynamic Mask Bits FIFO Full Flag | Full | Not |
| Bit 17: EFB Event ID Empty Error If this bit is set, the data from the Formatters has arrived at the EFB before the ID information was ready for the building of the event. This is a fatal error that requires a soft reset for recovery. | Error | OK |
| Bit 18: Event Memory A FIFO Empty Flag | Empty | Not |
| Bit 19: Event Memory A FIFO Full Flag | Full | Not |
| Bit 20: Event Memory B FIFO Empty Flag | Empty | Not |
| Bit 21: Event Memory B FIFO Full Flag | Full | Not |
| Bits[29:22]: FE Command Pulse Counter | Count |
| Bit 30: FE Occupancy Counters All Zero | All Zero | > Zero |
| Bit 31: Command Mask Ready | Ready | Not |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Spare Status Register, RRIF_STATUS_0 | 21C | 00404424 | R | 32 |
|  | Bit Value |
| Bits [ 7:0]: TTC line Monitor | Value |
| Bits [18:8]: Trigger Counter Value | Count |
| Bit 19: External Interrupt Ack Num Input 0 | Ack | Clear |
| Bit 20: External Interrupt Ack Num Input 1 | Ack | Clear |
| Bit 21: External Interrupt Ack Num Input 2 | Ack | Clear |
| Bit 22: External Interrupt Ack Num Input 3 | Ack | Clear |
| Bit 23: External Interrupt Ack Num Input 4 | Ack | Clear |
| Bit 24: RCF DLL Locked | Locked | Not |
| Bit 25: S-Link Xoff | Xoff | OK |
| Bit 26: S-Link Down or not Installed | Down | OK |
| Bit 27: Slave DSP0 Detect Input | Present | Not |
| Bit 28: Slave DSP1 Detect Input | Present | Not |
| Bit 29: Slave DSP2 Detect Input | Present | Not |
| Bit 30: Slave DSP3 Detect Input | Present | Not |
| Bit 31: ROD Type from EFB | Pixel | SCT |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: ROD BUSY Status Register |  | 00404428 | RW | 32 |
|  | Bit Value |
|  | 1 | 0 |
| Bit [0]: Main ROD BUSY to PRM (Latched) | BUSY | OK |
| Bit [1]: Formatter Bank A ROD Busy (Latched) | BUSY | OK |
| Bit [2]: Formatter Bank B ROD Busy (Latched) | BUSY | OK |
| Bit [3]: EFB Event Header FIFO ROD Busy (Latched) | BUSY | OK |
| Bit [4]: Pause ROL Triggers (Latched) | BUSY | OK |
| Bit [5]: Pause Formatter Bank A from EFB (Latched) | BUSY | OK |
| Bit [6]: Pause Formatter Bank B from EFB (Latched) | BUSY | OK |
| Bit [7]: RCF Internal Test Pause Triggers (Latched) (USE TO MONITOR DSP TRIGGER RATE EFFECTS ON ROD BUSY) | BUSY | OK |
| Bit [8]: Sweeper Event on ROD (Latched) | Sweeper | OK |
| Bit [9]: Formatter Bank A Header Trailer Limit (Latched) | LIMIT | OK |
| Bit [10]: Formatter Bank B Header Trailer Limit (Latched) | LIMIT | OK |
| Bit [11]: TBD |  |  |
| Bit [12]: Main ROD BUSY to PRM | BUSY | OK |
| Bit [13]: Formatter Bank A ROD Busy | BUSY | OK |
| Bit [14]: Formatter Bank B ROD Busy | BUSY | OK |
| Bit [15]: EFB Event Header FIFO ROD Busy | BUSY | OK |
| Bit [16]: Pause ROL Triggers | BUSY | OK |
| Bit [17]: Pause Formatter Bank A from EFB | BUSY | OK |
| Bit [18]: Pause Formatter Bank B from EFB | BUSY | OK |
| Bit [19]: RCF Internal Test Pause Triggers (USE TO VETO TRIGGERS IN DSP SCAN MODES) | BUSY | OK |
| Bit [20]: Sweeper Event on ROD | Sweeper | OK |
| Bit [21]: Formatter Bank A Header Trailer Limit | LIMIT | OK |
| Bit [22]: Formatter Bank B Header Trailer Limit | LIMIT | OK |
| Bit [23]: TBD |  |  |
| Bit [24]: Manual ROD Busy (R/W) | BUSY | OK |
| Bits [31:24]: TBD |  |  |
| MAIN ROD BUSY sent to TIM for use as system ROD BUSY signal MAIN ROD BUSY == Formatter Bank A ROD Busy OR Formatter Bank B ROD Busy OR Event Header FIFO ROD Busy OR Pause ROL Triggers RCF Pause Triggers used for internal ROD triggers only. NO AFFECT IN PHYSICS DATA TAKING MODES RCF Pause Triggers == Formatter Bank A ROD Busy OR Formatter Bank B ROD Busy OR Event Header FIFO ROD Busy OR Pause ROL Triggers OR Pause Formatter Bank A OR Pause Formatter Bank B |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: EFB Event ID Wait Value |  | 0040442C | R | 24 |
| Maximum duration of time between the arrival of an L1A and the Event ID from the TIM | Bit Value |
| Bits[ 23:0]: Event ID Wait Value (25ns Increments) | Value |

## ROD Controller FE Command Stream Mask Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: FE Command Link Mask0_LO Register FE_CMND_MASK_0_LO | 21F | 00404430 | RW | 32 |
| Mask for Data Streams 0 to 31. This Mask applies to the Serial Data Streams generated by the TIM or MDSP SP0. | Bit Value |
|  | 1 | 0 |
| Bits [31:0]: FE Command Link 0 to 31 Mask Bit 0 sets the mask for Link 0, bit 1 for link 1, up to bit 31 for link 31. To load the mask, the “New Mask Ready” bit must be set in the Main Control Register after the mask value has been written to this register. If the ROD is in Normal Data Taking Mode, the Mask will be loaded when the next L1 Trigger is received from the TIM. If the “Config/Cal Mask Load Enable” bit is set in the Main Control Register, the mask will be loaded when the “New Mask Ready” bit is set. | Enable Output | Mask Output |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: FE Command Link Mask0_HI Register FE_CMND_MASK_0_HI | 220 | 00404434 | RW | 16 |
| Mask for Data Streams 32 to 47. This Mask applies to the Serial Data Streams generated by the TIM or MDSP SP0. | Bit Value |
|  | 1 | 0 |
| Bits [31:0]: FE Command Link 32 to 47 Mask Bit 0 sets the mask for Link 32, bit 1 for link 37, up to bit 15 for link 47. To load the mask, the “New Mask Ready” bit must be set in the Main Control Register after the mask value has been written to this register. If the ROD is in Normal Data Taking Mode, the Mask will be loaded when the next L1 Trigger is received from the TIM. If the “Config/Cal Mask Load Enable” bit is set in the Main Control Register, the mask will be loaded when the “New Mask Ready” bit is set. | Enable Output | Mask Output |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: FE Command Link Mask1_LO Register FE_CMND_MASK_1_LO | 221 | 00404438 | RW | 32 |
| Mask for Data Streams 0 to 31. This Mask applies to the Serial Data Streams generated by MDSP SP1. | Bit Value |
|  | 1 | 0 |
| Bits [31:0]: FE Command Link 0 to 31 Mask Bit 0 sets the mask for Link 0, bit 1 for link 1, up to bit 31 for link 31. To load the mask, the “New Mask Ready” bit must be set in the Main Control Register after the mask value has been written to this register. If the ROD is in Normal Data Taking Mode, the Mask will be loaded when the next L1 Trigger is received from the TIM. If the “Config/Cal Mask Load Enable” bit is set in the Main Control Register, the mask will be loaded when the “New Mask Ready” bit is set. | Enable Output | Mask Output |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: FE Command Link Mask1_HI Register FE_CMND_MASK_1_HI | 222 | 0040443C | RW | 16 |
| Mask for Data Streams 32 to 47. This Mask applies to the Serial Data Streams generated by MDSP SP1. | Bit Value |
|  | 1 | 0 |
| Bits [31:0]: FE Command Link 32 to 47 Mask Bit 0 sets the mask for Link 32, bit 1 for link 37, up to bit 15 for link 47. To load the mask, the “New Mask Ready” bit must be set in the Main Control Register after the mask value has been written to this register. If the ROD is in Normal Data Taking Mode, the Mask will be loaded when the next L1 Trigger is received from the TIM. If the “Config/Cal Mask Load Enable” bit is set in the Main Control Register, the mask will be loaded when the “New Mask Ready” bit is set. | Enable Output | Mask Output |

## ROD Controller Calibration Command Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Calibration Strobe Delay Register CALSTROBE_DELAY | 223 | 00404440 | RW | 8 |
| Sets the amount of delay in 25ns increments that will be inserted before sending the contents of the Cal Command Register after receiving a Cal Strobe from the TIM | Bit Value |
| Bits [7:0]: Calibration Strobe Delay | Count |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Calibration Command Data Register CAL_CMND | 224 | 00404444 | RW | 26 |
| Sets the Calibration Command Serial Data Stream to be sent after receiving a Cal Strobe from the TIM. SCT ONLY | Bit Value |
| Bits [25:0]: Calibration Command Data | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: ECR Counter Register ECR_COUNTER_VAL | 225 | 00404448 | RW | 8 |
| Used to set the required ECR Counter value. | Bit Value |
| Bits [7:0]: Initial ECR Value | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: ECR Counter Register ECR_COUNTER_STAT | 226 | 0040444C | RW | 8 |
| ECR Counter Value Monitor. | Bit Value |
| Bits [7:0]: Current ECR Value | Value |

## ROD Controller Mode Bits and Dynamic Mask Status Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Formatter Mode Bits FIFO Status Reg FRMT_RMB_STATUS | 227 | 00404450 | R | 32 |
|  | Bit Value |
|  | 1 | 0 |
| Bit 0: Internal Formatter A Mode Bits FIFO Empty Flag | Empty | OK |
| Bit 1: Internal Formatter A Mode Bits FIFO Full Flag | Full | OK |
| Bits [9:2]: Internal Formatter A Mode Bits Occupancy Count | Count |
| Bits [15:10]: Not Used |  |  |
| Bit 16: Internal Formatter B Mode Bits FIFO Empty Flag | Empty | OK |
| Bit 17: Internal Formatter B Mode Bits FIFO Full Flag | Full | OK |
| Bits [25:18]: Internal Formatter B Mode Bits Occupancy Count | Count |
| Bits [31:26]: Not Used |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: EFB Dynamic Mask FIFO Flags Status Reg EFB_DM_FIFO_FLAG_STA | 229 | 00404458 | R | 32 |
|  | Bit Value |
|  | 1 | 0 |
| Bit 0: Internal L1ID/BCID FIFO Empty Flag | Empty | OK |
| Bit 1: Internal Trigger Type FIFO Empty Flag | Empty | OK |
| Bit 2: Internal L1ID/BCID/TT FIFO Empty Flag | Empty | OK |
| Bit 3: Internal Default Dynamic Mask FIFO Empty Flag | Empty | OK |
| Bit 4: Internal Corrective Dynamic Mask FIFO Empty Flag | Empty | OK |
| Bits[7:5]: Not Used |  |  |
| Bit 8: Internal L1ID/BCID FIFO Full Flag | Full | OK |
| Bit 9: Internal Trigger Type FIFO Full Flag | Full | OK |
| Bit 10: Internal L1ID/BCID/TT FIFO Full Flag | Full | OK |
| Bit 11: Internal Default Dynamic Mask FIFO Full Flag | Full | OK |
| Bit 12: Internal Corrective Dynamic Mask FIFO Full Flag | Full | OK |
| Bits[31:13]: Not Used |  |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: EFB Dynamic Mask FIFO Word Count Reg EFB_DM_WC_STA_REG | 22A | 0040445C | R | 32 |
| Word Count Status for all of the FIFO used in the EFB Dynamic Mask Encoder Block of the Controller FPGA. | Bit Value |
|  | 1 | 0 |
| Bits[ 6: 0]: Internal L1ID/BCID FIFO Count | Count |
| Bits[14: 8]: Internal Trigger Type FIFO Count | Count |
| Bits[22:16]: Internal Event Mask FIFO Count | Count |
| Bits[30:24]: Internal Event Header FIFO Count | Count |

## ROD Controller Diagnostic Counters Command and Status Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Inmem A/B Count Register, INP_MEM_CTRL | 22B | 00404460 | RW | 32 |
| The ROD Controller Test Bench Block uses these counter registers. See the section that describes the Test Bench Modes to see the definitions for each of the registers. Each increment in value is equal to 25ns. | Bit Value |
| Bits[15: 0]: Inmem A Count Value | Count |
| Bits[31:16]: Inmem B Count Value | Count |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: DEBUGMEM A/B Count Register, DBG_MEM_CTRL | 22C | 00404464 | RW | 32 |
| The ROD Controller Test Bench Block uses these counter registers. See the section that describes the Test Bench Modes to see the definitions for each of the registers. Each increment in value is equal to 25ns. | Bit Value |
| Bits[15: 0]: DEBUGMEM A Count Value | Count |
| Bits[31:16]: DEBUGMEM B Count Value | Count |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Configuration Readback Count Register CFG_READBACK_CNT | 22D | 00404468 | RW | 32 |
| The ROD Controller uses these counter registers to set the parameters used when configuration data is being read back from the modules. Each increment in value is equal to 25ns. | Bit Value |
| Bits[15: 0]: Write FIFO Count Value This value sets the length of time that the FIFO will be trapping data. | Count |
| Bits[31:16]: Delay FIFO Write Count Value This value sets the length of delay from the time that the “Configuration ReadBack” bit (Bit 19, Register 0x00404410) is set to when Write Enable is active on the Input Memory FIFO. | Count |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Debug Mode Configuration Register IDE_MEM_CTRL | 22F | 00404470 | RW | 32 |
|  | Bit Value |
|  | 1 | 0 |
| Bit 0: External Control, INMEM A Count Enable | Enable | Idle |
| Bit 1: External Control, INMEM A Count Load | Load | Idle |
| Bit 2: External Control, INMEM B Count Enable | Enable | Idle |
| Bit 3: External Control, INMEM B Count Load | Load | Idle |
| Bit 4: External Control, DEBUGMEM A Count Enable | Enable | Idle |
| Bit 5: External Control, DEBUGMEM A Count Load | Load | Idle |
| Bit 6: External Control, DEBUGMEM B Count Enable | Enable | Idle |
| Bit 7: External Control, DEBUGMEM B Count Load | Load | Idle |
| Bit 8: External Control, CNFGRDBACK Write Count Enable | Enable | Idle |
| Bit 9: External Control, CNFGRDBACK Write Count Load | Load | Idle |
| Bit 10: External Control, CNFGRDBACK Delay Count Enable | Enable | Idle |
| Bit 11: External Control, CNFGRDBACK Delay Count Load | Load | Idle |
| Bits[17:12]: Test Bench Mode Select |
| INMEM->Formatters->EFB->Router->SDSP INMEM A Word Count: Number of Words to play out of the FIFO | 1 | 0 | 0 | 0 | 0 | 0 |
| INMEM->Formatters->EFB->Router->SDSP with retransmit INMEM A Word Count: Number of Words to play out of the FIFO INMEM B Word Count: Numbers of Retransmits | 1 | 0 | 0 | 1 | 0 | 0 |
| Bits[23:20]: ROL Test Block Control SETUP step OPERATION/RUN RESET/STOP Send Repeat Events - Bits[23:21] = 0x0; Set Bit 20 = 0x1; Clear Bit 20 Send Single Event – Bits[23:21] = 0x1; Set Bit 20 = 0x1; Clear Bit 20 Send TIM Events - Bits[23:21] = 0x2; Set Bit 20 = 0x1; Clear Bit 20 Send n Events - Bits[23:21] = 0x4; Set Bit 20 = 0x1; Clear Bit 20, Status=Bit15,IDE_MEM_STAT n = Bits[23:0], DBG_MEM_CTRL The setup step must be done before the ROL Start bit is set |
| Bit 20: Start ROL Test | Start | Idle |
| Bit 21: Send Single Event | Single | Repeat |
| Bit 22: Send ROL Test Block with L1A | Send | Idle |
| Bit 23: Enable ROL Trigger Counter (0x00404464 - DBG_MEM_CTRL: 22C) | Enable | Idle |
| Bits [29:24]: ROL Test Block Multiplier | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Debug Mode Status Register IDE_MEM_STAT | 230 | 00404474 | R | 32 |
|  | Bit Value |
|  | 1 | 0 |
| Bit 0: INMEM A Count Done | Done | Idle |
| Bit 1: INMEM B Count Done | Done | Idle |
| Bit 2: DEBUGMEM A Count Done | Done | Idle |
| Bit 3: DEBUGMEM B Count Done | Done | Idle |
| Bit 4: CNFGRDBACK Write Count Done | Done | Idle |
| Bit 5: CNFGRDBACK Delay Count Done | Done | Idle |
| Bit 6: Test Bench OP0 Status Bit | Done | Idle |
| Bit 7: Test Bench OP1 Status Bit | Done | Idle |
| Bit 8: Input Memory A FIFO Empty Flag | Empty | OK |
| Bit 9: Input Memory A FIFO Full Flag | Full | OK |
| Bit 10: Input Memory B FIFO Empty Flag | Empty | OK |
| Bit 11: Input Memory B FIFO Full Flag | Full | OK |
| Bit 12: NOT USED | Empty | OK |
| Bit 13: NOT USED | Full | OK |
| Bit 14: NOT USED | Empty | OK |
| Bit 15: ROL Test Triggers Active | Active | Idle |
| Bit 16: Internal TIM FIFO Empty Flag | Empty | OK |
| Bit 17: Internal TIM FIFO Full Flag | Full | OK |
| Bits [30:18]: Internal TIM FIFO Occupancy Count | Count |

## ROD Controller Internal TIM FIFO Register

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Internal TIM FIFO Input Register | ACCESS FIFO | 00404480 | RW | 8 |
|  | Bit Value |
| Bits[7:0]: Internal TIM Input Data A read to this register will read the data from the Internal TIM FIFO, and place the result at this memory location. A write to this register will data the value to the next available TIM FIFO Write Location. | Value |

## ROD Controller DSP Interrupt Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: MDSP to SDSP Interrupt, INTRPT_TO_SLV | 237 | 00404490 | RW | 4 |
| MDSP can issue interrupt to Ext pin 5 input of all Slaves | Bit Value |
|  | 1 | 0 |
| Bit 0: MDSP to SDSP0 | Int | Idle |
| Bit 1: MDSP to SDSP1 | Int | Idle |
| Bit 2: MDSP to SDSP2 | Int | Idle |
| Bit 3: MDSP to SDSP3 | Int | Idle |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: SDSP to MDSP Interrupt, INTRPT_FROM_SLV | 238 | 00404494 | RW | 4 |
| HPI Interrupt Out from each slave can be mapped to any MDSP External Interrupt input | Bit Value |
|  | 1 | 0 |
| Bit 0: SDSP0 to MDSP | Int | Idle |
| Bit 1: SDSP1 to MDSP | Int | Idle |
| Bit 2: SDSP2 to MDSP | Int | Idle |
| Bit 3: SDSP3 to MDSP | Int | Idle |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: VME Interrupt Test |  | 00404498 | RW | 7 |
| Signal used to test VME interrupts | Bit Value |
|  | 1 | 0 |
| Bit 0: Generate Test Pulse (Self Clearing) | Int | Idle |
| Bits[6:4]: IRQ value | Value |

## ROD Controller FE Occupancy Counter Control Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: FE Occupancy Counter Reset: Links (31:0) FE_OCC_CNTR_RESET(0) | 24F | 004044A0 | RW | 32 |
| Reset the FE Occupancy counters for Input Data Links 0 to 31. | Bit Value |
|  | 1 | 0 |
| Bits [31:0]: Resets for the FE Occupancy Counters Bit 0 resets the counter for Link 0, bit 1 for link 1, up to bit 31 for link 31. | Reset | Count |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: FE Occupancy Counter Reset: Links (63:32) FE_OCC_CNTR_RESET(1) | 250 | 004044A4 | RW | 32 |
| Reset the FE Occupancy counters for Input Data Links 32 to 63. | Bit Value |
|  | 1 | 0 |
| Bits [31:0]: Resets for the FE Occupancy Counters Bit 0 resets the counter for Link 32, bit 1 for link 33, up to bit 31 for link 63. | Reset | Count |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: FE Occupancy Counter Reset: Links (95:64) FE_OCC_CNTR_RESET(2) | 251 | 004044A8 | RW | 32 |
| Reset the FE Occupancy counters for Input Data Links 64 to 95. | Bit Value |
|  | 1 | 0 |
| Bits [31:0]: Resets for the FE Occupancy Counters Bit 0 resets the counter for Link 64, bit 1 for link 65, up to bit 31 for link 95. | Reset | Count |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: FE Occupancy Counter L1A Value (31:0) FE_OCC_CNTR_NUM_ACC(0) | 252 | 004044B0 | RW | 32 |
| This register stores the number of L1 Accepts to expect from each FE module and is used in the Pixel FE Occupancy Counters. | Bit Value |
| Bits [ 3: 0]: Num Accepts value for FE Module (0:0 F40¦F80¦F160) | Value |
| Bits [ 7: 4]: Num Accepts value for FE Module (0:1 F40¦F80) | Value |
| Bits [11: 8]: Num Accepts value for FE Module (0:2 F40) | Value |
| Bits [15:12]: Num Accepts value for FE Module (0:3 F40) | Value |
| Bits [19:16]: Num Accepts value for FE Module (1:0 F40¦F80¦F160) | Value |
| Bits [23:20]: Num Accepts value for FE Module (1:1 F40¦F80) | Value |
| Bits [27:24]: Num Accepts value for FE Module (1:2 F40) | Value |
| Bits [31:28]: Num Accepts value for FE Module (2:0 F40¦F80¦F1600) | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: FE Occupancy Counter L1A Value (31:0) FE_OCC_CNTR_NUM_ACC(1) | 253 | 004044B4 | RW | 32 |
| This register stores the number of L1 Accepts to expect from each FE module and is used in the Pixel FE Occupancy Counters. | Bit Value |
| Bits [ 3: 0]: Num Accepts value for FE Module (2:1 F40¦F80) | Value |
| Bits [ 7: 4]: Num Accepts value for FE Module (2:2 F40) | Value |
| Bits [11: 8]: Num Accepts value for FE Module (2:3 F40) | Value |
| Bits [15:12]: Num Accepts value for FE Module (3:0 F40¦F80¦F160) | Value |
| Bits [19:16]: Num Accepts value for FE Module (3:1 F40¦F80) | Value |
| Bits [23:20]: Num Accepts value for FE Module (4:0 F40¦F80¦F160) | Value |
| Bits [27:24]: Num Accepts value for FE Module (4:1 F40¦F80) | Value |
| Bits [31:28]: Num Accepts value for FE Module (4:2 F40) | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: FE Occupancy Counter L1A Value (31:0) FE_OCC_CNTR_NUM_ACC(2) | 254 | 004044B8 | RW | 32 |
| This register stores the number of L1 Accepts to expect from each FE module and is used in the Pixel FE Occupancy Counters. | Bit Value |
| Bits [ 3: 0]: Num Accepts value for FE Module (4:3 F40) | Value |
| Bits [ 7: 4]: Num Accepts value for FE Module (5:0 F40¦F80¦F160) | Value |
| Bits [11: 8]: Num Accepts value for FE Module (5:1 F40¦F80) | Value |
| Bits [15:12]: Num Accepts value for FE Module (5:2 F40) | Value |
| Bits [19:16]: Num Accepts value for FE Module (6:0 F40¦F80¦F160) | Value |
| Bits [23:20]: Num Accepts value for FE Module (6:1 F40¦F80) | Value |
| Bits [27:24]: Num Accepts value for FE Module (6:2 F40) | Value |
| Bits [31:28]: Num Accepts value for FE Module (6:3 F40) | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: FE Occupancy Counter L1A Value (31:0) FE_OCC_CNTR_NUM_ACC(3) | 255 | 004044BC | RW | 8 |
| This register stores the number of L1 Accepts to expect from each FE module and is used in the Pixel FE Occupancy Counters. | Bit Value |
| Bits [ 3:0]: Num Accepts value for FE Module (7:0 F40¦F80¦F160) | Value |
| Bits [ 7:4]: Num Accepts value for FE Module (7:1 F40¦F80) | Value |
| Bits [31:8]: Not Used | 0 |

## ROD Controller Internal Scan Calibration and Event ID Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Internal Scan NEvent Register: (23:0) DATA_LINK_MASK(0) | 256 | 004044C0 | RW | 15 |
| Number of events to issue to Pixel FE Modules. NEvent : Number of command sequences to issue in this mask stage | Bit Value |
| Bits [15: 0]: NEvent Value | Value |
| Bits [23:16]: Pre CAL Command Delay Value | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Internal Scan TrigDelay Register: (31:0) DATA_LINK_MASK(1) | 257 | 004044C4 | RW | 32 |
| Trigger Delay for Internal scans. TrigDelay0 : Delay between CAL and L1 commands in 100ns inc. for even groups TrigDelay1 : Delay between CAL and L1 commands in 100ns inc. for odd groups | Bit Value |
| Bits [15: 0]: TrigDelay0 | Value |
| Bits [31:16]: TrigDelay1 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Internal Scan Interval Register: (31:0) DATA_LINK_MASK(2) | 258 | 004044C8 | RW | 32 |
| Event Interval for Internal scans. Interval : Delay between successive cmd sequences in 25ns increment | Bit Value |
|  | 1 | 0 |
| Bits [31:0]: Event Interval | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Internal Scan Trigger Mode: (31:0) Trigger Mode Select Register/Active groups |  | 004044CC | RW | 32 |
| Trigger Mode for Internal scans. VALUE SCAN DESCRIPTION 0x1 Self Trigger up to 4 groups L1A only 0x2 Group synchronous scan >> CAL/TD0/L1A 0x3 Fixed interval scan >> CAL/TD0/L1A 0x4 Fully synchronous scan >> CAL/TD0/L1A 0x5 Cross-Talk 1 scan: Group(0) Default Mask >> CAL/TD0/L1A Group(0) Corrective >> PREDELAY/CAL/TD1/L1A 0x6 Cross-Talk 2 scan: Group(0) Default Mask >> CAL/TD0/L1A Group(0) Corrective >> PREDELAY/NOCAL/TD1/L1A NOCAL = “000000000” to match timing of Pixel CAL command | Bit Value |
|  | 1 | 0 |
| Bits [3:0]: Trigger Mode | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Calibration Event Type0 Register CAL_L1_TRIG_TYPE_0 | 23B | 004044D0 | RW | 10 |
| ATLAS and TIM Event Types to send to the EFB if DSP SP0 is used as the source for the Command Data Streams | Bit Value |
| Bits [7:0]: ATLAS Event Type for SP0 | Value |
| Bits [9:8]: TIM Event Type for SP0 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Calibration Event Type1 Register CAL_L1_TRIG_TYPE_1 | 23C | 004044D4 | RW | 10 |
| ATLAS and TIM Event Types to send to the EFB if DSP SP1 is used as the source for the Command Data Streams | Bit Value |
| Bits [7:0]: ATLAS Event Type for SP1 | Value |
| Bits [9:8]: TIM Event Type for SP1 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Internal Scan Status |  | 004044D8 | R | 1 |
|  | Bit Value |
| Bit [0]: Scan Done | Done | Idle |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Calibration L1ID SP0 Register CAL_L1_ID_0 | 23D | 004044E0 | R | 24 |
| If the ROD is configured for calibration using MDSP SP0 as a trigger source, then the value of this register is the L1ID sent to Event Fragment Builder. In this mode the user can choose to set the register prior to each trigger orf allow a counter to increment the value for each trigger detected. If the ROD is configured in Internal Calibration mode, then the value in this register will increment for each trigger detected. If the ROD is configured in Physics Data Taking mode and the Diagnostic Event Counter bit is set then this register will count L1 triggers received from the TTC system. | Bit Value |
| Bits [23:0]: L1ID for SP0 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Calibration L1ID SP1 Register CAL_L1_ID_1 | 23E | 004044E4 | R | 24 |
| If the ROD is configured for calibration using MDSP SP1 as a trigger source, then the value of this register is the L1ID sent to Event Fragment Builder. In this mode the user can choose to set the register prior to each trigger orf allow a counter to increment the value for each trigger detected. If the ROD is configured in Internal Calibration mode, then the value in this register will increment for each trigger detected. If the ROD is configured in Physics Data Taking mode and the Diagnostic Event Counter bit is set then this register will count L1 triggers received from the TTC system while ROD Busy is asserted. | Bit Value |
| Bits [23:0]: L1ID for SP1 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Calibration BCID Register CAL_BCID | 23F | 004044E8 | RW | 28 |
| BCID values to send to the EFB if DSP SP0 or SP1 are used as the sources for the Command Data Streams | Bit Value |
| Bits [11: 0]: BCID for SP0 | Value |
| Bits [27:16]: BCID for SP1 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Event L1ID |  | 004044EC | RW | 23 |
| Latched value of the last L1ID sent to the EFB | Bit Value |
| Bits [23: 0]: L1ID | Value |

## ROD Controller Fixed Frequency Trigger Veto Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Fixed Frequency Trigger Veto Command FFTV_CMND |  | 004044F0 | RW | 8 |
|  | Bit Value |
|  | 1 | 0 |
| Bit [0] : Emergency Clear | Clear | Idle |
| Bit [1] : Count Clear | Clear | Idle |
| Bit [2] : ID Clear | Clear | Idle |
| Bit [3] : Not Used |  |  |
| Bits [7:4] : FFTV Match Level | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Fixed Frequency Trigger Veto Busy Counter FFTV_BUSY_COUNT |  | 004044F4 | R | 23 |
|  | Bit Value |
|  | 1 | 0 |
| Bits [19:0] : Busy Time Counter | Value |
| Bit [20] : Busy Time Counter Rollover (Latching) | Over | Idle |
| Bit [21] : Busy Active | Busy | Idle |
| Bit [22] : Busy Active (Latching) | Busy | Idle |
| Bit [23] : Emergency Active | Emerg | Idle |
| Bit [24] : Emergency Active (Latching) | Emerg | Idle |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Controller: Fixed Frequency Trigger Veto Status FFTV_STAT |  | 004044F8 | R | 21 |
|  | Bit Value |
|  | 1 | 0 |
| Bits [11:0] : ID Counter | Value |
| Bit [12] : ID Counter Rollover (Latching) | Over | Idle |
| Bit [13] : Not Used | Over | Idle |
| Bit [14] : Not Used | Over | Idle |
| Bit [15] : Not Used | Over | Idle |
| Bits [19:16] : FFTV Match Level Readback | Value |

## ROD Controller FE Occupancy Counters

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| FE Occupancy Counters: Links ( 7: 0), FE_OCC_CNTR(0) | 259 | 00404500 | R | 32 |
| FE Occupancy Counters: Links (15: 8), FE_OCC_CNTR(1) | 25A | 00404504 | R | 32 |
| FE Occupancy Counters: Links (23:16), FE_OCC_CNTR(2) | 25B | 00404508 | R | 32 |
| FE Occupancy Counters: Links (31:24), FE_OCC_CNTR(3) | 25C | 0040450C | R | 32 |
| FE Occupancy Counters: Links (39:32), FE_OCC_CNTR(4) | 25D | 00404510 | R | 32 |
| FE Occupancy Counters: Links (47:40), FE_OCC_CNTR(5) | 25E | 00404514 | R | 32 |
| FE Occupancy Counters: Links (55:48), FE_OCC_CNTR(6) | 25F | 00404518 | R | 32 |
| FE Occupancy Counters: Links (63:56), FE_OCC_CNTR(7) | 260 | 0040451C | R | 32 |
| FE Occupancy Counters: Links (71:64), FE_OCC_CNTR(8) |  | 00404520 | R | 32 |
| FE Occupancy Counters: Links (79:72), FE_OCC_CNTR(9) |  | 00404524 | R | 32 |
| FE Occupancy Counters: Links (87:80), FE_OCC_CNTR(10) |  | 00404528 | R | 32 |
| FE Occupancy Counters: Links (95:88), FE_OCC_CNTR(11) |  | 0040452C | R | 32 |
|  | Bit Value |
| Bits[ 3: 0]: FE OCC Counter Links 0, 8,16,24,32,40,48,56,64,72,80,88 | Count |
| Bits[ 7: 4]: FE OCC Counter Links 1, 9,17,25,33,41,49,57,65,73,81,89 | Count |
| Bits[11: 8]: FE OCC Counter Links 2,10,18,26,34,42,50,58,66,74,82,90 | Count |
| Bits[15:12]: FE OCC Counter Links 3,11,19,27,35,43,51,59,67,75,83,91 | Count |
| Bits[19:16]: FE OCC Counter Links 4,12,20,28,36,44,52,60,68,76,84,92 | Count |
| Bits[23:20]: FE OCC Counter Links 5,13,21,29,37,45,53,61,69,77,85,93 | Count |
| Bits[27:24]: FE OCC Counter Links 6,14,22,30,38,46,54,62,70,78,86,94 | Count |
| Bits[32:28]: FE OCC Counter Links 7,15,23,31,39,47,55,63,71,79,87,95 | Count |

## ROD Controller Internal Scan Group to Link Map

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| FE Occupancy Counters: Group to Link Map |  | 00404530 | RW | 32 |
| Highest link in Engine 0 ( (12*n + 0, 1, 2, 3) n=Formatter Number Highest link in Engine 1 ( ((48+(12*n) + 0, 1, 2, 3) | Bit Value |
| Bits[ 5: 0]: Group 0 Highest Link in Engine 0 | 0x0 to 0x2F |
| Bits[13: 8]: Group 0 Highest Link in Engine 1 | 0x0 to 0x2F |
| Bits[21:16]: Group 1 Highest Link in Engine 0 | 0x0 to 0x2F |
| Bits[29:24]: Group 1 Highest Link in Engine 1 | 0x0 to 0x2F |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| FE Occupancy Counters: Group to Link Map |  | 00404534 | RW | 32 |
| Highest link in Engine 0 ( (12*n + 0, 1, 2, 3) n=Formatter Number Highest link in Engine 1 ( ((48+(12*n) + 0, 1, 2, 3) | Bit Value |
| Bits[ 5: 0]: Group 2 Highest Link in Engine 0 | 0x0 to 0x2F |
| Bits[13: 8]: Group 2 Highest Link in Engine 1 | 0x0 to 0x2F |
| Bits[21:16]: Group 3 Highest Link in Engine 0 | 0x0 to 0x2F |
| Bits[29:24]: Group 3 Highest Link in Engine 1 | 0x0 to 0x2F |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| FE Occupancy Counters: Internal Scan Group Enable |  | 00404540 | RW | 8 |
|  | Bit Value |
| Bit[0]: Group 0 Enable | Enable | Disable |
| Bit[1]: Group 1 Enable | Enable | Disable |
| Bit[2]: Group 2 Enable | Enable | Disable |
| Bit[3]: Group 3 Enable | Enable | Disable |
| Bit[4]: Group 4 Enable | Enable | Disable |
| Bit[5]: Group 5 Enable | Enable | Disable |
| Bit[6]: Group 6 Enable | Enable | Disable |
| Bit[7]: Group 7 Enable | Enable | Disable |

## ROD Controller FE Command Mask LUT

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| FE Command Mask, SP0, Mask 0, Links (31:0): CMND_MASK_LUT(0,0,0) | 398 | 00404600 | RW | 32 |
| FE Command Mask, SP0, Mask 0, Links (47:32): CMND_MASK_LUT(0,0,1) | 399 | 00404604 | RW | 16 |
| FE Command Mask, SP1, Mask 0, Links (31: 0): CMND_MASK_LUT(0,1,0) | 39A | 00404608 | RW | 32 |
| FE Command Mask, SP1, Mask 0, Links (47:32): CMND_MASK_LUT(0,1,1) | 39B | 0040460C | RW | 16 |
| FE Command Mask, SP0, Mask 1, Links (31:0): CMND_MASK_LUT(1,0,0) | 39C | 00404610 | RW | 32 |
| FE Command Mask, SP0, Mask 1, Links (47:32): CMND_MASK_LUT(1,0,1) | 39D | 00404614 | RW | 16 |
| FE Command Mask, SP1, Mask 1, Links (31: 0): CMND_MASK_LUT(1,1,0) | 39E | 00404618 | RW | 32 |
| FE Command Mask, SP1, Mask 1, Links (47:32): CMND_MASK_LUT(1,1,1) | 39F | 0040461C | RW | 16 |
| FE Command Mask, SP0, Mask 2, Links (31:0): CMND_MASK_LUT(2,0,0) | 3A0 | 00404620 | RW | 32 |
| FE Command Mask, SP0, Mask 2, Links (47:32): CMND_MASK_LUT(2,0,1) | 3A1 | 00404624 | RW | 16 |
| FE Command Mask, SP1, Mask 2, Links (31: 0): CMND_MASK_LUT(2,1,0) | 3A2 | 00404628 | RW | 32 |
| FE Command Mask, SP1, Mask 2, Links (47:32): CMND_MASK_LUT(2,1,1) | 3A3 | 0040462C | RW | 16 |
| FE Command Mask, SP0, Mask 3, Links (31:0): CMND_MASK_LUT(3,0,0) | 3A4 | 00404630 | RW | 32 |
| FE Command Mask, SP0, Mask 3, Links (47:32): CMND_MASK_LUT(3,0,1) | 3A5 | 00404634 | RW | 16 |
| FE Command Mask, SP1, Mask 3, Links (31: 0): CMND_MASK_LUT(3,1,0) | 3A6 | 00404638 | RW | 32 |
| FE Command Mask, SP1, Mask 3, Links (47:32): CMND_MASK_LUT(3,1,1) | 3A7 | 0040463C | RW | 16 |
| FE Command Mask, SP0, Mask 4, Links (31:0): CMND_MASK_LUT(4,0,0) | 3A8 | 00404640 | RW | 32 |
| FE Command Mask, SP0, Mask 4, Links (47:32): CMND_MASK_LUT(4,0,1) | 3A9 | 00404644 | RW | 16 |
| FE Command Mask, SP1, Mask 4, Links (31: 0): CMND_MASK_LUT(4,1,0) | 3AA | 00404648 | RW | 32 |
| FE Command Mask, SP1, Mask 4, Links (47:32): CMND_MASK_LUT(4,1,1) | 3AB | 0040464C | RW | 16 |
| FE Command Mask, SP0, Mask 5, Links (31:0): CMND_MASK_LUT(5,0,0) | 3AC | 00404650 | RW | 32 |
| FE Command Mask, SP0, Mask 5, Links (47:32): CMND_MASK_LUT(5,0,1) | 3AD | 00404654 | RW | 16 |
| FE Command Mask, SP1, Mask 5, Links (31: 0): CMND_MASK_LUT(5,1,0) | 3AE | 00404658 | RW | 32 |
| FE Command Mask, SP1, Mask 5, Links (47:32): CMND_MASK_LUT(5,1,1) | 3AF | 0040465C | RW | 16 |
| FE Command Mask, SP0, Mask 6, Links (31:0): CMND_MASK_LUT(6,0,0) | 3B0 | 00404660 | RW | 32 |
| FE Command Mask, SP0, Mask 6, Links (47:32): CMND_MASK_LUT(6,0,1) | 3B1 | 00404664 | RW | 16 |
| FE Command Mask, SP1, Mask 6, Links (31: 0): CMND_MASK_LUT(6,1,0) | 3B2 | 00404668 | RW | 32 |
| FE Command Mask, SP1, Mask 6, Links (47:32): CMND_MASK_LUT(6,1,1) | 3B3 | 0040466C | RW | 16 |
| FE Command Mask, SP0, Mask 7, Links (31:0): CMND_MASK_LUT(7,0,0) | 3B4 | 00404670 | RW | 32 |
| FE Command Mask, SP0, Mask 7, Links (47:32): CMND_MASK_LUT(7,0,1) | 3B5 | 00404674 | RW | 16 |
| FE Command Mask, SP1, Mask 7, Links (31: 0): CMND_MASK_LUT(7,1,0) | 3B6 | 00404678 | RW | 32 |
| FE Command Mask, SP1, Mask 7, Links (47:32): CMND_MASK_LUT(7,1,1) | 3B7 | 0040467C | RW | 16 |
| Stores the values used by the FE Command Processor to send or mask commands to the FE Modules. | Bit Value |
| Bits[31: 0]: Mask Values for output command links | Value |

## ROD Controller Default Event Type Register

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Default Event Type (7:0), DFLT_ROD_EVT_TYPE | 239 | 00404700 | RW | 7 |
| This Register stores the value of the ROD Specific Event Type used when a Normal or SP0 L1A Trigger is detected | Bit Value |
| Bits [7: 0]: Default ROD Event Type | Value |

## ROD Controller Default Dynamic Mask LUTs

The EFB Dynamic Mask Bits, default and corrective, are stored in Look-Up Tables (LUTs) that are implemented using internal block RAM blocks in the ROD Controller FPGA (RCF).  When the RCF is configured (loading of configuration data from the Program Reset Manager FPGA or a hardware reset), the values in the RAM blocks are initialized to 0.  A software reset to the ROD does not clear the previous values stored in the EFB DM LUTs.  After a soft reset to the ROD the EFB dynamic mask bits must be set to the desired values prior to a take data command.

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB Default Dynamic Mask: Links ( 7: 0), DM_DFLT_LUT(0) | 270 | 00404704 | RW | 16 |
| EFB Default Dynamic Mask: Links (15: 8), DM_DFLT_LUT(1) | 271 | 00404708 | RW | 16 |
| EFB Default Dynamic Mask: Links (23:16), DM_DFLT_LUT(2) | 272 | 0040470C | RW | 16 |
| EFB Default Dynamic Mask: Links (31:24), DM_DFLT_LUT(3) | 273 | 00404710 | RW | 16 |
| EFB Default Dynamic Mask: Links (39:32), DM_DFLT_LUT(4) | 274 | 00404714 | RW | 16 |
| EFB Default Dynamic Mask: Links (47:40), DM_DFLT_LUT(5) | 275 | 00404718 | RW | 16 |
| EFB Default Dynamic Mask: Links (55:48), DM_DFLT_LUT(6) | 276 | 0040471C | RW | 16 |
| EFB Default Dynamic Mask: Links (63:56), DM_DFLT_LUT(7) | 277 | 00404720 | RW | 16 |
| EFB Default Dynamic Mask: Links (71:64), DM_DFLT_LUT(8) | 278 | 00404724 | RW | 16 |
| EFB Default Dynamic Mask: Links (79:72), DM_DFLT_LUT(9) | 279 | 00404728 | RW | 16 |
| EFB Default Dynamic Mask: Links (87:80), DM_DFLT_LUT(10) | 27A | 0040472C | RW | 16 |
| EFB Default Dynamic Mask: Links (95:88), DM_DFLT_LUT(11) | 27B | 00404730 | RW | 16 |
| This Register stores the mask values used when a Normal or SP0 L1A Trigger is detected. Mask = 00: L1ID OK, No Modification Mask = 01: Increment L1ID for this Link by 1 Mask = 10: Decrement L1ID for this Link by 1 | Bit Value |
| Bits[ 1: 0]: Default Mask, Links 0, 8,16,24,32,40,48,56,64,72,80,88 | Mask |
| Bits[ 3: 2]: Default Mask, Links 1, 9,17,25,33,41,49,57,65,73,81,89 | Mask |
| Bits[ 5: 4]: Default Mask, Links 2,10,18,26,34,42,50,58,66,74,82,90 | Mask |
| Bits[ 7: 6]: Default Mask, Links 3,11,19,27,35,43,51,59,67,75,83,91 | Mask |
| Bits[ 9: 8]: Default Mask, Links 4,12,20,28,36,44,52,60,68,76,84,92 | Mask |
| Bits[11:10]: Default Mask, Links 5,13,21,29,37,45,53,61,69,77,85,93 | Mask |
| Bits[13:12]: Default Mask, Links 6,14,22,30,38,46,54,62,70,78,86,94 | Mask |
| Bits[15:14]: Default Mask, Links 7,15,23,31,39,47,55,63,71,79,87,95 | Mask |

## ROD Controller Corrective Event Type Register

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| ROD Corrective Event Type (7:0), CRTV_ROD_EVT_TYPE | 23A | 00404740 | RW | 7 |
| This Register stores the value of the ROD Specific Event Type used when a Corrective or SP1 L1A Trigger is detected | Bit Value |
| Bits [7: 0]: Corrective ROD Event Type | Value |

## ROD Controller Corrective Dynamic Mask LUTs

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| EFB Corrective Dynamic Mask: Links( 7: 0), DM_CRTV_LUT(0) | 27C | 00404744 | RW | 16 |
| EFB Corrective Dynamic Mask: Links(15: 8), DM_CRTV_LUT(1) | 27D | 00404748 | RW | 16 |
| EFB Corrective Dynamic Mask: Links(23:16), DM_CRTV_LUT(2) | 27E | 0040474C | RW | 16 |
| EFB Corrective Dynamic Mask: Links(31:24), DM_CRTV_LUT(3) | 27F | 00404750 | RW | 16 |
| EFB Corrective Dynamic Mask: Links(39:32), DM_CRTV_LUT(4) | 280 | 00404754 | RW | 16 |
| EFB Corrective Dynamic Mask: Links(47:40), DM_CRTV_LUT(5) | 281 | 00404758 | RW | 16 |
| EFB Corrective Dynamic Mask: Links(55:48), DM_CRTV_LUT(6) | 282 | 0040475C | RW | 16 |
| EFB Corrective Dynamic Mask: Links(63:56), DM_CRTV_LUT(7) | 283 | 00404760 | RW | 16 |
| EFB Corrective Dynamic Mask: Links(71:64), DM_CRTV_LUT(8) | 284 | 00404764 | RW | 16 |
| EFB Corrective Dynamic Mask: Links(79:72), DM_CRTV_LUT(9) | 285 | 00404768 | RW | 16 |
| EFB Corrective Dynamic Mask: Links(87:80), DM_CRTV_LUT(10) | 286 | 0040476C | RW | 16 |
| EFB Corrective Dynamic Mask: Links(95:88), DM_CRTV_LUT(11) | 287 | 00404770 | RW | 16 |
| This Register stores the mask values used when a Corrective or SP1 L1A Trigger is detected. Mask = 00: L1ID OK, No Modification Mask = 01: Increment L1ID for this Link by 1 Mask = 10: Decrement L1ID for this Link by 1 | Bit Value |
| Bits[ 1: 0]: Corrective Mask Links 0, 8,16,24,32,40,48,56,64,72,80,88 | Mask |
| Bits[ 3: 2]: Corrective Mask Links 1, 9,17,25,33,41,49,57,65,73,81,89 | Mask |
| Bits[ 5: 4]: Corrective Mask Links 2,10,18,26,34,42,50,58,66,74,82,90 | Mask |
| Bits[ 7: 6]: Corrective Mask Links 3,11,19,27,35,43,51,59,67,75,83,91 | Mask |
| Bits[ 9: 8]: Corrective Mask Links 4,12,20,28,36,44,52,60,68,76,84,92 | Mask |
| Bits[11:10]: Corrective Mask Links 5,13,21,29,37,45,53,61,69,77,85,93 | Mask |
| Bits[13:12]: Corrective Mask Links 6,14,22,30,38,46,54,62,70,78,86,94 | Mask |
| Bits[15:14]: Corrective Mask Links 7,15,23,31,39,47,55,63,71,79,87,95 | Mask |

## ROD Controller Corrected Events FIFO

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Corrected Event FIFO, CORRECTED_EVENTS_FIFO | 288 | 00404780 | RW | 16 |
|  | Bit Value |
| Bits[15: 0]: Corrective Events FIFO Data | Value |

## ROD Controller Formatter Mode Bits LUT

The Formatter Dynamic Mode Bits, default and corrective, are stored in Look-Up Tables (LUTs) that are implemented using internal block RAM blocks in the ROD Controller FPGA (RCF).  When the RCF is configured (loading of configuration data from the Program Reset Manager FPGA or a hardware reset), the values in the RAM blocks are initialized to 0.  A software reset to the ROD does not clear the previous values stored in the FMB LUT.  After a soft reset to the ROD the dynamic mode bits must be set to the desired values prior to a take data command.

| MB1 | MB0 | Formatter Read Out Mode Bits Definitions |
| --- | --- | --- |
| 0 | 0 | Play 1st event from Link FIFO. Normal data flow from Formatter to EFB. |
| 0 | 1 | Mask this link for 1 event. In this mode, the formatter will dump one event from the link FIFO. |
| 1 | 0 | Skip read out of this link for 1 event for re-synchronization. |
| 1 | 1 | Read out 1st event from FIFO and dump it on the floor, play the 2nd event to the EFB. |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Default MB0, Links (11: 0), Mask0: RMB_DFLT_LUT(0,0,0) | 298 | 00404800 | RW | 12 |
| Default MB0, Links (23:12), Mask0: RMB_DFLT_LUT(0,1,0) | 29A | 00404808 | RW | 12 |
| Default MB0, Links (35:24), Mask0: RMB_DFLT_LUT(0,2,0) | 29C | 00404810 | RW | 12 |
| Default MB0, Links (47:36), Mask0: RMB_DFLT_LUT(0,3,0) | 29E | 00404818 | RW | 12 |
| Default MB0, Links (59:48), Mask0: RMB_DFLT_LUT(0,4,0) | 2A0 | 00404820 | RW | 12 |
| Default MB0, Links (71:60), Mask0: RMB_DFLT_LUT(0,5,0) | 2A2 | 00404828 | RW | 12 |
| Default MB0, Links (83:72), Mask0: RMB_DFLT_LUT(0,6,0) | 2A4 | 00404830 | RW | 12 |
| Default MB0, Links (95:84), Mask0: RMB_DFLT_LUT(0,7,0) | 2A6 | 00404838 | RW | 12 |
| This Register stores the values of Mode Bit 0 (MB0) used when a normal or SP0 Trigger is detected. | Bit Value |
| Bit 0: Formatter Mode Bits: Default MB0, Links 0,12,24,36,48,60,72,84 | MB0 |  |
| Bit 1: Formatter Mode Bits: Default MB0, Links 1,13,25,37,49,61,73,85 | MB0 |  |
| Bit 2: Formatter Mode Bits: Default MB0, Links 2,14,26,38,50,62,74,86 | MB0 |  |
| Bit 3: Formatter Mode Bits: Default MB0, Links 3,15,27,39,51,63,75,87 | MB0 |  |
| Bit 4: Formatter Mode Bits: Default MB0, Links 4,16,28,40,52,64,76,88 | MB0 |  |
| Bit 5: Formatter Mode Bits: Default MB0, Links 5,17,29,41,53,65,77,89 | MB0 |  |
| Bit 6: Formatter Mode Bits: Default MB0, Links 6,18,30,42,54,66,78,90 | MB0 |  |
| Bit 7: Formatter Mode Bits: Default MB0, Links 7,19,31,43,55,67,79,91 | MB0 |  |
| Bit 8: Formatter Mode Bits: Default MB0, Links 8,20,32,44,56,68,80,92 | MB0 |  |
| Bit 9: Formatter Mode Bits: Default MB0, Links 9,21,33,45,57,69,81,93 | MB0 |  |
| Bit 10: Formatter Mode Bits: Default MB0, Links 10,22,34,46,58,70,82,94 | MB0 |  |
| Bit 11: Formatter Mode Bits: Default MB0, Links 11,23,35,47,59,71,83,95 | MB0 |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Default MB1, Links (11: 0), Mask0: RMB_DFLT_LUT(0,0,1) | 299 | 00404804 | RW | 12 |
| Default MB1, Links (23:12), Mask0: RMB_DFLT_LUT(0,1,1) | 29B | 0040480C | RW | 12 |
| Default MB1, Links (35:24), Mask0: RMB_DFLT_LUT(0,2,1) | 29D | 00404814 | RW | 12 |
| Default MB1, Links (47:36), Mask0: RMB_DFLT_LUT(0,3,1) | 29F | 0040481C | RW | 12 |
| Default MB1, Links (59:48), Mask0: RMB_DFLT_LUT(0,4,1) | 2A1 | 00404824 | RW | 12 |
| Default MB1, Links (71:60), Mask0: RMB_DFLT_LUT(0,5,1) | 2A3 | 0040482C | RW | 12 |
| Default MB1, Links (83:72), Mask0: RMB_DFLT_LUT(0,6,1) | 2A5 | 00404834 | RW | 12 |
| Default MB1, Links (95:84), Mask0: RMB_DFLT_LUT(0,7,1) | 2A7 | 0040483C | RW | 12 |
| This Register stores the values of Mode Bit 1 (MB1) used when a normal or SP0 Trigger is detected. | Bit Value |
| Bit 0: Formatter Mode Bits: Default MB1, Links 0,12,24,36,48,60,72,84 | MB1 |  |
| Bit 1: Formatter Mode Bits: Default MB1, Links 1,13,25,37,49,61,73,85 | MB1 |  |
| Bit 2: Formatter Mode Bits: Default MB1, Links 2,14,26,38,50,62,74,86 | MB1 |  |
| Bit 3: Formatter Mode Bits: Default MB1, Links 3,15,27,39,51,63,75,87 | MB1 |  |
| Bit 4: Formatter Mode Bits: Default MB1, Links 4,16,28,40,52,64,76,88 | MB1 |  |
| Bit 5: Formatter Mode Bits: Default MB1, Links 5,17,29,41,53,65,77,89 | MB1 |  |
| Bit 6: Formatter Mode Bits: Default MB1, Links 6,18,30,42,54,66,78,90 | MB1 |  |
| Bit 7: Formatter Mode Bits: Default MB1, Links 7,19,31,43,55,67,79,91 | MB1 |  |
| Bit 8: Formatter Mode Bits: Default MB1, Links 8,20,32,44,56,68,80,92 | MB1 |  |
| Bit 9: Formatter Mode Bits: Default MB1, Links 9,21,33,45,57,69,81,93 | MB1 |  |
| Bit 10: Formatter Mode Bits: Default MB1, Links 10,22,34,46,58,70,82,94 | MB1 |  |
| Bit 11: Formatter Mode Bits: Default MB1, Links 11,23,35,47,59,71,83,95 | MB1 |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Corrective MB0, Links (11: 0), Mask0: RMB_CRTV_LUT(0,0,0) | 318 | 00404840 | RW | 12 |
| Corrective MB0, Links (23:12), Mask0: RMB_CRTV_LUT(0,1,0) | 31A | 00404848 | RW | 12 |
| Corrective MB0, Links (35:24), Mask0: RMB_CRTV_LUT(0,2,0) | 31C | 00404850 | RW | 12 |
| Corrective MB0, Links (47:36), Mask0: RMB_CRTV_LUT(0,3,0) | 31E | 00404858 | RW | 12 |
| Corrective MB0, Links (59:48), Mask0: RMB_CRTV_LUT(0,4,0) | 320 | 00404860 | RW | 12 |
| Corrective MB0, Links (71:60), Mask0: RMB_CRTV_LUT(0,5,0) | 322 | 00404868 | RW | 12 |
| Corrective MB0, Links (83:72), Mask0: RMB_CRTV_LUT(0,6,0) | 324 | 00404870 | RW | 12 |
| Corrective MB0, Links (95:84), Mask0: RMB_CRTV_LUT(0,7,0) | 326 | 00404878 | RW | 12 |
| This Register stores the values of Mode Bit 0 (MB0) used when a Corrective or SP1 Trigger is detected. | Bit Value |
| Bit 0: Formatter Mode Bits: Corrective MB0, Links 0,12,24,36,48,60,72,84 | MB0 |  |
| Bit 1: Formatter Mode Bits: Corrective MB0, Links 1,13,25,37,49,61,73,85 | MB0 |  |
| Bit 2: Formatter Mode Bits: Corrective MB0, Links 2,14,26,38,50,62,74,86 | MB0 |  |
| Bit 3: Formatter Mode Bits: Corrective MB0, Links 3,15,27,39,51,63,75,87 | MB0 |  |
| Bit 4: Formatter Mode Bits: Corrective MB0, Links 4,16,28,40,52,64,76,88 | MB0 |  |
| Bit 5: Formatter Mode Bits: Corrective MB0, Links 5,17,29,41,53,65,77,89 | MB0 |  |
| Bit 6: Formatter Mode Bits: Corrective MB0, Links 6,18,30,42,54,66,78,90 | MB0 |  |
| Bit 7: Formatter Mode Bits: Corrective MB0, Links 7,19,31,43,55,67,79,91 | MB0 |  |
| Bit 8: Formatter Mode Bits: Corrective MB0, Links 8,20,32,44,56,68,80,92 | MB0 |  |
| Bit 9: Formatter Mode Bits: Corrective MB0, Links 9,21,33,45,57,69,81,93 | MB0 |  |
| Bit 10: Formatter Mode Bits: Corrective MB0, Links 10,22,34,46,58,70,82,94 | MB0 |  |
| Bit 11: Formatter Mode Bits: Corrective MB0, Links 11,23,35,47,59,71,83,95 | MB0 |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Corrective MB1, Links (11: 0), Mask0: RMB_CRTV_LUT(0,0,1) | 319 | 00404844 | RW | 12 |
| Corrective MB1, Links (23:12), Mask0: RMB_CRTV_LUT(0,1,1) | 31B | 0040484C | RW | 12 |
| Corrective MB1, Links (35:24), Mask0: RMB_CRTV_LUT(0,2,1) | 31D | 00404854 | RW | 12 |
| Corrective MB1, Links (47:36), Mask0: RMB_CRTV_LUT(0,3,1) | 31F | 0040485C | RW | 12 |
| Corrective MB1, Links (59:48), Mask0: RMB_CRTV_LUT(0,4,1) | 321 | 00404864 | RW | 12 |
| Corrective MB1, Links (71:60), Mask0: RMB_CRTV_LUT(0,5,1) | 323 | 0040486C | RW | 12 |
| Corrective MB1, Links (83:72), Mask0: RMB_CRTV_LUT(0,6,1) | 325 | 00404874 | RW | 12 |
| Corrective MB1, Links (95:84), Mask0: RMB_CRTV_LUT(0,7,1) | 327 | 0040487C | RW | 12 |
| This Register stores the values of Mode Bit 1 (MB1) used when a Corrective or SP1 Trigger is detected. | Bit Value |
| Bit 0: Formatter Mode Bits: Corrective MB1, Links 0,12,24,36,48,60,72,84 | MB1 |  |
| Bit 1: Formatter Mode Bits: Corrective MB1, Links 1,13,25,37,49,61,73,85 | MB1 |  |
| Bit 2: Formatter Mode Bits: Corrective MB1, Links 2,14,26,38,50,62,74,86 | MB1 |  |
| Bit 3: Formatter Mode Bits: Corrective MB1, Links 3,15,27,39,51,63,75,87 | MB1 |  |
| Bit 4: Formatter Mode Bits: Corrective MB1, Links 4,16,28,40,52,64,76,88 | MB1 |  |
| Bit 5: Formatter Mode Bits: Corrective MB1, Links 5,17,29,41,53,65,77,89 | MB1 |  |
| Bit 6: Formatter Mode Bits: Corrective MB1, Links 6,18,30,42,54,66,78,90 | MB1 |  |
| Bit 7: Formatter Mode Bits: Corrective MB1, Links 7,19,31,43,55,67,79,91 | MB1 |  |
| Bit 8: Formatter Mode Bits: Corrective MB1, Links 8,20,32,44,56,68,80,92 | MB1 |  |
| Bit 9: Formatter Mode Bits: Corrective MB1, Links 9,21,33,45,57,69,81,93 | MB1 |  |
| Bit 10: Formatter Mode Bits: Corrective MB1, Links 10,22,34,46,58,70,82,94 | MB1 |  |
| Bit 11: Formatter Mode Bits: Corrective MB1, Links 11,23,35,47,59,71,83,95 | MB1 |  |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Default MB0, Links (11: 0), Mask1: RMB_DFLT_LUT(1,0,0) | 2A8 | 00404880 | RW | 12 |
| Default MB1, Links (11: 0), Mask1: RMB_DFLT_LUT(1,0,1) | 2A9 | 00404884 | RW | 12 |
| Default MB0, Links (23:12), Mask1: RMB_DFLT_LUT(1,1,0) | 2AA | 00404888 | RW | 12 |
| Default MB1, Links (23:12), Mask1: RMB_DFLT_LUT(1,1,1) | 2AB | 0040488C | RW | 12 |
| Default MB0, Links (35:24), Mask1: RMB_DFLT_LUT(1,2,0) | 2AC | 00404890 | RW | 12 |
| Default MB1, Links (35:24), Mask1: RMB_DFLT_LUT(1,2,1) | 2AD | 00404894 | RW | 12 |
| Default MB0, Links (47:36), Mask1: RMB_DFLT_LUT(1,3,0) | 2AE | 00404898 | RW | 12 |
| Default MB1, Links (47:36), Mask1: RMB_DFLT_LUT(1,3,1) | 2AF | 0040489C | RW | 12 |
| Default MB0, Links (59:48), Mask1: RMB_DFLT_LUT(1,4,0) | 2B0 | 004048A0 | RW | 12 |
| Default MB1, Links (59:48), Mask1: RMB_DFLT_LUT(1,4,1) | 2B1 | 004048A4 | RW | 12 |
| Default MB0, Links (71:60), Mask1: RMB_DFLT_LUT(1,5,0) | 2B2 | 004048A8 | RW | 12 |
| Default MB1, Links (71:60), Mask1: RMB_DFLT_LUT(1,5,1) | 2B3 | 004048AC | RW | 12 |
| Default MB0, Links (83:72), Mask1: RMB_DFLT_LUT(1,6,0) | 2B4 | 004048B0 | RW | 12 |
| Default MB1, Links (83:72), Mask1: RMB_DFLT_LUT(1,6,1) | 2B5 | 004048B4 | RW | 12 |
| Default MB0, Links (95:84), Mask1: RMB_DFLT_LUT(1,7,0) | 2B6 | 004048B8 | RW | 12 |
| Default MB1, Links (95:84), Mask1: RMB_DFLT_LUT(1,7,1) | 2B7 | 004048BC | RW | 12 |
| Corrective MB0, Links (11: 0), Mask1: RMB_CRTV_LUT(1,0,0) | 328 | 004048C0 | RW | 12 |
| Corrective MB1, Links (11: 0), Mask1: RMB_CRTV_LUT(1,0,1) | 329 | 004048C4 | RW | 12 |
| Corrective MB0, Links (23:12), Mask1: RMB_CRTV_LUT(1,1,0) | 32A | 004048C8 | RW | 12 |
| Corrective MB1, Links (23:12), Mask1: RMB_CRTV_LUT(1,1,1) | 32B | 004048CC | RW | 12 |
| Corrective MB0, Links (35:24), Mask1: RMB_CRTV_LUT(1,2,0) | 32C | 004048D0 | RW | 12 |
| Corrective MB1, Links (35:24), Mask1: RMB_CRTV_LUT(1,2,1) | 32D | 004048D4 | RW | 12 |
| Corrective MB0, Links (47:36), Mask1: RMB_CRTV_LUT(1,3,0) | 32E | 004048D8 | RW | 12 |
| Corrective MB1, Links (47:36), Mask1: RMB_CRTV_LUT(1,3,1) | 32F | 004048DC | RW | 12 |
| Corrective MB0, Links (59:48), Mask1: RMB_CRTV_LUT(1,4,0) | 330 | 004048E0 | RW | 12 |
| Corrective MB1, Links (59:48), Mask1: RMB_CRTV_LUT(1,4,1) | 331 | 004048E4 | RW | 12 |
| Corrective MB0, Links (71:60), Mask1: RMB_CRTV_LUT(1,5,0) | 332 | 004048E8 | RW | 12 |
| Corrective MB1, Links (71:60), Mask1: RMB_CRTV_LUT(1,5,1) | 333 | 004048EC | RW | 12 |
| Corrective MB0, Links (83:72), Mask1: RMB_CRTV_LUT(1,6,0) | 334 | 004048F0 | RW | 12 |
| Corrective MB1, Links (83:72), Mask1: RMB_CRTV_LUT(1,6,1) | 335 | 004048F4 | RW | 12 |
| Corrective MB0, Links (95:84), Mask1: RMB_CRTV_LUT(1,7,0) | 336 | 004048F8 | RW | 12 |
| Corrective MB1, Links (95:84), Mask1: RMB_CRTV_LUT(1,7,1) | 337 | 004048FC | RW | 12 |
| Description | REG ID | Address | Access | Width |
| Default MB0, Links (11: 0), Mask2: RMB_DFLT_LUT(2,0,0) | 2B8 | 00404900 | RW | 12 |
| Default MB1, Links (11: 0), Mask2: RMB_DFLT_LUT(2,0,1) | 2B9 | 00404904 | RW | 12 |
| Default MB0, Links (23:12), Mask2: RMB_DFLT_LUT(2,1,0) | 2BA | 00404908 | RW | 12 |
| Default MB1, Links (23:12), Mask2: RMB_DFLT_LUT(2,1,1) | 2BB | 0040490C | RW | 12 |
| Default MB0, Links (35:24), Mask2: RMB_DFLT_LUT(2,2,0) | 2BC | 00404910 | RW | 12 |
| Default MB1, Links (35:24), Mask2: RMB_DFLT_LUT(2,2,1) | 2BD | 00404914 | RW | 12 |
| Default MB0, Links (47:36), Mask2: RMB_DFLT_LUT(2,3,0) | 2BE | 00404918 | RW | 12 |
| Default MB1, Links (47:36), Mask2: RMB_DFLT_LUT(2,3,1) | 2BF | 0040491C | RW | 12 |
| Default MB0, Links (59:48), Mask2: RMB_DFLT_LUT(2,4,0) | 2C0 | 00404920 | RW | 12 |
| Default MB1, Links (59:48), Mask2: RMB_DFLT_LUT(2,4,1) | 2C1 | 00404924 | RW | 12 |
| Default MB0, Links (71:60), Mask2: RMB_DFLT_LUT(2,5,0) | 2C2 | 00404928 | RW | 12 |
| Default MB1, Links (71:60), Mask2: RMB_DFLT_LUT(2,5,1) | 2C3 | 0040492C | RW | 12 |
| Default MB0, Links (83:72), Mask2: RMB_DFLT_LUT(2,6,0) | 2C4 | 00404930 | RW | 12 |
| Default MB1, Links (83:72), Mask2: RMB_DFLT_LUT(2,6,1) | 2C5 | 00404924 | RW | 12 |
| Default MB0, Links (95:84), Mask2: RMB_DFLT_LUT(2,7,0) | 2C6 | 00404938 | RW | 12 |
| Default MB1, Links (95:84), Mask2: RMB_DFLT_LUT(2,7,1) | 2C7 | 0040493C | RW | 12 |
| Corrective MB0, Links (11: 0), Mask2: RMB_CRTV_LUT(2,0,0) | 338 | 00404940 | RW | 12 |
| Corrective MB1, Links (11: 0), Mask2: RMB_CRTV_LUT(2,0,1) | 339 | 00404944 | RW | 12 |
| Corrective MB0, Links (23:12), Mask2: RMB_CRTV_LUT(2,1,0) | 33A | 00404948 | RW | 12 |
| Corrective MB1, Links (23:12), Mask2: RMB_CRTV_LUT(2,1,1) | 33B | 0040494C | RW | 12 |
| Corrective MB0, Links (35:24), Mask2: RMB_CRTV_LUT(2,2,0) | 33C | 00404950 | RW | 12 |
| Corrective MB1, Links (35:24), Mask2: RMB_CRTV_LUT(2,2,1) | 33D | 00404954 | RW | 12 |
| Corrective MB0, Links (47:36), Mask2: RMB_CRTV_LUT(2,3,0) | 33E | 00404958 | RW | 12 |
| Corrective MB1, Links (47:36), Mask2: RMB_CRTV_LUT(2,3,1) | 33F | 0040495C | RW | 12 |
| Corrective MB0, Links (59:48), Mask2: RMB_CRTV_LUT(2,4,0) | 340 | 00404960 | RW | 12 |
| Corrective MB1, Links (59:48), Mask2: RMB_CRTV_LUT(2,4,1) | 341 | 00404964 | RW | 12 |
| Corrective MB0, Links (71:60), Mask2: RMB_CRTV_LUT(2,5,0) | 342 | 00404968 | RW | 12 |
| Corrective MB1, Links (71:60), Mask2: RMB_CRTV_LUT(2,5,1) | 343 | 0040496C | RW | 12 |
| Corrective MB0, Links (83:72), Mask2: RMB_CRTV_LUT(2,6,0) | 344 | 00404970 | RW | 12 |
| Corrective MB1, Links (83:72), Mask2: RMB_CRTV_LUT(2,6,1) | 345 | 00404974 | RW | 12 |
| Corrective MB0, Links (95:84), Mask2: RMB_CRTV_LUT(2,7,0) | 346 | 00404978 | RW | 12 |
| Corrective MB1, Links (95:84), Mask2: RMB_CRTV_LUT(2,7,1) | 347 | 0040497C | RW | 12 |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Default MB0, Links (11: 0), Mask3: RMB_DFLT_LUT(3,0,0) | 2C8 | 00404980 | RW | 12 |
| Default MB1, Links (11: 0), Mask3: RMB_DFLT_LUT(3,0,1) | 2C9 | 00404984 | RW | 12 |
| Default MB0, Links (23:12), Mask3: RMB_DFLT_LUT(3,1,0) | 2CA | 00404988 | RW | 12 |
| Default MB1, Links (23:12), Mask3: RMB_DFLT_LUT(3,1,1) | 2CB | 0040498C | RW | 12 |
| Default MB0, Links (35:24), Mask3: RMB_DFLT_LUT(3,2,0) | 2CC | 00404990 | RW | 12 |
| Default MB1, Links (35:24), Mask3: RMB_DFLT_LUT(3,2,1) | 2CD | 00404994 | RW | 12 |
| Default MB0, Links (47:36), Mask3: RMB_DFLT_LUT(3,3,0) | 2CE | 00404998 | RW | 12 |
| Default MB1, Links (47:36), Mask3: RMB_DFLT_LUT(3,3,1) | 2CF | 0040499C | RW | 12 |
| Default MB0, Links (59:48), Mask3: RMB_DFLT_LUT(3,4,0) | 2D0 | 004049A0 | RW | 12 |
| Default MB1, Links (59:48), Mask3: RMB_DFLT_LUT(3,4,1) | 2D1 | 004049A4 | RW | 12 |
| Default MB0, Links (71:60), Mask3: RMB_DFLT_LUT(3,5,0) | 2D2 | 004049A8 | RW | 12 |
| Default MB1, Links (71:60), Mask3: RMB_DFLT_LUT(3,5,1) | 2D3 | 004049AC | RW | 12 |
| Default MB0, Links (83:72), Mask3: RMB_DFLT_LUT(3,6,0) | 2D4 | 004049B0 | RW | 12 |
| Default MB1, Links (83:72), Mask3: RMB_DFLT_LUT(3,6,1) | 2D5 | 004049B4 | RW | 12 |
| Default MB0, Links (95:84), Mask3: RMB_DFLT_LUT(3,7,0) | 2D6 | 004049B8 | RW | 12 |
| Default MB1, Links (95:84), Mask3: RMB_DFLT_LUT(3,7,1) | 2D7 | 004049BC | RW | 12 |
| Corrective MB0, Links (11: 0), Mask3: RMB_CRTV_LUT(3,0,0) | 348 | 004049C0 | RW | 12 |
| Corrective MB1, Links (11: 0), Mask3: RMB_CRTV_LUT(3,0,1) | 349 | 004049C4 | RW | 12 |
| Corrective MB0, Links (23:12), Mask3: RMB_CRTV_LUT(3,1,0) | 34A | 004049C8 | RW | 12 |
| Corrective MB1, Links (23:12), Mask3: RMB_CRTV_LUT(3,1,1) | 34B | 004049CC | RW | 12 |
| Corrective MB0, Links (35:24), Mask3: RMB_CRTV_LUT(3,2,0) | 34C | 004049D0 | RW | 12 |
| Corrective MB1, Links (35:24), Mask3: RMB_CRTV_LUT(3,2,1) | 34D | 004049D4 | RW | 12 |
| Corrective MB0, Links (47:36), Mask3: RMB_CRTV_LUT(3,3,0) | 34E | 004049D8 | RW | 12 |
| Corrective MB1, Links (47:36), Mask3: RMB_CRTV_LUT(3,3,1) | 34F | 004049DC | RW | 12 |
| Corrective MB0, Links (59:48), Mask3: RMB_CRTV_LUT(3,4,0) | 350 | 004049E0 | RW | 12 |
| Corrective MB1, Links (59:48), Mask3: RMB_CRTV_LUT(3,4,1) | 351 | 004049E4 | RW | 12 |
| Corrective MB0, Links (71:60), Mask3: RMB_CRTV_LUT(3,5,0) | 352 | 004049E8 | RW | 12 |
| Corrective MB1, Links (71:60), Mask3: RMB_CRTV_LUT(3,5,1) | 353 | 004049EC | RW | 12 |
| Corrective MB0, Links (83:72), Mask3: RMB_CRTV_LUT(3,6,0) | 354 | 004049F0 | RW | 12 |
| Corrective MB1, Links (83:72), Mask3: RMB_CRTV_LUT(3,6,1) | 355 | 004049F4 | RW | 12 |
| Corrective MB0, Links (95:84), Mask3: RMB_CRTV_LUT(3,7,0) | 356 | 004049F8 | RW | 12 |
| Corrective MB1, Links (95:84), Mask3: RMB_CRTV_LUT(3,7,1) | 357 | 004049FC | RW | 12 |
| Default MB0, Links (11: 0), Mask4: RMB_DFLT_LUT(4,0,0) | 2D8 | 00404A00 | RW | 12 |
| Default MB1, Links (11: 0), Mask4: RMB_DFLT_LUT(4,0,1) | 2D9 | 00404A04 | RW | 12 |
| Default MB0, Links (23:12), Mask4: RMB_DFLT_LUT(4,1,0) | 2DA | 00404A08 | RW | 12 |
| Default MB1, Links (23:12), Mask4: RMB_DFLT_LUT(4,1,1) | 2DB | 00404A0C | RW | 12 |
| Default MB0, Links (35:24), Mask4: RMB_DFLT_LUT(4,2,0) | 2DC | 00404A10 | RW | 12 |
| Default MB1, Links (35:24), Mask4: RMB_DFLT_LUT(4,2,1) | 2DD | 00404A14 | RW | 12 |
| Default MB0, Links (47:36), Mask4: RMB_DFLT_LUT(4,3,0) | 2DE | 00404A18 | RW | 12 |
| Default MB1, Links (47:36), Mask4: RMB_DFLT_LUT(4,3,1) | 2DF | 00404A1C | RW | 12 |
| Default MB0, Links (59:48), Mask4: RMB_DFLT_LUT(4,4,0) | 2E0 | 00404A20 | RW | 12 |
| Default MB1, Links (59:48), Mask4: RMB_DFLT_LUT(4,4,1) | 2E1 | 00404A24 | RW | 12 |
| Default MB0, Links (71:60), Mask4: RMB_DFLT_LUT(4,5,0) | 2E2 | 00404A28 | RW | 12 |
| Default MB1, Links (71:60), Mask4: RMB_DFLT_LUT(4,5,1) | 2E3 | 00404A2C | RW | 12 |
| Default MB0, Links (83:72), Mask4: RMB_DFLT_LUT(4,6,0) | 2E4 | 00404A30 | RW | 12 |
| Default MB1, Links (83:72), Mask4: RMB_DFLT_LUT(4,6,1) | 2E5 | 00404A34 | RW | 12 |
| Default MB0, Links (95:84), Mask4: RMB_DFLT_LUT(4,7,0) | 2E6 | 00404A38 | RW | 12 |
| Default MB1, Links (95:84), Mask4: RMB_DFLT_LUT(4,7,1) | 2E7 | 00404A3C | RW | 12 |
| Corrective MB0, Links (11: 0), Mask4: RMB_CRTV_LUT(4,0,0) | 358 | 00404A40 | RW | 12 |
| Corrective MB1, Links (11: 0), Mask4: RMB_CRTV_LUT(4,0,1) | 359 | 00404A44 | RW | 12 |
| Corrective MB0, Links (23:12), Mask4: RMB_CRTV_LUT(4,1,0) | 35A | 00404A48 | RW | 12 |
| Corrective MB1, Links (23:12), Mask4: RMB_CRTV_LUT(4,1,1) | 35B | 00404A4C | RW | 12 |
| Corrective MB0, Links (35:24), Mask4: RMB_CRTV_LUT(4,2,0) | 35C | 00404A50 | RW | 12 |
| Corrective MB1, Links (35:24), Mask4: RMB_CRTV_LUT(4,2,1) | 35D | 00404A54 | RW | 12 |
| Corrective MB0, Links (47:36), Mask4: RMB_CRTV_LUT(4,3,0) | 35E | 00404A58 | RW | 12 |
| Corrective MB1, Links (47:36), Mask4: RMB_CRTV_LUT(4,3,1) | 35F | 00404A5C | RW | 12 |
| Corrective MB0, Links (59:48), Mask4: RMB_CRTV_LUT(4,4,0) | 360 | 00404A60 | RW | 12 |
| Corrective MB1, Links (59:48), Mask4: RMB_CRTV_LUT(4,4,1) | 361 | 00404A64 | RW | 12 |
| Corrective MB0, Links (71:60), Mask4: RMB_CRTV_LUT(4,5,0) | 362 | 00404A68 | RW | 12 |
| Corrective MB1, Links (71:60), Mask4: RMB_CRTV_LUT(4,5,1) | 363 | 00404A6C | RW | 12 |
| Corrective MB0, Links (83:72), Mask4: RMB_CRTV_LUT(4,6,0) | 364 | 00404A70 | RW | 12 |
| Corrective MB1, Links (83:72), Mask4: RMB_CRTV_LUT(4,6,1) | 365 | 00404A74 | RW | 12 |
| Corrective MB0, Links (95:84), Mask4: RMB_CRTV_LUT(4,7,0) | 366 | 00404A78 | RW | 12 |
| Corrective MB1, Links (95:84), Mask4: RMB_CRTV_LUT(4,7,1) | 367 | 00404A7C | RW | 12 |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Default MB0, Links (11: 0), Mask5: RMB_DFLT_LUT(5,0,0) | 2E8 | 00404A80 | RW | 12 |
| Default MB1, Links (11: 0), Mask5: RMB_DFLT_LUT(5,0,1) | 2E9 | 00404A84 | RW | 12 |
| Default MB0, Links (23:12), Mask5: RMB_DFLT_LUT(5,1,0) | 2EA | 00404A88 | RW | 12 |
| Default MB1, Links (23:12), Mask5: RMB_DFLT_LUT(5,1,1) | 2EB | 00404A8C | RW | 12 |
| Default MB0, Links (35:24), Mask5: RMB_DFLT_LUT(5,2,0) | 2EC | 00404A90 | RW | 12 |
| Default MB1, Links (35:24), Mask5: RMB_DFLT_LUT(5,2,1) | 2ED | 00404A94 | RW | 12 |
| Default MB0, Links (47:36), Mask5: RMB_DFLT_LUT(5,3,0) | 2EE | 00404A98 | RW | 12 |
| Default MB1, Links (47:36), Mask5: RMB_DFLT_LUT(5,3,1) | 2EF | 00404A9C | RW | 12 |
| Default MB0, Links (59:48), Mask5: RMB_DFLT_LUT(5,4,0) | 2F0 | 00404AA0 | RW | 12 |
| Default MB1, Links (59:48), Mask5: RMB_DFLT_LUT(5,4,1) | 2F1 | 00404AA4 | RW | 12 |
| Default MB0, Links (71:60), Mask5: RMB_DFLT_LUT(5,5,0) | 2F2 | 00404AA8 | RW | 12 |
| Default MB1, Links (71:60), Mask5: RMB_DFLT_LUT(5,5,1) | 2F3 | 00404AAC | RW | 12 |
| Default MB0, Links (83:72), Mask5: RMB_DFLT_LUT(5,6,0) | 2F4 | 00404AB0 | RW | 12 |
| Default MB1, Links (83:72), Mask5: RMB_DFLT_LUT(5,6,1) | 2F5 | 00404AB4 | RW | 12 |
| Default MB0, Links (95:84), Mask5: RMB_DFLT_LUT(5,7,0) | 2F6 | 00404AB8 | RW | 12 |
| Default MB1, Links (95:84), Mask5: RMB_DFLT_LUT(5,7,1) | 2F7 | 00404ABC | RW | 12 |
| Corrective MB0, Links (11: 0), Mask5: RMB_CRTV_LUT(5,0,0) | 368 | 00404AC0 | RW | 12 |
| Corrective MB1, Links (11: 0), Mask5: RMB_CRTV_LUT(5,0,1) | 369 | 00404AC4 | RW | 12 |
| Corrective MB0, Links (23:12), Mask5: RMB_CRTV_LUT(5,1,0) | 36A | 00404AC8 | RW | 12 |
| Corrective MB1, Links (23:12), Mask5: RMB_CRTV_LUT(5,1,1) | 36B | 00404ACC | RW | 12 |
| Corrective MB0, Links (35:24), Mask5: RMB_CRTV_LUT(5,2,0) | 36C | 00404AD0 | RW | 12 |
| Corrective MB1, Links (35:24), Mask5: RMB_CRTV_LUT(5,2,1) | 36D | 00404AD4 | RW | 12 |
| Corrective MB0, Links (47:36), Mask5: RMB_CRTV_LUT(5,3,0) | 36E | 00404AD8 | RW | 12 |
| Corrective MB1, Links (47:36), Mask5: RMB_CRTV_LUT(5,3,1) | 36F | 00404ADC | RW | 12 |
| Corrective MB0, Links (59:48), Mask5: RMB_CRTV_LUT(5,4,0) | 370 | 00404AE0 | RW | 12 |
| Corrective MB1, Links (59:48), Mask5: RMB_CRTV_LUT(5,4,1) | 371 | 00404AE4 | RW | 12 |
| Corrective MB0, Links (71:60), Mask5: RMB_CRTV_LUT(5,5,0) | 372 | 00404AE8 | RW | 12 |
| Corrective MB1, Links (71:60), Mask5: RMB_CRTV_LUT(5,5,1) | 373 | 00404AEC | RW | 12 |
| Corrective MB0, Links (83:72), Mask5: RMB_CRTV_LUT(5,6,0) | 374 | 00404AF0 | RW | 12 |
| Corrective MB1, Links (83:72), Mask5: RMB_CRTV_LUT(5,6,1) | 375 | 00404AF4 | RW | 12 |
| Corrective MB0, Links (95:84), Mask5: RMB_CRTV_LUT(5,7,0) | 376 | 00404AF8 | RW | 12 |
| Corrective MB1, Links (95:84), Mask5: RMB_CRTV_LUT(5,7,1) | 377 | 00404AFC | RW | 12 |
| Default MB0, Links (11: 0), Mask6: RMB_DFLT_LUT(6,0,0) | 2F8 | 00404B00 | RW | 12 |
| Default MB1, Links (11: 0), Mask6: RMB_DFLT_LUT(6,0,1) | 2F9 | 00404B04 | RW | 12 |
| Default MB0, Links (23:12), Mask6: RMB_DFLT_LUT(6,1,0) | 2FA | 00404B08 | RW | 12 |
| Default MB1, Links (23:12), Mask6: RMB_DFLT_LUT(6,1,1) | 2FB | 00404B0C | RW | 12 |
| Default MB0, Links (35:24), Mask6: RMB_DFLT_LUT(6,2,0) | 2FC | 00404B10 | RW | 12 |
| Default MB1, Links (35:24), Mask6: RMB_DFLT_LUT(6,2,1) | 2FD | 00404B14 | RW | 12 |
| Default MB0, Links (47:36), Mask6: RMB_DFLT_LUT(6,3,0) | 2FE | 00404B18 | RW | 12 |
| Default MB1, Links (47:36), Mask6: RMB_DFLT_LUT(6,3,1) | 2FF | 00404B1C | RW | 12 |
| Default MB0, Links (59:48), Mask6: RMB_DFLT_LUT(6,4,0) | 300 | 00404B20 | RW | 12 |
| Default MB1, Links (59:48), Mask6: RMB_DFLT_LUT(6,4,1) | 301 | 00404B24 | RW | 12 |
| Default MB0, Links (71:60), Mask6: RMB_DFLT_LUT(6,5,0) | 302 | 00404B28 | RW | 12 |
| Default MB1, Links (71:60), Mask6: RMB_DFLT_LUT(6,5,1) | 303 | 00404B2C | RW | 12 |
| Default MB0, Links (83:72), Mask6: RMB_DFLT_LUT(6,6,0) | 304 | 00404B30 | RW | 12 |
| Default MB1, Links (83:72), Mask6: RMB_DFLT_LUT(6,6,1) | 305 | 00404B34 | RW | 12 |
| Default MB0, Links (95:84), Mask6: RMB_DFLT_LUT(6,7,0) | 306 | 00404B38 | RW | 12 |
| Default MB1, Links (95:84), Mask6: RMB_DFLT_LUT(6,7,1) | 307 | 00404B3C | RW | 12 |
| Corrective MB0, Links (11: 0), Mask6: RMB_CRTV_LUT(6,0,0) | 378 | 00404B40 | RW | 12 |
| Corrective MB1, Links (11: 0), Mask6: RMB_CRTV_LUT(6,0,1) | 379 | 00404B44 | RW | 12 |
| Corrective MB0, Links (23:12), Mask6: RMB_CRTV_LUT(6,1,0) | 37A | 00404B48 | RW | 12 |
| Corrective MB1, Links (23:12), Mask6: RMB_CRTV_LUT(6,1,1) | 37B | 00404B4C | RW | 12 |
| Corrective MB0, Links (35:24), Mask6: RMB_CRTV_LUT(6,2,0) | 37C | 00404B50 | RW | 12 |
| Corrective MB1, Links (35:24), Mask6: RMB_CRTV_LUT(6,2,1) | 37D | 00404B54 | RW | 12 |
| Corrective MB0, Links (47:36), Mask6: RMB_CRTV_LUT(6,3,0) | 37E | 00404B58 | RW | 12 |
| Corrective MB1, Links (47:36), Mask6: RMB_CRTV_LUT(6,3,1) | 37F | 00404B5C | RW | 12 |
| Corrective MB0, Links (59:48), Mask6: RMB_CRTV_LUT(6,4,0) | 380 | 00404B60 | RW | 12 |
| Corrective MB1, Links (59:48), Mask6: RMB_CRTV_LUT(6,4,1) | 381 | 00404B64 | RW | 12 |
| Corrective MB0, Links (71:60), Mask6: RMB_CRTV_LUT(6,5,0) | 382 | 00404B68 | RW | 12 |
| Corrective MB1, Links (71:60), Mask6: RMB_CRTV_LUT(6,5,1) | 383 | 00404B6C | RW | 12 |
| Corrective MB0, Links (83:72), Mask6: RMB_CRTV_LUT(6,6,0) | 384 | 00404B70 | RW | 12 |
| Corrective MB1, Links (83:72), Mask6: RMB_CRTV_LUT(6,6,1) | 385 | 00404B74 | RW | 12 |
| Corrective MB0, Links (95:84), Mask6: RMB_CRTV_LUT(6,7,0) | 386 | 00404B78 | RW | 12 |
| Corrective MB1, Links (95:84), Mask6: RMB_CRTV_LUT(6,7,1) | 387 | 00404B7C | RW | 12 |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Default MB0, Links (11: 0), Mask7: RMB_DFLT_LUT(7,0,0) | 308 | 00404B80 | RW | 12 |
| Default MB1, Links (11: 0), Mask7: RMB_DFLT_LUT(7,0,1) | 309 | 00404B84 | RW | 12 |
| Default MB0, Links (23:12), Mask7: RMB_DFLT_LUT(7,1,0) | 30A | 00404B88 | RW | 12 |
| Default MB1, Links (23:12), Mask7: RMB_DFLT_LUT(7,1,1) | 30B | 00404B8C | RW | 12 |
| Default MB0, Links (35:24), Mask7: RMB_DFLT_LUT(7,2,0) | 30C | 00404B90 | RW | 12 |
| Default MB1, Links (35:24), Mask7: RMB_DFLT_LUT(7,2,1) | 30D | 00404B94 | RW | 12 |
| Default MB0, Links (47:36), Mask7: RMB_DFLT_LUT(7,3,0) | 30E | 00404B98 | RW | 12 |
| Default MB1, Links (47:36), Mask7: RMB_DFLT_LUT(7,3,1) | 30F | 00404B9C | RW | 12 |
| Default MB0, Links (59:48), Mask7: RMB_DFLT_LUT(7,4,0) | 310 | 00404BA0 | RW | 12 |
| Default MB1, Links (59:48), Mask7: RMB_DFLT_LUT(7,4,1) | 311 | 00404BA4 | RW | 12 |
| Default MB0, Links (71:60), Mask7: RMB_DFLT_LUT(7,5,0) | 312 | 00404BA8 | RW | 12 |
| Default MB1, Links (71:60), Mask7: RMB_DFLT_LUT(7,5,1) | 313 | 00404BAC | RW | 12 |
| Default MB0, Links (83:72), Mask7: RMB_DFLT_LUT(7,6,0) | 314 | 00404BB0 | RW | 12 |
| Default MB1, Links (83:72), Mask7: RMB_DFLT_LUT(7,6,1) | 315 | 00404BB4 | RW | 12 |
| Default MB0, Links (95:84), Mask7: RMB_DFLT_LUT(7,7,0) | 316 | 00404BB8 | RW | 12 |
| Default MB1, Links (95:84), Mask7: RMB_DFLT_LUT(7,7,1) | 317 | 00404BBC | RW | 12 |
| Corrective MB0, Links (11: 0), Mask7: RMB_CRTV_LUT(7,0,0) | 388 | 00404BC0 | RW | 12 |
| Corrective MB1, Links (11: 0), Mask7: RMB_CRTV_LUT(7,0,1) | 389 | 00404BC4 | RW | 12 |
| Corrective MB0, Links (23:12), Mask7: RMB_CRTV_LUT(7,1,0) | 38A | 00404BC8 | RW | 12 |
| Corrective MB1, Links (23:12), Mask7: RMB_CRTV_LUT(7,1,1) | 38B | 00404BCC | RW | 12 |
| Corrective MB0, Links (35:24), Mask7: RMB_CRTV_LUT(7,2,0) | 38C | 00404BD0 | RW | 12 |
| Corrective MB1, Links (35:24), Mask7: RMB_CRTV_LUT(7,2,1) | 38D | 00404BD4 | RW | 12 |
| Corrective MB0, Links (47:36), Mask7: RMB_CRTV_LUT(7,3,0) | 38E | 00404BD8 | RW | 12 |
| Corrective MB1, Links (47:36), Mask7: RMB_CRTV_LUT(7,3,1) | 38F | 00404BDC | RW | 12 |
| Corrective MB0, Links (59:48), Mask7: RMB_CRTV_LUT(7,4,0) | 390 | 00404BE0 | RW | 12 |
| Corrective MB1, Links (59:48), Mask7: RMB_CRTV_LUT(7,4,1) | 391 | 00404BE4 | RW | 12 |
| Corrective MB0, Links (71:60), Mask7: RMB_CRTV_LUT(7,5,0) | 392 | 00404BE8 | RW | 12 |
| Corrective MB1, Links (71:60), Mask7: RMB_CRTV_LUT(7,5,1) | 393 | 00404BEC | RW | 12 |
| Corrective MB0, Links (83:72), Mask7: RMB_CRTV_LUT(7,6,0) | 394 | 00404BF0 | RW | 12 |
| Corrective MB1, Links (83:72), Mask7: RMB_CRTV_LUT(7,6,1) | 395 | 00404BF4 | RW | 12 |
| Corrective MB0, Links (95:84), Mask7: RMB_CRTV_LUT(7,7,0) | 396 | 00404BF8 | RW | 12 |
| Corrective MB1, Links (95:84), Mask7: RMB_CRTV_LUT(7,7,1) | 397 | 00404BFC | RW | 12 |

# ROD Diagnostic Memory FIFO Registers

## Input Memory FIFO Registers

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Input Memory FIFO A: Low Order Word Write Register | 00406000 | RW | 32 |
|  | Bit Value |
| Bits[31: 0]: LSW Value | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Input Memory FIFO A: High Order Word Write Register | 00406004 | RW | 16 |
|  | Bit Value |
| Bits[15: 0]: MSW Value | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Input Memory FIFO B: Low Order Word Write Register | 00406008 | RW | 32 |
|  | Bit Value |
| Bits[31: 0]: LSW Value | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Input Memory FIFO B: High Order Word Write Register | 0040600C | RW | 16 |
|  | Bit Value |
| Bits[15: 0]: MSW Value | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Input Memory FIFO A: Low Order Word Read Register | 00406020 | R | 32 |
|  | Bit Value |
| Bits[31: 0]: LSW Value | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Input Memory FIFO A: High Order Word Read Register | 00406024 | R | 16 |
|  | Bit Value |
| Bits[15: 0]: MSW Value | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Input Memory FIFO B: Low Order Word Read Register | 00406028 | R | 32 |
|  | Bit Value |
| Bits[31: 0]: LSW Value | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Input Memory FIFO B: High Order Word Read Register | 0040602C | R | 16 |
|  | Bit Value |
| Bits[15: 0]: MSW Value | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Input Memory FIFO A: Advance FIFO A | 00406040 | RW | 1 |
| A write operation to this register writes the value in the Write Register for FIFO A into the FIFO. A read operation to this register loads the data from the FIFO into the Read Register. The bit value of this register is ignored. | Bit Value |
|  | 1 | 0 |
| Bit 0: Advance 1 Word | ADV | IDLE |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Input Memory FIFO B: Advance FIFO B | 00406048 | RW | 1 |
| A write operation to this register writes the value in the Write Register for FIFO A into the FIFO. A read operation to this register loads the data from the FIFO into the Read Register. The bit value of this register is ignored. | Bit Value |
|  | 1 | 0 |
| Bit 0: Advance 1 Word | ADV | IDLE |

## Event Memory FIFO Registers

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Event Memory FIFO A: Low Order Word Read Register | 00406120 | R | 32 |
|  | Bit Value |
| Bits[31: 0]: LSW Value | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Event Memory FIFO A: High Order Word Read Register | 00406124 | R | 16 |
|  | Bit Value |
| Bits[15: 0]: MSW Value | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Event Memory FIFO B: Low Order Word Read Register | 00406128 | R | 32 |
|  | Bit Value |
| Bits[31: 0]: LSW Value | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Event Memory FIFO B: High Order Word Read Register | 0040612C | R | 16 |
|  | Bit Value |
| Bits[15: 0]: MSW Value | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Event Memory FIFO C: Word Read Register | 00406130 | R | 32 |
|  | Bit Value |
| Bits[31: 0]: Value | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Event Memory FIFO A: Advance FIFO A | 00406140 | R | 1 |
| A read operation to this register loads the data from the FIFO into the Read Register. A write operation to this register is ignored. The bit value of this register is ignored. | Bit Value |
|  | 1 | 0 |
| Bit 0: Advance 1 Word | ADV | IDLE |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Event Memory FIFO B: Advance FIFO B | 00406148 | R | 1 |
| A read operation to this register loads the data from the FIFO into the Read Register. A write operation to this register is ignored. The bit value of this register is ignored. | Bit Value |
|  | 1 | 0 |
| Bit 0: Advance 1 Word | ADV | IDLE |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Event Memory FIFO C: Advance FIFO C | 00406150 | R | 1 |
| A read operation to this register loads the data from the FIFO into the Read Register. A write operation to this register is ignored. The bit value of this register is ignored. | Bit Value |
|  | 1 | 0 |
| Bit 0: Advance 1 Word | ADV | IDLE |

# BOC Registers

| BOC1 Set-Up Bus |
| --- |
| Top Level Address Map |
| Mnemonic | VME Add (Hex) | SetUpBus Add (hex) | Function |  | Mnemonic | VME Add (Hex) | SetUpBus Add (hex) | Function |
|  |  | 200 |  |  |  |  | 400 |  |
|  |  |  | Unused |  |  |  |  | BOC Control Registers |
|  |  | 1E0 |  |  |  |  | 3E0 |  |
|  |  |  | Reserved |  |  |  |  |  |
|  |  | 1C0 |  |  | CREGS: | 00408F00 | 3C0 |  |
|  |  |  |  |  |  |  |  | Reserved _________________ _Monitoring(series)__ Reserved |
|  |  | 1A0 | TX Laser Current DACs |  |  |  | 3A0 |  |
| TXDACS: | 00408600 | 180 |  |  |  |  | 380 |  |
|  |  | 160 |  |  |  |  | 360 |  |
|  |  |  |  |  |  |  |  | RX Threshold DACs |
|  |  | 140 |  |  |  |  | 340 |  |
|  |  | 120 |  |  |  |  | 320 |  |
|  |  | 100 |  |  | RXDACS: | 00408C00 | 300 |  |
|  |  | 0F0 |  |  |  |  |  |  |
|  |  | 0E0 | BPM12_3 Lasers[47:36] |  |  |  | 2E0 | Strobe Delays |
|  |  | 0D0 |  |  |  |  |  |  |
|  | 00408300 | 0C0 |  |  |  |  | 2C0 |  |
|  |  | 0B0 |  |  |  |  |  |  |
|  |  | 0A0 | BPM12_2 Lasers[35:24] |  |  |  | 2A0 |  |
|  |  | 090 |  |  |  |  |  |  |
|  | 00408200 | 080 |  |  |  | 00408A00 | 280 |  |
|  |  | 070 |  |  |  |  |  |  |
|  |  | 060 | BPM12_1 Lasers[23:12] |  | CLK_PHASES: | 00408980 | 260 | Clock Phases |
|  |  | 050 |  |  |  |  |  | Delays |
|  | 00408100 | 040 |  |  |  |  | 240 |  |
|  |  | 030 |  |  |  |  |  |  |
|  |  | 020 | BPM12_0 Lasers[11:0] |  |  |  | 220 |  |
|  |  | 010 |  |  |  |  |  |  |
| BPMS: | 00408000 | 000 |  |  | RXDELAYS: | 00408800 | 200 |  |

## FE Command Stream Control Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| FE Command Stream 0: Stream Inhibit |  | 00408000 | RW | 1 |
| FE Command Stream 1: Stream Inhibit |  | 00408010 |  |  |
| FE Command Stream 2: Stream Inhibit |  | 00408020 |  |  |
| FE Command Stream 3: Stream Inhibit |  | 00408030 |  |  |
| FE Command Stream 4: Stream Inhibit |  | 00408040 |  |  |
| FE Command Stream 5: Stream Inhibit |  | 00408050 |  |  |
| FE Command Stream 6: Stream Inhibit |  | 00408060 |  |  |
| FE Command Stream 7: Stream Inhibit |  | 00408070 |  |  |
| FE Command Stream 8: Stream Inhibit |  | 00408080 |  |  |
| FE Command Stream 9: Stream Inhibit |  | 00408090 |  |  |
| FE Command Stream 10: Stream Inhibit |  | 004080A0 |  |  |
| FE Command Stream 11: Stream Inhibit |  | 004080B0 |  |  |
| FE Command Stream 12: Stream Inhibit |  | 00408100 |  |  |
| FE Command Stream 13: Stream Inhibit |  | 00408110 |  |  |
| FE Command Stream 14: Stream Inhibit |  | 00408120 |  |  |
| FE Command Stream 15: Stream Inhibit |  | 00408130 |  |  |
| FE Command Stream 16: Stream Inhibit |  | 00408140 |  |  |
| FE Command Stream 17: Stream Inhibit |  | 00408150 |  |  |
| FE Command Stream 18: Stream Inhibit |  | 00408160 |  |  |
| FE Command Stream 19: Stream Inhibit |  | 00408170 |  |  |
| FE Command Stream 20: Stream Inhibit |  | 00408180 |  |  |
| FE Command Stream 21: Stream Inhibit |  | 00408190 |  |  |
| FE Command Stream 22: Stream Inhibit |  | 004081A0 |  |  |
| FE Command Stream 23: Stream Inhibit |  | 004081B0 |  |  |
| FE Command Stream 24: Stream Inhibit |  | 00408200 |  |  |
| FE Command Stream 25: Stream Inhibit |  | 00408210 |  |  |
| FE Command Stream 26: Stream Inhibit |  | 00408220 |  |  |
| FE Command Stream 27: Stream Inhibit |  | 00408230 |  |  |
| FE Command Stream 28: Stream Inhibit |  | 00408240 |  |  |
| FE Command Stream 29: Stream Inhibit |  | 00408250 |  |  |
| FE Command Stream 30: Stream Inhibit |  | 00408260 |  |  |
| FE Command Stream 31: Stream Inhibit |  | 00408270 |  |  |
| FE Command Stream 32: Stream Inhibit |  | 00408280 |  |  |
| FE Command Stream 33: Stream Inhibit |  | 00408290 |  |  |
| FE Command Stream 34: Stream Inhibit |  | 004082A0 |  |  |
| FE Command Stream 35: Stream Inhibit |  | 004082B0 |  |  |
| FE Command Stream 36: Stream Inhibit |  | 00408300 |  |  |
| FE Command Stream 37: Stream Inhibit |  | 00408310 |  |  |
| FE Command Stream 38: Stream Inhibit |  | 00408320 |  |  |
| FE Command Stream 39: Stream Inhibit |  | 00408330 |  |  |
| FE Command Stream 40: Stream Inhibit |  | 00408340 |  |  |
| FE Command Stream 41: Stream Inhibit |  | 00408350 |  |  |
| FE Command Stream 42: Stream Inhibit |  | 00408360 |  |  |
| FE Command Stream 43: Stream Inhibit |  | 00408370 |  |  |
| FE Command Stream 44: Stream Inhibit |  | 00408380 |  |  |
| FE Command Stream 45: Stream Inhibit |  | 00408390 |  |  |
| FE Command Stream 46: Stream Inhibit |  | 004083A0 |  |  |
| FE Command Stream 47: Stream Inhibit |  | 004083B0 |  |  |
| Bit to inhibit output of optical data streams | Bit Value |
|  | 1 | 0 |
| Bit 0: Stream Inhibit (Reset Value = 0) | Inhibit | Enabled |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| FE Command Stream 0: Mark Space |  | 00408004 | RW | 5 |
| FE Command Stream 1: Mark Space |  | 00408014 |  |  |
| FE Command Stream 2: Mark Space |  | 00408024 |  |  |
| FE Command Stream 3: Mark Space |  | 00408034 |  |  |
| FE Command Stream 4: Mark Space |  | 00408044 |  |  |
| FE Command Stream 5: Mark Space |  | 00408054 |  |  |
| FE Command Stream 6: Mark Space |  | 00408064 |  |  |
| FE Command Stream 7: Mark Space |  | 00408074 |  |  |
| FE Command Stream 8: Mark Space |  | 00408084 |  |  |
| FE Command Stream 9: Mark Space |  | 00408094 |  |  |
| FE Command Stream 10: Mark Space |  | 004080A4 |  |  |
| FE Command Stream 11: Mark Space |  | 004080B4 |  |  |
| FE Command Stream 12: Mark Space |  | 00408104 |  |  |
| FE Command Stream 13: Mark Space |  | 00408114 |  |  |
| FE Command Stream 14: Mark Space |  | 00408124 |  |  |
| FE Command Stream 15: Mark Space |  | 00408134 |  |  |
| FE Command Stream 16: Mark Space |  | 00408144 |  |  |
| FE Command Stream 17: Mark Space |  | 00408154 |  |  |
| FE Command Stream 18: Mark Space |  | 00408164 |  |  |
| FE Command Stream 19: Mark Space |  | 00408174 |  |  |
| FE Command Stream 20: Mark Space |  | 00408184 |  |  |
| FE Command Stream 21: Mark Space |  | 00408194 |  |  |
| FE Command Stream 22: Mark Space |  | 004081A4 |  |  |
| FE Command Stream 23: Mark Space |  | 004081B4 |  |  |
| FE Command Stream 24: Mark Space |  | 00408204 |  |  |
| FE Command Stream 25: Mark Space |  | 00408214 |  |  |
| FE Command Stream 26: Mark Space |  | 00408224 |  |  |
| FE Command Stream 27: Mark Space |  | 00408234 |  |  |
| FE Command Stream 28: Mark Space |  | 00408244 |  |  |
| FE Command Stream 29: Mark Space |  | 00408254 |  |  |
| FE Command Stream 30: Mark Space |  | 00408264 |  |  |
| FE Command Stream 31: Mark Space |  | 00408274 |  |  |
| FE Command Stream 32: Mark Space |  | 00408284 |  |  |
| FE Command Stream 33: Mark Space |  | 00408294 |  |  |
| FE Command Stream 34: Mark Space |  | 004082A4 |  |  |
| FE Command Stream 35: Mark Space |  | 004082B4 |  |  |
| FE Command Stream 36: Mark Space |  | 00408304 |  |  |
| FE Command Stream 37: Mark Space |  | 00408314 |  |  |
| FE Command Stream 38: Mark Space |  | 00408324 |  |  |
| FE Command Stream 39: Mark Space |  | 00408334 |  |  |
| FE Command Stream 40: Mark Space |  | 00408344 |  |  |
| FE Command Stream 41: Mark Space |  | 00408354 |  |  |
| FE Command Stream 42: Mark Space |  | 00408364 |  |  |
| FE Command Stream 43: Mark Space |  | 00408374 |  |  |
| FE Command Stream 44: Mark Space |  | 00408384 |  |  |
| FE Command Stream 45: Mark Space |  | 00408394 |  |  |
| FE Command Stream 46: Mark Space |  | 004083A4 |  |  |
| FE Command Stream 47: Mark Space |  | 004083B4 |  |  |
|  | Bit Value |
| Bits[4:0]: Mark Space (Reset Value = 0x13 /~50%) | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| FE Command Stream 0: Coarse Delay |  | 004080084 | RW | 5 |
| FE Command Stream 1: Coarse Delay |  | 004080184 |  |  |
| FE Command Stream 2: Coarse Delay |  | 004080284 |  |  |
| FE Command Stream 3: Coarse Delay |  | 00408038 |  |  |
| FE Command Stream 4: Coarse Delay |  | 004080484 |  |  |
| FE Command Stream 5: Coarse Delay |  | 004080584 |  |  |
| FE Command Stream 6: Coarse Delay |  | 004080684 |  |  |
| FE Command Stream 7: Coarse Delay |  | 004080784 |  |  |
| FE Command Stream 8: Coarse Delay |  | 004080884 |  |  |
| FE Command Stream 9: Coarse Delay |  | 004080984 |  |  |
| FE Command Stream 10: Coarse Delay |  | 004080A84 |  |  |
| FE Command Stream 11: Coarse Delay |  | 004080B84 |  |  |
| FE Command Stream 12: Coarse Delay |  | 004081084 |  |  |
| FE Command Stream 13: Coarse Delay |  | 004081184 |  |  |
| FE Command Stream 14: Coarse Delay |  | 004081284 |  |  |
| FE Command Stream 15: Coarse Delay |  | 004081384 |  |  |
| FE Command Stream 16: Coarse Delay |  | 004081484 |  |  |
| FE Command Stream 17: Coarse Delay |  | 004081584 |  |  |
| FE Command Stream 18: Coarse Delay |  | 004081684 |  |  |
| FE Command Stream 19: Coarse Delay |  | 004081784 |  |  |
| FE Command Stream 20: Coarse Delay |  | 004081884 |  |  |
| FE Command Stream 21: Coarse Delay |  | 004081984 |  |  |
| FE Command Stream 22: Coarse Delay |  | 004081A84 |  |  |
| FE Command Stream 23: Coarse Delay |  | 004081B84 |  |  |
| FE Command Stream 24: Coarse Delay |  | 004082084 |  |  |
| FE Command Stream 25: Coarse Delay |  | 004082184 |  |  |
| FE Command Stream 26: Coarse Delay |  | 004082284 |  |  |
| FE Command Stream 27: Coarse Delay |  | 004082384 |  |  |
| FE Command Stream 28: Coarse Delay |  | 004082484 |  |  |
| FE Command Stream 29: Coarse Delay |  | 004082584 |  |  |
| FE Command Stream 30: Coarse Delay |  | 004082684 |  |  |
| FE Command Stream 31: Coarse Delay |  | 004082784 |  |  |
| FE Command Stream 32: Coarse Delay |  | 004082884 |  |  |
| FE Command Stream 33: Coarse Delay |  | 004082984 |  |  |
| FE Command Stream 34: Coarse Delay |  | 004082A84 |  |  |
| FE Command Stream 35: Coarse Delay |  | 004082B84 |  |  |
| FE Command Stream 36: Coarse Delay |  | 004083084 |  |  |
| FE Command Stream 37: Coarse Delay |  | 004083184 |  |  |
| FE Command Stream 38: Coarse Delay |  | 004083284 |  |  |
| FE Command Stream 39: Coarse Delay |  | 004083384 |  |  |
| FE Command Stream 40: Coarse Delay |  | 004083484 |  |  |
| FE Command Stream 41: Coarse Delay |  | 004083584 |  |  |
| FE Command Stream 42: Coarse Delay |  | 004083684 |  |  |
| FE Command Stream 43: Coarse Delay |  | 004083784 |  |  |
| FE Command Stream 44: Coarse Delay |  | 004083884 |  |  |
| FE Command Stream 45: Coarse Delay |  | 004083984 |  |  |
| FE Command Stream 46: Coarse Delay |  | 004083A84 |  |  |
| FE Command Stream 47: Coarse Delay |  | 004083B84 |  |  |
| Value that determines the coarse timing delay of the FE Command signal in 25 nsec steps (775 nsec maximum) | Bit Value |
| Bits[4:0]: Coarse Delay (Reset Value = 0) | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| FE Command Stream 0: Fine Delay |  | 0040800C84 | RW | 7 |
| FE Command Stream 1: Fine Delay |  | 0040801C84 |  |  |
| FE Command Stream 2: Fine Delay |  | 0040802C84 |  |  |
| FE Command Stream 3: Fine Delay |  | 0040803C8 |  |  |
| FE Command Stream 4: Fine Delay |  | 0040804C84 |  |  |
| FE Command Stream 5: Fine Delay |  | 0040805C84 |  |  |
| FE Command Stream 6: Fine Delay |  | 0040806C84 |  |  |
| FE Command Stream 7: Fine Delay |  | 0040807C84 |  |  |
| FE Command Stream 8: Fine Delay |  | 0040808C84 |  |  |
| FE Command Stream 9: Fine Delay |  | 0040809C84 |  |  |
| FE Command Stream 10: Fine Delay |  | 004080AC84 |  |  |
| FE Command Stream 11: Fine Delay |  | 004080BC84 |  |  |
| FE Command Stream 12: Fine Delay |  | 0040810C84 |  |  |
| FE Command Stream 13: Fine Delay |  | 0040811C84 |  |  |
| FE Command Stream 14: Fine Delay |  | 0040812C84 |  |  |
| FE Command Stream 15: Fine Delay |  | 0040813C84 |  |  |
| FE Command Stream 16: Fine Delay |  | 0040814C84 |  |  |
| FE Command Stream 17: Fine Delay |  | 0040815C84 |  |  |
| FE Command Stream 18: Fine Delay |  | 0040816C84 |  |  |
| FE Command Stream 19: Fine Delay |  | 0040817C84 |  |  |
| FE Command Stream 20: Fine Delay |  | 0040818C84 |  |  |
| FE Command Stream 21: Fine Delay |  | 0040819C84 |  |  |
| FE Command Stream 22: Fine Delay |  | 004081AC84 |  |  |
| FE Command Stream 23: Fine Delay |  | 004081BC84 |  |  |
| FE Command Stream 24: Fine Delay |  | 0040820C84 |  |  |
| FE Command Stream 25: Fine Delay |  | 0040821C84 |  |  |
| FE Command Stream 26: Fine Delay |  | 0040822C84 |  |  |
| FE Command Stream 27: Fine Delay |  | 0040823C84 |  |  |
| FE Command Stream 28: Fine Delay |  | 0040824C84 |  |  |
| FE Command Stream 29: Fine Delay |  | 0040825C84 |  |  |
| FE Command Stream 30: Fine Delay |  | 0040826C84 |  |  |
| FE Command Stream 31: Fine Delay |  | 0040827C84 |  |  |
| FE Command Stream 32: Fine Delay |  | 0040828C84 |  |  |
| FE Command Stream 33: Fine Delay |  | 0040829C84 |  |  |
| FE Command Stream 34: Fine Delay |  | 004082AC84 |  |  |
| FE Command Stream 35: Fine Delay |  | 004082BC84 |  |  |
| FE Command Stream 36: Fine Delay |  | 0040830C84 |  |  |
| FE Command Stream 37: Fine Delay |  | 0040831C84 |  |  |
| FE Command Stream 38: Fine Delay |  | 0040832C84 |  |  |
| FE Command Stream 39: Fine Delay |  | 0040833C84 |  |  |
| FE Command Stream 40: Fine Delay |  | 0040834C84 |  |  |
| FE Command Stream 41: Fine Delay |  | 0040835C84 |  |  |
| FE Command Stream 42: Fine Delay |  | 0040836C84 |  |  |
| FE Command Stream 43: Fine Delay |  | 0040837C84 |  |  |
| FE Command Stream 44: Fine Delay |  | 0040838C84 |  |  |
| FE Command Stream 45: Fine Delay |  | 0040839C84 |  |  |
| FE Command Stream 46: Fine Delay |  | 004083AC84 |  |  |
| FE Command Stream 47: Fine Delay |  | 004083BC84 |  |  |
| Value that determines the fine timing delay of the FE Command signal in 280 psec steps (35 nsec maximum) | Bit Value |
| Bits[6:0]: Fine Delay (Reset Value = 0) | Value |

## BPM Laser BPM Test Structure Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| BPM12 Test Structures: 1st BPM12, channel 12 |  | 004080C0 | RW | 8 |
|  | Bit Value |
| Bits[7:0]: Must be set to 0x20 for proper operation of BPM12 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| BPM12 Test Structures: 1st BPM12, channel 13 |  | 004080D0 | RW | 8 |
|  | Bit Value |
| Bits[7:0]: Must be set to 0x40 for proper operation of BPM12 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| BPM12 Test Structures: 2nd BPM12, channel 12 |  | 004081C0 | RW | 8 |
|  | Bit Value |
| Bits[7:0]: Must be set to 0x20 for proper operation of BPM12 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| BPM12 Test Structures: 2nd BPM12, channel 13 |  | 004081D0 | RW | 8 |
|  | Bit Value |
| Bits[7:0]: Must be set to 0x40 for proper operation of BPM12 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| BPM12 Test Structures: 3rd BPM12, channel 12 |  | 004082C0 | RW | 8 |
|  | Bit Value |
| Bits[7:0]: Must be set to 0x20 for proper operation of BPM12 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| BPM12 Test Structures: 3rd BPM12, channel 13 |  | 004082D0 | RW | 8 |
|  | Bit Value |
| Bits[7:0]: Must be set to 0x40 for proper operation of BPM12 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| BPM12 Test Structures: 4th BPM12, channel 12 |  | 004083C0 | RW | 8 |
|  | Bit Value |
| Bits[7:0]: Must be set to 0x20 for proper operation of BPM12 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| BPM12 Test Structures: 4th BPM12, channel 13 |  | 004083D0 | RW | 8 |
|  | Bit Value |
| Bits[7:0]: Must be set to 0x40 for proper operation of BPM12 | Value |

## FE Command Laser Current DAC Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| FE Command Stream 0: Laser Current DAC |  | 0040860084 | RW | 8 |
| FE Command Stream 1: Laser Current DAC |  | 00408604 |  |  |
| FE Command Stream 2: Laser Current DAC |  | 00408608 |  |  |
| FE Command Stream 3: Laser Current DAC |  | 0040860C |  |  |
| FE Command Stream 4: Laser Current DAC |  | 00408610084 |  |  |
| FE Command Stream 5: Laser Current DAC |  | 004086104 |  |  |
| FE Command Stream 6: Laser Current DAC |  | 004086108 |  |  |
| FE Command Stream 7: Laser Current DAC |  | 00408610C |  |  |
| FE Command Stream 8: Laser Current DAC |  | 00408620084 |  |  |
| FE Command Stream 9: Laser Current DAC |  | 004086204 |  |  |
| FE Command Stream 10: Laser Current DAC |  | 004086208 |  |  |
| FE Command Stream 11: Laser Current DAC |  | 00408620C |  |  |
| FE Command Stream 12: Laser Current DAC |  | 00408630084 |  |  |
| FE Command Stream 13: Laser Current DAC |  | 004086304 |  |  |
| FE Command Stream 14: Laser Current DAC |  | 004086308 |  |  |
| FE Command Stream 15: Laser Current DAC |  | 00408630C |  |  |
| FE Command Stream 16: Laser Current DAC |  | 00408640084 |  |  |
| FE Command Stream 17: Laser Current DAC |  | 004086404 |  |  |
| FE Command Stream 18: Laser Current DAC |  | 004086408 |  |  |
| FE Command Stream 19: Laser Current DAC |  | 00408640C |  |  |
| FE Command Stream 20: Laser Current DAC |  | 00408650084 |  |  |
| FE Command Stream 21: Laser Current DAC |  | 004086504 |  |  |
| FE Command Stream 22: Laser Current DAC |  | 004086508 |  |  |
| FE Command Stream 23: Laser Current DAC |  | 00408650C |  |  |
| FE Command Stream 24: Laser Current DAC |  | 00408660084 |  |  |
| FE Command Stream 25: Laser Current DAC |  | 004086604 |  |  |
| FE Command Stream 26: Laser Current DAC |  | 004086608 |  |  |
| FE Command Stream 27: Laser Current DAC |  | 00408660C |  |  |
| FE Command Stream 28: Laser Current DAC |  | 00408670084 |  |  |
| FE Command Stream 29: Laser Current DAC |  | 004086704 |  |  |
| FE Command Stream 30: Laser Current DAC |  | 004086708 |  |  |
| FE Command Stream 31: Laser Current DAC |  | 00408670C |  |  |
| FE Command Stream 32: Laser Current DAC |  | 00408680084 |  |  |
| FE Command Stream 33: Laser Current DAC |  | 004086804 |  |  |
| FE Command Stream 34: Laser Current DAC |  | 004086808 |  |  |
| FE Command Stream 35: Laser Current DAC |  | 00408680C |  |  |
| FE Command Stream 36: Laser Current DAC |  | 00408690084 |  |  |
| FE Command Stream 37: Laser Current DAC |  | 004086904 |  |  |
| FE Command Stream 38: Laser Current DAC |  | 004086908 |  |  |
| FE Command Stream 39: Laser Current DAC |  | 00408690C |  |  |
| FE Command Stream 40: Laser Current DAC |  | 004086A0084 |  |  |
| FE Command Stream 41: Laser Current DAC |  | 004086A04 |  |  |
| FE Command Stream 42: Laser Current DAC |  | 004086A08 |  |  |
| FE Command Stream 43: Laser Current DAC |  | 004086A0C |  |  |
| FE Command Stream 44: Laser Current DAC |  | 004086B0084 |  |  |
| FE Command Stream 45: Laser Current DAC |  | 004086B04 |  |  |
| FE Command Stream 46: Laser Current DAC |  | 004086B08 |  |  |
| FE Command Stream 47: Laser Current DAC |  | 004086B0C |  |  |
| Value that determines the current out of the Laser Current DAC | Bit Value |
| Bits[7:0]: Laser Current Value | Value |

## FE Link Input Data Delay Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Input Link 0: Data Delay |  | 00408800 | RW | 5 |
| Input Link 1: Data Delay |  | 00408804 |  |  |
| Input Link 2: Data Delay |  | 00408808 |  |  |
| Input Link 3: Data Delay |  | 0040880C |  |  |
| Input Link 4: Data Delay |  | 004088100 |  |  |
| Input Link 5: Data Delay |  | 00408814 |  |  |
| Input Link 6: Data Delay |  | 00408818 |  |  |
| Input Link 7: Data Delay |  | 0040881C |  |  |
| Input Link 8: Data Delay |  | 00408820 |  |  |
| Input Link 9: Data Delay |  | 00408824 |  |  |
| Input Link 10: Data Delay |  | 00408828 |  |  |
| Input Link 11: Data Delay |  | 0040882C |  |  |
| Input Link 12: Data Delay |  | 00408830 |  |  |
| Input Link 13: Data Delay |  | 00408834 |  |  |
| Input Link 14: Data Delay |  | 00408838 |  |  |
| Input Link 15: Data Delay |  | 0040883C |  |  |
| Input Link 16: Data Delay |  | 00408840 |  |  |
| Input Link 17: Data Delay |  | 00408844 |  |  |
| Input Link 18: Data Delay |  | 00408848 |  |  |
| Input Link 19: Data Delay |  | 0040884C |  |  |
| Input Link 20: Data Delay |  | 00408850 |  |  |
| Input Link 21: Data Delay |  | 00408854 |  |  |
| Input Link 22: Data Delay |  | 00408858 |  |  |
| Input Link 23: Data Delay |  | 0040885C |  |  |
| Input Link 24: Data Delay |  | 00408860 |  |  |
| Input Link 25: Data Delay |  | 00408864 |  |  |
| Input Link 26: Data Delay |  | 00408868 |  |  |
| Input Link 27: Data Delay |  | 0040886C |  |  |
| Input Link 28: Data Delay |  | 00408870 |  |  |
| Input Link 29: Data Delay |  | 00408874 |  |  |
| Input Link 30: Data Delay |  | 00408878 |  |  |
| Input Link 31: Data Delay |  | 0040887C |  |  |
| Input Link 32: Data Delay |  | 00408880 |  |  |
| Input Link 33: Data Delay |  | 00408884 |  |  |
| Input Link 34: Data Delay |  | 00408888 |  |  |
| Input Link 35: Data Delay |  | 0040888C |  |  |
| Input Link 36: Data Delay |  | 00408890 |  |  |
| Input Link 37: Data Delay |  | 00408894 |  |  |
| Input Link 38: Data Delay |  | 00408898 |  |  |
| Input Link 39: Data Delay |  | 0040889C |  |  |
| Input Link 40: Data Delay |  | 004088A0 |  |  |
| Input Link 41: Data Delay |  | 004088A4 |  |  |
| Input Link 42: Data Delay |  | 004088A8 |  |  |
| Input Link 43: Data Delay |  | 004088AC |  |  |
| Input Link 44: Data Delay |  | 004088B0 |  |  |
| Input Link 45: Data Delay |  | 004088B4 |  |  |
| Input Link 46: Data Delay |  | 004088B8 |  |  |
| Input Link 47: Data Delay |  | 004088BC |  |  |
|  | Bit Value |
| Bits[4:0]: Data Delay Value | Delay in ns |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Input Link 48: Data Delay |  | 004088C0 | RW | 5 |
| Input Link 49: Data Delay |  | 004088C4 |  |  |
| Input Link 50: Data Delay |  | 004088C8 |  |  |
| Input Link 51: Data Delay |  | 004088CC |  |  |
| Input Link 52: Data Delay |  | 004088D0 |  |  |
| Input Link 53: Data Delay |  | 004088D4 |  |  |
| Input Link 54: Data Delay |  | 004088D8 |  |  |
| Input Link 55: Data Delay |  | 004088DC |  |  |
| Input Link 56: Data Delay |  | 004088E0 |  |  |
| Input Link 57: Data Delay |  | 004088E4 |  |  |
| Input Link 58: Data Delay |  | 004088E8 |  |  |
| Input Link 59: Data Delay |  | 004088EC |  |  |
| Input Link 60: Data Delay |  | 004088F0 |  |  |
| Input Link 61: Data Delay |  | 004088F4 |  |  |
| Input Link 62: Data Delay |  | 004088F8 |  |  |
| Input Link 63: Data Delay |  | 004088FC |  |  |
| Input Link 64: Data Delay |  | 00408900 |  |  |
| Input Link 65: Data Delay |  | 00408904 |  |  |
| Input Link 66: Data Delay |  | 00408908 |  |  |
| Input Link 67: Data Delay |  | 0040890C |  |  |
| Input Link 68: Data Delay |  | 00408910 |  |  |
| Input Link 69: Data Delay |  | 00408914 |  |  |
| Input Link 70: Data Delay |  | 00408918 |  |  |
| Input Link 71: Data Delay |  | 0040891C |  |  |
| Input Link 72: Data Delay |  | 00408920 |  |  |
| Input Link 73: Data Delay |  | 00408924 |  |  |
| Input Link 74: Data Delay |  | 00408928 |  |  |
| Input Link 75: Data Delay |  | 0040892C |  |  |
| Input Link 76: Data Delay |  | 00408930 |  |  |
| Input Link 77: Data Delay |  | 00408934 |  |  |
| Input Link 78: Data Delay |  | 00408938 |  |  |
| Input Link 79: Data Delay |  | 0040893C |  |  |
| Input Link 80: Data Delay |  | 00408940 |  |  |
| Input Link 81: Data Delay |  | 00408944 |  |  |
| Input Link 82: Data Delay |  | 00408948 |  |  |
| Input Link 83: Data Delay |  | 0040894C |  |  |
| Input Link 84: Data Delay |  | 00408950 |  |  |
| Input Link 85: Data Delay |  | 00408954 |  |  |
| Input Link 86: Data Delay |  | 00408958 |  |  |
| Input Link 87: Data Delay |  | 0040895C |  |  |
| Input Link 88: Data Delay |  | 00408960 |  |  |
| Input Link 89: Data Delay |  | 00408964 |  |  |
| Input Link 90: Data Delay |  | 00408968 |  |  |
| Input Link 91: Data Delay |  | 0040896C |  |  |
| Input Link 92: Data Delay |  | 00408970 |  |  |
| Input Link 93: Data Delay |  | 00408974 |  |  |
| Input Link 94: Data Delay |  | 00408978 |  |  |
| Input Link 95: Data Delay |  | 0040897C |  |  |
|  | Bit Value |
| Bits[4:0]: Data Delay Value | Delay in ns |

## BPM Clock Phase and Vernier Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| BPM Clock Phase |  | 00408980 | RW | 8 |
|  | Bit Value |
| Bits[7:0]: | Delay |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| B-Reg Clock Phase |  | 0040898C | RW | 8 |
|  | Bit Value |
| Bits[7:0]: | Delay |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Vernier Clock Step Phase0 |  | 00408990 | RW | 5 |
| This and the following register are in series, giving a delay of 0-50 nsec | Bit Value |
| Bits[4:0]: Clock Delay Value | Delay in ns |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Vernier Clock Step Phase1 |  | 00408994 | RW | 5 |
| This and the previous register are in series, giving a delay of 0-50 nsec | Bit Value |
| Bits[4:0]: Clock Delay Value | Delay in ns |

## Strobe Delay Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Strobe Delay 0 |  | 00408A00 | RW | 1 |
| Strobe Delay 1 |  | 00408A10 |  |  |
| Strobe Delay 2 |  | 00408A20 |  |  |
| Strobe Delay 3 |  | 00408A30 |  |  |
| Strobe Delay 4 |  | 00408A40 |  |  |
| Strobe Delay 5 |  | 00408A50 |  |  |
| Strobe Delay 6 |  | 00408A60 |  |  |
| Strobe Delay 7 |  | 00408A70 |  |  |
| Strobe Delay 8 |  | 00408A80 |  |  |
| Strobe Delay 9 |  | 00408A90 |  |  |
| Strobe Delay 10 |  | 00408AA0 |  |  |
| Strobe Delay 11 |  | 00408AB0 |  |  |
| Strobe Delay 12 |  | 00408AC0 |  |  |
| Strobe Delay 13 |  | 00408AD0 |  |  |
| Strobe Delay 14 |  | 00408AE0 |  |  |
| Strobe Delay 15 |  | 00408AF0 |  |  |
| Strobe Delay 16 |  | 00408B00 |  |  |
| Strobe Delay 17 |  | 00408B10 |  |  |
| Strobe Delay 18 |  | 00408B20 |  |  |
| Strobe Delay 19 |  | 00408B30 |  |  |
| Strobe Delay 20 |  | 00408B40 |  |  |
| Strobe Delay 21 |  | 00408B50 |  |  |
| Strobe Delay 22 |  | 00408B60 |  |  |
| Strobe Delay 23 |  | 00408B70 |  |  |
| Strobe Delay 24 |  | 00408B80 |  |  |
| Strobe Delay 25 |  | 00408B90 |  |  |
| Adds a delay to the clock output from PHOS4 chip | Bit Value |
| Bits[4:0]: Clock Delay Value | Delay in ns |

## FE Link Input RX DAC Threshold Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Input Link 0: RX DAC Threshold |  | 00408C00 | RW | 8 |
| Input Link 1: RX DAC Threshold |  | 00408C04 |  |  |
| Input Link 2: RX DAC Threshold |  | 00408C08 |  |  |
| Input Link 3: RX DAC Threshold |  | 00408C0C |  |  |
| Input Link 4: RX DAC Threshold |  | 00408C10 |  |  |
| Input Link 5: RX DAC Threshold |  | 00408C14 |  |  |
| Input Link 6: RX DAC Threshold |  | 00408C18 |  |  |
| Input Link 7: RX DAC Threshold |  | 00408C1C |  |  |
| Input Link 8: RX DAC Threshold |  | 00408C20 |  |  |
| Input Link 9: RX DAC Threshold |  | 00408C24 |  |  |
| Input Link 10: RX DAC Threshold |  | 00408C28 |  |  |
| Input Link 11: RX DAC Threshold |  | 00408C2C |  |  |
| Input Link 12: RX DAC Threshold |  | 00408C30 |  |  |
| Input Link 13: RX DAC Threshold |  | 00408C34 |  |  |
| Input Link 14: RX DAC Threshold |  | 00408C38 |  |  |
| Input Link 15: RX DAC Threshold |  | 00408C3C |  |  |
| Input Link 16: RX DAC Threshold |  | 00408C40 |  |  |
| Input Link 17: RX DAC Threshold |  | 00408C44 |  |  |
| Input Link 18: RX DAC Threshold |  | 00408C48 |  |  |
| Input Link 19: RX DAC Threshold |  | 00408C4C |  |  |
| Input Link 20: RX DAC Threshold |  | 00408C50 |  |  |
| Input Link 21: RX DAC Threshold |  | 00408C54 |  |  |
| Input Link 22: RX DAC Threshold |  | 00408C58 |  |  |
| Input Link 23: RX DAC Threshold |  | 00408C5C |  |  |
| Input Link 24: RX DAC Threshold |  | 00408C60 |  |  |
| Input Link 25: RX DAC Threshold |  | 00408C64 |  |  |
| Input Link 26: RX DAC Threshold |  | 00408C68 |  |  |
| Input Link 27: RX DAC Threshold |  | 00408C6C |  |  |
| Input Link 28: RX DAC Threshold |  | 00408C70 |  |  |
| Input Link 29: RX DAC Threshold |  | 00408C74 |  |  |
| Input Link 30: RX DAC Threshold |  | 00408C78 |  |  |
| Input Link 31: RX DAC Threshold |  | 00408C7C |  |  |
| Input Link 32: RX DAC Threshold |  | 00408C80 |  |  |
| Input Link 33: RX DAC Threshold |  | 00408C84 |  |  |
| Input Link 34: RX DAC Threshold |  | 00408C88 |  |  |
| Input Link 35: RX DAC Threshold |  | 00408C8C |  |  |
| Input Link 36: RX DAC Threshold |  | 00408C90 |  |  |
| Input Link 37: RX DAC Threshold |  | 00408C94 |  |  |
| Input Link 38: RX DAC Threshold |  | 00408C98 |  |  |
| Input Link 39: RX DAC Threshold |  | 00408C9C |  |  |
| Input Link 40: RX DAC Threshold |  | 00408CA0 |  |  |
| Input Link 41: RX DAC Threshold |  | 00408CA4 |  |  |
| Input Link 42: RX DAC Threshold |  | 00408CA8 |  |  |
| Input Link 43: RX DAC Threshold |  | 00408CAC |  |  |
| Input Link 44: RX DAC Threshold |  | 00408CB0 |  |  |
| Input Link 45: RX DAC Threshold |  | 00408CB4 |  |  |
| Input Link 46: RX DAC Threshold |  | 00408CB8 |  |  |
| Input Link 47: RX DAC Threshold |  | 00408CBC |  |  |
|  | Bit Value |
| Bits[7:0]: DAC Threshold setting | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Input Link 48: RX DAC Threshold |  | 00408CC0 | RW | 8 |
| Input Link 49: RX DAC Threshold |  | 00408CC4 |  |  |
| Input Link 50: RX DAC Threshold |  | 00408CC8 |  |  |
| Input Link 51: RX DAC Threshold |  | 00408CCC |  |  |
| Input Link 52: RX DAC Threshold |  | 00408CD0 |  |  |
| Input Link 53: RX DAC Threshold |  | 00408CD4 |  |  |
| Input Link 54: RX DAC Threshold |  | 00408CD8 |  |  |
| Input Link 55: RX DAC Threshold |  | 00408CDC |  |  |
| Input Link 56: RX DAC Threshold |  | 00408CE0 |  |  |
| Input Link 57: RX DAC Threshold |  | 00408CE4 |  |  |
| Input Link 58: RX DAC Threshold |  | 00408CE8 |  |  |
| Input Link 59: RX DAC Threshold |  | 00408CEC |  |  |
| Input Link 60: RX DAC Threshold |  | 00408CF0 |  |  |
| Input Link 61: RX DAC Threshold |  | 00408CF4 |  |  |
| Input Link 62: RX DAC Threshold |  | 00408CF8 |  |  |
| Input Link 63: RX DAC Threshold |  | 00408CFC |  |  |
| Input Link 64: RX DAC Threshold |  | 00408D00 |  |  |
| Input Link 65: RX DAC Threshold |  | 00408D04 |  |  |
| Input Link 66: RX DAC Threshold |  | 00408D08 |  |  |
| Input Link 67: RX DAC Threshold |  | 00408D0C |  |  |
| Input Link 68: RX DAC Threshold |  | 00408D10 |  |  |
| Input Link 69: RX DAC Threshold |  | 00408D14 |  |  |
| Input Link 70: RX DAC Threshold |  | 00408D18 |  |  |
| Input Link 71: RX DAC Threshold |  | 00408D1C |  |  |
| Input Link 72: RX DAC Threshold |  | 00408D20 |  |  |
| Input Link 73: RX DAC Threshold |  | 00408D24 |  |  |
| Input Link 74: RX DAC Threshold |  | 00408D28 |  |  |
| Input Link 75: RX DAC Threshold |  | 00408D2C |  |  |
| Input Link 76: RX DAC Threshold |  | 00408D30 |  |  |
| Input Link 77: RX DAC Threshold |  | 00408D34 |  |  |
| Input Link 78: RX DAC Threshold |  | 00408D38 |  |  |
| Input Link 79: RX DAC Threshold |  | 00408D3C |  |  |
| Input Link 80: RX DAC Threshold |  | 00408D40 |  |  |
| Input Link 81: RX DAC Threshold |  | 00408D44 |  |  |
| Input Link 82: RX DAC Threshold |  | 00408D48 |  |  |
| Input Link 83: RX DAC Threshold |  | 00408D4C |  |  |
| Input Link 84: RX DAC Threshold |  | 00408D50 |  |  |
| Input Link 85: RX DAC Threshold |  | 00408D54 |  |  |
| Input Link 86: RX DAC Threshold |  | 00408D58 |  |  |
| Input Link 87: RX DAC Threshold |  | 00408D5C |  |  |
| Input Link 88: RX DAC Threshold |  | 00408D60 |  |  |
| Input Link 89: RX DAC Threshold |  | 00408D64 |  |  |
| Input Link 90: RX DAC Threshold |  | 00408D68 |  |  |
| Input Link 91: RX DAC Threshold |  | 00408D6C |  |  |
| Input Link 92: RX DAC Threshold |  | 00408D70 |  |  |
| Input Link 93: RX DAC Threshold |  | 00408D74 |  |  |
| Input Link 94: RX DAC Threshold |  | 00408D78 |  |  |
| Input Link 95: RX DAC Threshold |  | 00408D7C |  |  |
|  | Bit Value |
| Bits[7:0]: DAC Threshold setting | Value |

## Monitoring ADC Setup Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Monitoring ADC Setup (SCT & PIXEL series cards only) Label: MON_SUP |  | 00408E00 | W | 8 |
| Write to this register to set up the monitoring ADC. Data written is ignored. | Bit Value |
| Bits[7:0]: | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Monitoring ADC Config (SCT & PIXEL series cards only) Label: MON_FIG |  | 00408E04 | W | 8 |
| Write to this register to set up the channel for the monitoring ADC to convert. Data written is the channel number. | Bit Value |
| Bits[7:0]: Channel Number | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Monitoring ADC Convert (SCT & PIXEL series cards only) Label: MON_CONV |  | 00408E08 | W | 8 |
| Write to this register to instruct the monitoring ADC to do a conversion. Data written is ignored. | Bit Value |
| Bits[7:0]: | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Spare Register (SCT & PIXEL series cards only) Label: MON_SPARE |  | 00408E0C | TBD | 8 |
| TBD. | Bit Value |
| Bits[7:0]: | TBD |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Monitoring ADC Data LSB (SCT & PIXEL series cards only) Label: MON_LSDAT |  | 00408E10 | R | 8 |
| Lowest eight bits from ADC conversion are held in this register. | Bit Value |
| Bits[7:0]: Data bits 0-7 | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Monitoring ADC Data MSB (SCT & PIXEL series cards only) Label: MON_MSDAT |  | 00408E14 | R | 2 or 4 |
| Top bits from ADC conversion are held in this register. Numbers of bits depend on hardware revision number (low 5 bits of Hardware Information register). Hardware revision = 0 uses 2 bits Hardware revision = 1 uses 4 bits | Bit Value |
| Bits[1:0]: Data bits 9-8 OR Bits:[3:0] Data bits 11-8 | Value |

## BOC Reset and Status and Miscellaneous Registers

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| BOC Resets (Series cards only – see individual reset registers below for pre-production cards) |  | 00408F00 | RW | 8 |
| Write 1 followed by 0 into the relevant bit of this register to reset the BOC function and then release the reset. | Bit Value |
|  | 1 | 0 |
| Bits[0:2] Unused | X |
| Bits[3:3] BOC_OK | Preset | Release |
| Bits[4:4] Vpin reset | Reset | Release |
| Bits[5:5] RX DAC Clear | Reset | Release |
| Bits[6:6] TX DAC Clear | Reset | Release |
| Bits[7:7] BPM Reset | Reset | Release |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| BPM Reset (Pre-production cards only – see BOC Resets Register for Series cards) |  | 00408F04 | RW | 1 |
| Write 1 followed by 0 into this register to reset the BPM12 chips and then release the reset. | Bit Value |
|  | 1 | 0 |
| Bits[0:0] | Reset | Release |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| TX DAC Clear (Pre-production cards only – see BOC Resets Register for Series cards) |  | 00408F08 | RW | 1 |
| Write 1 followed by 0 into this register to clear the TX DACs and release the clear signal. | Bit Value |
|  | 1 | 0 |
| Bits[0:0] | Clear | Release |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| RX DAC Clear (Pre-production cards only – see BOC Resets Register for Series cards) |  | 00408F0C | RW | 1 |
| Write 1 followed by 0 into this register to clear the RX DACs and release the clear signal. | Bit Value |
|  | 1 | 0 |
| Bits[0:0] | Clear | Release |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| BOC Status (Pre-production cards – see below for Series cards) |  | 00408F10 | R | 8 |
| Status of the BOC | Bit Value |
|  | 1 | 0 |
| Bit 0: SW1 on BOC (not used) | 0 |
| Bit 1: SW4 on BOC (on-board laser enable switch) | On | Off |
| Bit 2: SW5 on BOC (not used) | 0 |
| Bit 3: SW6 on BOC (not used) | 0 |
| Bit 4: Unused | 0 |
| Bit 5: RODSENSE | !Sense | Sense |
| Bit 6: Local Laser Enable | Enabled | Interlock |
| Bit 7: Remote Laser Enable | Enabled | Interlock |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| BOC Status (Series cards – see above for Pre-production cards). |  | 00408F10 | R | 8 |
| Status of the BOC | Bit Value |
|  | 1 | 0 |
| Bit 0: Unused | X |
| Bit 1: BOC_OK (latched) | OK | Not OK |
| Bit 2: Vb_OK | OK | Not OK |
| Bit 3: Va_OK | OK | Not OK |
| Bit 4: Err_flag | Error | No error |
| Bit 5: RODSENSE | !Sense | Sense |
| Bit 6: Local Laser Enable | Enabled | Interlock |
| Bit 7: Remote Laser Enable | Enabled | Interlock |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| RX Data Mode |  | 00408F14 | RW | 3 |
| Sets the data mode for the receiver side of the BOC. Normally set to 0 for SCT | Value |
| 0: | Normal SCT(B-reg) |
| 1: | SCT timing (B- & V-reg) |
| 2: | PIXEL LAYER 2 (40Mb/s) |
| 3: | PIXEL LAYER 1 & B (80Mb/s) |
| 4: | Reserved |
| 5: | Reserved |
| 6: | CLOCK as DATA |
| 7: | TRANSPARENT MODE |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Vernier Clock Fine Phase |  | 00408F20 | RW | 8 |
| Fine phase adjustment of the vernier clock | Value |
| Bits[7:0]: DAC setting | Delay in 40ps steps |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Clock Control (note variation between Rev C series BOC and other cards) |  | 00408F28 | RW | 5 |
| Control bits for the clock. Normally all bits are 0. The Half Clock Inhibit bit, if set, will stop the circuitry generating the 20MHz clock, even if the Half Clock bit is cleared (and hence the 20MHz clock is not in use). | Bit Value |
|  | 1 | 0 |
| Bit 0: Clock invert | Invert | Normal |
| Bit 1: Half Clock | Halve | Normal |
| Bit 2: Vernier bypass | Bypass | Normal |
| Bit 3: BPM bypass | Bypass | Normal |
| Bit 4: Phos4_fix (Series cards only) | Fix | Normal |
| Bit 5: Half Clock Inhibit (Rev C series cards only) | Inhibit | Enable |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Firmware revision |  | 00408F40 | R | 8 |
| Revision level of the firmware | Value |
| Bits[7:0]: Revision level | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Hardware information |  | 00408F44 | R | 8 |
| Revision level of the hardware. The information returned in this byte now separately identifies the PCB version (bits 5-7) and the hardware revision for that PCB version (bits 0-4). | Value |
| Bits[0:4] Hardware revision | Value |
| Bits[7:5] PCB version | 0 = pre-production 1 = series Rev A 2 = series Rev B 3 = series Rev C |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Module type |  | 00408F48 | R | 8 |
| Module type designation | Value |
| Bits[7:0]: Module type | Pre-production: 44 Series: 46 |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Manufacturer |  | 00408F4C | R | 8 |
| Manufacturer identification | Value |
| Bits[7:0]: Manufacturer | 0xCB |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Serial Number |  | 00408F60 | R | 8 |
| Module serial number – set by 2 HEX switches on the board | Value |
| Bits[7:0]: Serial Number | Value |

## Monitoring ADC Tables and Conversion Information: SCT Version

| Monitoring ADC (SCT series cards only): channel information |
| --- |
| Channel | Parameter | Formulae Rev A Rev B |
| 0 | PIN Current | Streams[0:11] | 1 | 4 |
| 1 | PIN Current | Streams[12:23] | 1 | 4 |
| 2 | PIN Current | Streams[24:35] | 1 | 4 |
| 3 | PIN Current | Streams[36:47] | 1 | 4 |
| 4 | PIN Current | Streams[48:59] | 1 | 4 |
| 5 | PIN Current | Streams[60:71] | 1 | 4 |
| 6 | PIN Current | Streams[72:83] | 1 | 4 |
| 7 | PIN Current | Streams[84:95] | 1 | 4 |
| 8 | PIN Voltage | Streams[0:47] | 2 | 5 |
| 9 | PIN Voltage | Streams[48:95] | 2 | 5 |
| 10 | Thermistor 1 | 3 | 6 |
| 11 | Thermistor 2 | 3 | 6 |

| Formulae to convert ADC reading to true value |
| --- |
| Board Revision | Formula Number Form | Parameter Values A B | Range Max | Nominal Value |
| Rev A | 1 | A+B*Reading | 41.52mA | -0.04051 mA/count | 41.52 mA |  |
|  | 2 | A+B*Reading | 0.0mV | 11.106 mV/count | 11.36 V | 8.42V |
|  | 3 | RTherm=A*((B/Reading)-1) | 10000 Ohm | 1023 |  | 10k Ohm@ 25C |
| Rev B | 4 | A+B*Reading | 0.0mA | 0.02383 mA/count | 23.375 mA |  |
|  | 5 | A+B*Reading | 0.0mV | 14.494 mV/count | 14.83 V | 9.78V |
|  | 6 | RTherm=A*((B/Reading)-1) | 10000 Ohm | 1023 |  | 10kOhm @25C |

| Converting RTherm to Temperature |
| --- |
| Thermistor used: | ATC Semitec 103KT1608 to VADC with 10k to ground |
| Steinhart-Hart Formula: | 1/T(Kelvin) = C0 + C1*ln(RTherm) + C3*(ln(RTherm))**3 |
| Parameters optimized over 20-100C | Rev A | C0 | 7.4717E-04 |
|  |  | C1 | 2.7726E-04 |
|  |  | C3 | 6.8388E-08 |
|  | Rev B | C4 | 7.4717E-04 |
|  |  | C5 | 2.7726E-04 |
|  |  | C6 | 6.8388E-08 |

## Monitoring ADC Tables and Conversion Information: PIXEL Version

| Monitoring ADC (PIXEL series cards only): channel information |
| --- |
| Channel | Parameter | Formulae Rev A Rev B & C |
| 0 | PIN Current | Streams[0:11] | 1 | 4 |
| 1 | PIN Voltage | Streams[12:23] | 1 | 4 |
| 2 | PIN Voltage | Streams[24:35] | 1 | 4 |
| 3 | PIN Current | Streams[36:47] | 1 | 4 |
| 4 | PIN Current | Streams[48:59] | 1 | 4 |
| 5 | PIN Voltage | Streams[60:71] | 1 | 4 |
| 6 | PIN Voltage | Streams[72:83] | 1 | 4 |
| 7 | PIN Current | Streams[84:95] | 1 | 4 |
| 8 | PIN Voltage | Streams[0:47] | 2 | 5 |
| 9 | PIN Voltage | Streams[48:95] | 2 | 5 |
| 10 | Thermistor 1 | 3 | 6 |
| 11 | Thermistor 2 | 3 | 6 |

| Formulae to convert ADC reading to true value |
| --- |
| Board Revision | Formula Number Form | Parameter Values K M | Range Max | Nominal Value |
| Rev A | 1 | K+M*Reading | 41.52 mA | -10.147 uA/ct | 41.52 mA |  |
|  | 2 | M*Reading | 0.0 mV | 2.777 mV/ct | 11.36 V | 8.42 V |
|  | 3 | RTherm=K*((M/Reading)-1) | 10000 Ohm | 4095 |  | 10k @ 25C |
| Rev B & Rev C | 4 | K+M*Reading | -97 uA | 5.958 uA/ct | 24.375 mA |  |
|  | 5 | M*Reading | 0.0mV | 3.623 mV/ct | 14.83 V | 9.78V |
|  | 6 | RTherm=K*((M/Reading)-1) | 10000 Ohm | 4095 |  | 10k @ 25C |

| Converting RTherm to Temperature |
| --- |
| Thermistor used: | ATC Semitec 103KT1608 to VADC with 10k to ground |
| Steinhart-Hart Formula: | 1/T(Kelvin) = C0 + C1*ln(RTherm) + C3*(ln(RTherm))**3 |
| Parameters optimized over 20-100C | Rev A | C0 | 7.4717E-04 |
|  |  | C1 | 2.7726E-04 |
|  |  | C3 | 6.8388E-08 |
|  | Rev B & C | C4 | 7.4717E-04 |
|  |  | C5 | 2.7726E-04 |
|  |  | C6 | 6.8388E-08 |

# ROD Slave DSP HPI Registers

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Slave DSP 0: HPIC, Host Port Interface Control Register | 00780000 | RW | 32 |
| Slave DSP 1: HPIC, Host Port Interface Control Register | 007A0000 | RW | 32 |
| Slave DSP 2: HPIC, Host Port Interface Control Register | 007C0000 | RW | 32 |
| Slave DSP 3: HPIC, Host Port Interface Control Register | 007E0000 | RW | 32 |
| The HPIC register is normally the first register accessed to set configuration bits and initialize the interface. The HPIC is organized as a 32-bit register whose high half word and low half word contents are the same. On a host write, both half words must be identical. The lower half word is the write register, and the upper half word is the status register. No storage is allocated for the read-only reserved values. Only CPU writes to the lower half word affect HPIC values and HPI operation. | Bit Value |
|  | 1 | 0 |
| Bit[0]: HWOB – Read Only, see definition in bit 16 | FHW->LSW | FHW->MSW |
| Bit[1]: DSPINT - Read Only, see definition in bit 17 | INT | IDLE |
| Bit[2]: HINT - Read Only, see definition in bit 18 | HINT=0 | HINT=1 |
| Bit[3]: HRDY - Read Only, see definition in bit 19 | Ready | Busy |
| Bit[4]: FETCH - Read Only, see definition in bit 20 | Request | Idle |
| Bits[15:5]: Reserved | Not Used |
| Bit[16]: HWOB - If HWOB = 1, the first half word is least significant. If HWOB = 0, the first half word is most significant. HWOB affects both data and address transfers. Only the host can modify this bit. HWOB must be initialized before the first data or address register access. | FHW->LSW | FHW->MSW |
| Bit[17]: DSPINT – The host processor-to-CPU/DMA interrupt | INT | IDLE |
| Bit[18]: HINT - DSP-to-Host Interrupt. The inverted value of this bit determines the state of the CPU HINT output | HINT=0 | HINT=1 |
| Bit[19]: HRDY – Ready Signal to Host. If HRDY = 0, the internal bus is waiting for an HPI data access request to finish | Ready | Busy |
| Bit[20]: FETCH – Host Fetch Request. The value read by the host or CPU from this register field is always 0. The host writes a 1 to this bit to request a fetch into HPID of the word at the address pointed to by HPIA. The 1 is never actually written to this bit, however. | Fetch Request | Idle |
| Bits[31:21]: Reserved | Not Used |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Slave DSP 0: HPIA, Host Port Interface Address Register | 00780004 | RW | 32 |
| Slave DSP 1: HPIA, Host Port Interface Address Register | 007A0004 | RW | 32 |
| Slave DSP 2: HPIA, Host Port Interface Address Register | 007C0004 | RW | 32 |
| Slave DSP 3: HPIA, Host Port Interface Address Register | 007E0004 | RW | 32 |
| The HPIA contains the address of the memory accessed by the HPI at which the current access occurs. This address is a 30-bit word address, so the two LSBs are unaffected by HPIA writes and are always read as 0. The C62x/C67x HPIA register is only accessible by the host. It is not mapped to the DSP memory. | Bit Value |
| Bits[31: 0]: HPIA | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Slave DSP 0: HPID++, Host Port Interface Data Register w/Auto Inc | 00780008 | RW | 32 |
| Slave DSP 1: HPID++, Host Port Interface Data Register w/Auto Inc | 007A0008 | RW | 32 |
| Slave DSP 2: HPID++, Host Port Interface Data Register w/Auto Inc | 007C0008 | RW | 32 |
| Slave DSP 3: HPID++, Host Port Interface Data Register w/Auto Inc | 007E0008 | RW | 32 |
| The auto increment feature results in efficient sequential host accesses. For both HPID read and write accesses, this removes the need for the host to load incremented addresses into HPIA. For read accesses, the data pointed to by the next address is fetched immediately after the completion of the current read. For the C62x/C67x pre-fetching also occurs after a host write of FETCH = 1 to the HPIC register. If the next HPI access is an HPID read, then the data is not re-fetched and the pre-fetched data is sent to the host. Otherwise, the HPI must wait for the pre-fetch to finish. | Bit Value |
| Bits[31: 0]: HPID++ | Value |

| Description | Address | Access | Width |
| --- | --- | --- | --- |
| Slave DSP 0: HPID, Host Port Interface Data Register | 0078000C | RW | 32 |
| Slave DSP 1: HPID, Host Port Interface Data Register | 007A000C | RW | 32 |
| Slave DSP 2: HPID, Host Port Interface Data Register | 007C000C | RW | 32 |
| Slave DSP 3: HPID, Host Port Interface Data Register | 007E000C | RW | 32 |
| A read or write cycle to the HPID no Auto Increment Register will access a register on the ROD at the specific address set in the HPIA register. | Bit Value |
| Bits[31: 0]: HPID | Value |

| Description | REG ID | Address | Access | Width |
| --- | --- | --- | --- | --- |
| Template: |  | 0040 | RW | 32 |
|  | Bit Value |
|  | 1 | 0 |
| Bit [0] : | Over | Idle |
| Bit [1] : | Over | Idle |
| Bit [2] : | Over | Idle |

# Text boxes

BOC Inputs

0 12 24 36 48 60 72 84

1 13 25 37 49 61 73 85

2 14 26 38 50 62 74 86

3 15 27 39 51 63 75 87

4 16 28 40 52 64 76 88

5 17 29 41 53 65 77 89

6 18 30 42 54 66 78 90

7 19 31 43 55 67 79 91

8 20 32 44 56 68 80 92

9 21 33 45 57 69 81 93

10 22 34 46 58 70 82 94

11 23 35 47 59 71 83 95

- 1  2  3  4  5  6  7

FORMATTER

Value

0

1

2

3

4

5

6

7

8

9

A

B

Value == Nibble [31:28]

D40 = Link Decoder 3 (LD3)

D80 = LD1 Second Bit in

D160 = LD0 Fourth Bit in

Value == Nibble [27:24]

D40 = Link Decoder 2 (LD2)

D80 = LD1 First Bit in

D160 = LD0 Third Bit in

Value == Nibble [23:20]

D40 = Link Decoder 1 (LD1)

D80 = LD0 Second Bit in

D160 = LD0 Second Bit in

Value == Nibble [19:16]

D40 = Link Decoder 0 (LD0)

D80 = LD0 First Bit in

D160 = LD0 First Bit in

BOC Input Link

To

Link Decode

Module Mux

D40:

M0

M1

M2

M3

D80:

M0

M1

D160:

M0