## Slide 1
PXIE Support Frame Design Review
Matt Hoff LBNL February 5, 2015

## Slide 2
How the support frame works, in mostly chronological order
Main support frame
3 strut temp outrigger
Qty 3
4 strut temp outrigger
Qty 1

## Slide 3
3 strut temp outrigger
4 strut temp outrigger
First module is attached
Some of the temp struts are compliant since the module is over constrained
Lifting set-up for placing modules

## Slide 4
Modules 2 and 3 are attached
Temp outrigger between modules 1 &2 removed
Permanent 4 strut to RFQ mount with 4 precision struts attached.
Module 4 is attached with temp outrigger
Assembly sequence

## Slide 5
Temp outrigger between Module 3&4 removed. 2 strut to RFQ permanent mount with 2 precision struts is attached
This assembly configuration is also the shipping configuration. At this point the temp outriggers and struts can be left attached during bead pull and vacuum testing, or they can be removed if they get in the way. If removed, they will need to be reinstalled for shipping.
Precision struts are ridged (x6). All temp struts are mildly compliant (x10).
Complete assembly

## Slide 6
Struts types
Compliant
Strut
(shipping)
Permanent
Strut
(precision)
Special precision rod eyes with no play, swaged extra tight.
Precision lock collars.
Usually incorporate differential threading (fine and course) in rod ends.
Steel tube body. 6 required
Neoprene bushing
Neoprene tube cut to length –McMaster 8637K211
Durometer 75A
McMaster 3031T963
Standard inexpensive left hand thread rod end. McMaster 60645K182
¾ inch HHCS
Made from 2 inch aluminum hex rod stock with left and right ¾ inch threads in the ends. 13 required.
Right hand thread

## Slide 7
PXIE RFQ Shipping Frame
Shipping frame in green
Air ride trailer

## Slide 8
A shipping frame like below will be made out of C 10 x 20lb steel channels bolted together at the overlaps. 4 machine mounts are attached. 4 attachment points are on the corners for the truck tie-down chains. Hoist rings are used to attach the support frame / RFQ to the shipping frame. The frame is not painted.
This is very similar to how the SNS shipping frame was designed.
Machine mount
Trucker attach point

## Slide 9
This is the catalog page for the machine mounts. The RFQ and support frame weighs about 12,500 lbs. There fore 4 SLM-48A’s rated at 4,800 lbs each should be adequate.

## Slide 10
The fork lift loads the package into the side of the LBNL air ride curtain truck. Its fast and easy.
SNS RFQ June 2002

## Slide 11
Truck bed
Trucker’s chains (red)
Shipping frame made from channel stock bolted together. Bolts not shown.
4 discrete point for the trucking chains
Machine mounts, one at each corner. Bolted to support and shipping frame
Experiment binders, Qty 8 (yellow). Could be either ratchet strap or binder chain. Installed by LBNL. See slide 8.
PXIE shipping frame details

## Slide 12
A top and side view of the PXIE RFQ shipping frame.

## Slide 13
After loading, the truck driver is now allowed to chain the package to the truck bed using the four attachment points provided. The truck load chains never touch the support frame or RFQ.
Pictures are from shipping the SNS RFQ June 2002
Trucker’s chains

## Slide 14
Shipping Frame vs Support Frame Integration
3 hoist rings attachment holes per corner of the support frame.
(3/4-10 UNC supports a 5,000 lb hoist ring.)
Hole for attaching the machine mount (vibration mount)
Shipping frame
Machine mount (vibration mount)
Swivel hoist rings

## Slide 15
Lifting Points
Each corner of the support frame can accept a 5,000 lb hoist ring
RFQ + 6 struts + Temp struts + Support Frame = 12,500 lbs
These 2 outriggers must be removed for a vertical crane lift
LBNL has not analyzed the frame for lifting at the four corners as shown

## Slide 16
Casters
10.5in
Hamilton Caster S-EDH2-83DT70 rated to 6,500 lbs each
5 caster mounts are provided

## Slide 17
Leveling Feet
McMaster-Carr 6111K333
¾-10 x 6 inch 7,400 lbs ea
Stainless $61 each
14 locations under the support frame are available. Not all need to be used.
Access hole for a deep socket to tighten lock nut if required

## Slide 18
Leveling Feet
1300 mm
94.5mm
3.7 inches
Approximately 12,500 lbs

## Slide 19
Earthquake Brackets
The easiest earthquake restraints to install are L-brackets bolted to the center frame member and then directly to the floor. The floor anchor shells can be drilled ahead of time with tolerances of +/- 1 inch. The L-brackets will be machined to match after alignment and leveling of the frame.
The Support Frame has 10 earthquake bracket locations available. Using 4 or 5 locations should be adequate.

## Slide 20
Earthquake Brackets
The brackets are cut from a 8 x 12 steel tube. The same size tube as used for the center tube of the support frame
After aligning and leveling the support frame, the final hole locations can be determined and drilled. Then the brackets will bolt into place easily and accurately.
The brackets will be sent to FNAL without holes.

## Slide 21
Earthquake Brackets
Brackets are bolted directly to 1 inch anchor shells in the floor and to the 8 x 12 main beam with 1 inch threaded rod.
Not all locations are required.

## Slide 22
Floor Boards
Floor boards are made from ¼ inch thick aluminum diamond plate. (Sorry, my CAD does not do diamond plate, so its modeled as regular plate.)
The floor boards are segmented into 8 pieces for easy installation and handling. The heaviest floor board is about 22 lbs.
The floor boards are held down around their perimeter with fasteners. Most are flush flat head screws around the outside, then a few hex bolts that are proud. The proud bolt heads are along the center tube in locations that do not cause a tripping hazard. Installation is done without reaching under the frame more then 3 inches.

## Slide 23
Floor Boards
8 floor boards
12 proud hex screw heads
38 flat head screws on the perimeter
Floor plates are well supported

## Slide 24
Floor Boards
One floor board in fore ground not shown
Proud ½-13 hex head bolts with fender washer

## Slide 25
Floor Boards
McMaster-Carr 91253A941 flat head socket cap screw 3/8-16 x 7 inch long. The bolt passes through 1 inch clearance holes in the frame and is held with a fender washer and standard nut.
Flat head screws
Qty 38

## Slide 26
CAD model of the RFQ and support frame in at FNAL

## Slide 27
Support frame fabrication drawings
Support frame parts are detailed and ready for fabrication

## Slide 28
Support frame fabrication drawings

## Slide 29
Support frame fabrication drawings

## Slide 30
Support frame fabrication drawings

## Slide 31
Support frame fabrication drawings
These are some examples of the support frame drawing. All drawings for the main frame are complete and ready for fabrication.

## Slide 32
Parts not detailed yet!
Shipping frame
Temp struts x10
Temp outrigger x4
Temp vertical support x1
Temp center support x3
Diamond floor plates x8
Precision struts x6
Strut to RFQ mounts x2

## Slide 33
Schedule
The Building 77 shops estimates the frame will take 8 to 12 weeks to fabricate.
Ordering and fabrication can start immediately. The shop is not busy. Needs work.
The remaining parts that need detailed will only take 5 days to detail.
The precision struts are considered a standard part at the ALS and are ordered by length and standard diameter (2.5 inches) though them.
The support frame and outriggers will be painted a silver – gray color.
The shipping frame is not painted or coated. Its is used raw.
The aluminum strut to RFQ mounts can be left raw or painted to add some pizzazz.